## Slide 1: RAN123 NTN topics for Rel-20 5G Advanced - Overview
Sources: Thales, Novamint, TNO, Echostar, ESA, Eutelsat, Airbus, Sateliot
3GPP TSG RAN Meeting #106 RP-242649
Madrid, Spain, December 09-13th, 2024
Agenda: 15.2
TDOC: RP-242664
For: discussion

## Slide 2: Proposed Rel-20 RAN123 led activities for 5G Advanced
Topics for both NR-NTN and IoT-NTN
  GNSS independent/resilient operation
Candidate topics for NR_NTN
  Multi orbit satellite support architecture
  NR NTN to/from LTE TN mobility in connected mode
  Resilient notification
  Rel-19 left overs
Candidate topics for IoT_NTN
  5GC support of IoT NTN
  IMS voice call over GEO
  Network-controlled anchor carrier mobility
  Inter-RAT mobility between TN and IoT NTN (Idle and Connected mode)
  Rel-19 left overs

## Slide 3: GNSS independent/resilient operation for NR and IoT-NTN (1/2)
Justification
  In most locations and at most times, GNSS provides a highly accurate position and time reference.
  However, evidence has been shown that GNSS jamming (leading to denial of service) and spoofing (leading to incorrect location reporting and potentially denial of service) may occur.
  Additionally, GNSS handling may cause delays to the UE operation due to positioning acquisition time (e.g., for a GNSS "cold start") and additional energy consumption.
  Therefore, NTN UEs of all types including handheld terminals and mobile VSAT devices do require an alternative means of achieving and maintaining successful uplink time and frequency synchronization in NTN based access.

## Slide 4: GNSS independent/resilient operation for NR and IoT-NTN (2/2)
Hypothesis
  At least one satellite in visibility per UE
  UE (up to 250 km/h) not relying on GNSS receiver to compensate timing/Doppler variation
  Applicable to both GSO and NGSO
Objectives
  Leverage existing 3GPP terrestrial positioning mechanisms by adapting positioning reference signals, measurements, methods, and signalling to include support for 3GPP satellite-based positioning.
  Define network assistance information broadcasted in SIB (e.g. PRS)
  Define positioning method for the UE to determine its position in Idle (including initial access) and Connected modes
  Define enhancement(s) to closed loop timing control techniques.
  If required, define new UE frequency correction mechanism, similar to the existing timing advance mechanism, allowing the terminal to stay frequency synchronized to the network
  Identify/address possible coexistence issues between Rel-17/Rel-18 UEs with GNSS and new (Rel-19) UE types without GNSS assistance in the same NTN radio cell

## Slide 5: NR-NTN: Multi-orbit satellite support
Hypothesis
  No simultaneous multi connectivity
  Satellite access at different orbits belong to the same operator PLMN.
Objectives
  Specify the signaling and the procedures at both NR and NG interfaces [RAN2, RAN3]
    to allow UE to acquire Satellite and Beam information of a Lower Altitude Orbit RAN (e.g. LEO) from a Higher Altitude Orbit RAN (e.g. GSO) while UE in RRC Idle and for UE to go to RRC Connected on the Lower Altitude Orbit RAN
    to assist directive UE (operating in above 10 GHz) in pointing its antenna towards an NGSO satellite
    for UE to select between Higher and Lower Altitude Orbit RAN upon multiple criteria (data rate, latency, energy efficiency, reduced mobility requirements)
    For mobility in connected mode between cells from different orbits with minimum service interruption time
    to inform UEs in a targeted area that NGSO Beam(s) have been switched to a different power saving mode or switched ON (e.g. when a GSO satellite detects a new RRC Connected UE in the footprint of that NGSO Satellite.)

## Slide 6: NR NTN to/from LTE TN mobility in connected mode
Justification
  Ensure quasi seamless service continuity in connected mode for automotive users that may drive on a road which is intermittently covered by a terrestrial network while fully covered by a non-terrestrial network
Objectives
  Define enhancements to the hand-over procedure addressing latency discrepancy between both links [RAN2]

## Slide 7: NR-NTN: Resilient notification
Justification
  Users might miss or not receive in a timely manner incoming calls/messages due to poor received SNR.
  It is therefore crucial to introduce a more resilient alert channel to enable delivery of emergency calls/messages and allow transitioning from insufficient link budget scenario to sufficient link budget scenario. The intent is to alert the UE to move to a better signal reception location for communication.
Objectives
  Define a dedicated robust notification mechanism that delivers notifications directly to user devices, such as smartphones, via satellite access. Target is be to operate with SNR [18] dB lower than legacy paging channel. [RAN1/2]
  Enhancement to SSB is not needed

## Slide 8: IoT-NTN: 5GC support
Justification
  IoT-NTN only supported by EPC
  NTN applies to new deployment and there is no existing EPC and therefore it is important to have 5GC support of IoT to have integrated NTN-NR and NTN-IoT services.
  Interest for a satellite network providing NR-NTN and IoT-NTN access technology NTN,
Objectives
  study/define the necessary architecture enablers [RAN3]

## Slide 9: IoT-NTN: IMS voice call over GEO
Justification
  While NB-IoT (GEO) already supports direct communication over GEO satellites, its design focuses on IoT devices and services. The study in SA1 has shown benefits to improve the IMS service by leveraging NB-IoT (GEO) satellite access, thereby introducing new opportunities and value across a wide range of markets, including IoT and smartphone sectors.
Objectives
  enhance IMS services, with a particular focus on voice and emergency calls, by utilizing NB-IoT (GEO) satellite access

## Slide 10: Network-Controlled/Steered Anchor-to-Anchor Carrier Switching for NB-IoT
Justification
  Satellite and satellite beam coverage areas are very large, with different beam sizes and very likely include multiple NB-IoT NTN carriers in the same footprint
  There are situations in which the network may need to move UE between NB-IoT NTN carriers for load-balancing or frequency management purposes
  There are situations in which the network may need to offload UE between beams for mobility, coverage, frequency or load-balancing purposes
  NB-IoT does not support CONNECTED_MODE mobility or any kind of Network-controlled mobility or load-balancing
  A combination of multiple NB-IoT NTN Anchor and Non-anchor carriers may be deployed within any given satellite beam coverage area
  NTN operators may have a constraint of being able to deploy only Anchor carriers in adjacent beams or within the same beam
  Moreover, it is likely expected that additional Non-Anchor carriers associated with a given Anchor carrier are only deployed within the same beam, and that adjacent beams will mostly be associated with different Anchor carriers
Objectives
  Identify and specify NB-IoT enhancements to support an efficient mechanism for Network-controlled or steered Anchor-to-Anchor and non-anchor-to-Anchor carrier switching for UE, beyond one-off RRC based re-direction [RAN2]
    Including after initial attach and in Connected Mode
    Note : No impact on connected measurements
    Note: How carriers are mapped to same or different satellite beams is left to an Operator’s deployment considerations

## Slide 11: Inter-RAT mobility between TN (E-UTRA, NR) and IoT NTN
Justification
  Despite the extensive work on Mobility aspects for NTN, many buildings blocks in TN-NTN mobility are still missing
  TN-NTN Mobility has been (or is being) almost fully addressed for NR NTN (except mobility from E-UTRA, which is currently being addressed).
  Some aspects have been ported to/from IoT NTN – but mostly limited to NTN-NTN
  Chiefly, Mobility from (E-UTRA or NR) TN to IoT NTN is not yet fully specified
  Some UE will be developed with full E-UTRA or NR TN support, and IoT NTN
Objectives
  Specify missing aspects to support TN-NTN inter-RAT mobility towards IoT NTN (eMTC, NB-IoT)
    to support Idle mode mobility via Cell Reselection
      from E-UTRA TN and IoT NTN
      from NR TN and IoT NTN
    to support Connected mode mobility via Handover (HO) and Conditional Handover (CHO)
      from E-UTRA TN and IoT NTN
      from NR TN and IoT NTN

## Slide 12: Questions ?