## Slide 1
Views on Multi-Modality in Rel-19 XR
Apple
  3GPP TSG RAN #106
  Madrid, Spain, December 9 - 12, 2024
  Source: Apple
  Agenda Item: 9.3.2.3
  RP-242791

## Slide 2
Background
In the revised WID on XR for NR Phase 3 (RP-241771), there is an objective on multi-modality:
  Specify support for multimodality in RAN for UL and DL [RAN3]:
    NOTE: This is subject to alignment with SA2, e.g., if MMSID is not available from CN, then UE assistance information-based approach as an alternative. RAN#106 to check handling of uplink discard based on SA2/SA4 outputs on whether the corresponding information is available at the UE.
    NOTE: Review in RAN#106 the conclusions in SA2 side (including MMSID delivery to RAN) to allocation for further TUs in RAN3 from Q1/25 onwards.
In summary, the following should be discussed in RAN #106 :
  Whether uplink packet discard based on multi-modality should be specified, and
  Whether the NG-RAN can obtain MMSID information from the core network.

## Slide 3
SA4/SA2 Progress
The reply LS from SA4 to RAN2/RAN3/SA2 (S4-242223) has indicated that packet discarding for multi-modality is not recommended:
  For DL, from the application perspective, there are well-defined mechanisms to support synchronized playout among different media flows, e.g. RTP timestamps, jitter buffering mechanism in the RTP client. These mechanisms guarantee frame level synchronization but do not provide packet level synchronization among different media flows. There is no evidence to suggest 5GS per packet inter-modal synchronization is needed for XR services, as the very low round trip latency requirements will prevent the system from introducing unacceptable inter-modal skew.
  Regarding PDU Set discard, it is recommended that the 5GS not jointly discard packets across multi-modal flows. Receiving packets for some modalities is preferred than receiving none at all as this enables the application to use the received modalities to better manage the user experience (e.g., pause the video while rendering received audio packets, or render received video packets while concealing an audio packet drop).
On the other hand, it seems no consensus can be made in SA2 on whether MMSID can be delivered to NG-RAN. The reply LS has been postponed in SA2 #166.
Observations:
  SA4 has indicated that packet-level synchronization for multi-modality is not needed.
  SA4 does not recommend UL packet discarding based on multi-modality.
  SA2 did not reach a consensus about whether MMSID can be delivered to NG-RAN.

## Slide 4
Conclusions
Based on the feedback from SA4 and status of SA2, we think there is no much value to further pursue enhancements for multi-modality in Rel-19 XR.
Even though RAN2 has agreed that UAI may be used an alternative for the RAN to get multi-modality awareness, we think the assistance information from the CN should be the baseline. If even the baseline cannot be supported, we do not see much need to specify the UAI for this purpose.
Thus, we propose that the entire WI objective for this topic can be removed from the WID.
Proposal: Remove the objective relating to multi-modality support from the WID for Rel-19 XR

## Slide 5
Suggested WID Change
4.1 Objective of SI or Core part WI or Testing part WI
The Rel-19 XR Phase 3 objectives are as follows:
-Specify support for multimodality in RAN for UL and DL [RAN3]:
NOTE: This is subject to alignment with SA2, e.g., if MMSID is not available from CN, then UE assistance information-based approach as an alternative. RAN#106 to check handling of uplink discard based on SA2/SA4 outputs on whether the corresponding information is available at the UE.
NOTE: Review in RAN#106 the conclusions in SA2 side (including MMSID delivery to RAN) to allocation for further TUs in RAN3 from Q1/25 onwards.
-Specify enhancements to enable transmission/reception in gaps/restrictions that are caused by RRM measurements (from inter-frequency RRM measurement gaps, or intra-frequency measurements, or other scheduling restrictions etc). [RAN1, RAN2, RAN4]
- Specify the corresponding measurement gap and scheduling restriction to enable the identified enhancements with RRM performance impact taken into consideration, work being triggered by LS. [RAN4]
-Specify Enhancements for support of UL scheduling to enable high XR capacity while meeting delay requirements/avoiding too late PDUs, as follows [RAN2]:
- Specify additional Logical Channel priority handling using delay/deadline information of packets;
- Specify enhanced DSR (Delay Status Report) reporting with multiple pairs of remaining time and buffer size for an LCG.
-Specify the following user plane enhancements [RAN2]:
RLC re-transmission related enhancements for operation of RLC Acknowledged Mode (AM) with small packet delay budget.
Extend Release 18 standalone mechanism to support NR-NR dual connectivity as follows [RAN3]:
- PDU set based handling;
- ECN marking;
- Burst Arrival Time reporting, if needed;
- PSI Discard coordination, if needed;
NOTE: No RAN2 impact from above items.
-Specify uplink congestion signalling [RAN2]:
- Specify in MAC layer XR rate control signalling over downlink per QoS flow/per DRB to enable faster source rate adaption to uplink congestion.
- Specify Core requirements related to the above objectives as necessary [RAN4].