## Slide 1: OPPO’s view on R20 5G-A package
3GPP TSG-RAN Meeting #106
Madrid, Spain, December 17-20, 2024
Agenda item: 15.1
Document for: Discussion
RP-242795

## Slide 2: General views on 5GA R20 package
Principles to build 5G-A package:
  Focus on the features that have strong market needs;
    Clear routine to commercialization;
  In Release 20, considering both 5GA package and 6G SI in parallel, OPPO prefers to have more TUs allocated to 6G SI than 5GA
  If there is potential collision between 5G-A and 6G, we prefer either commit it in 5G-A or 6G track but not in parallel
    In general mature feature will go to 5G-A
    Feature need carefully study and future proof will go to 6G
The rest slides illustrate high priority items. We are open to discuss others.
2024 |  |  |  | 2025 |  |  |  | 2026 |  |  |  | 2027 |  |  |  | 2028 |  |  |  | 2029 |  |  |  | 2030 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
 |  |  |  | RP 6G R20 SIDs, ITU and General Req. |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
6G SI R20 |  |  |  |  |  | RAN1 6G R20 SID |  |  |  |  |  |  | RAN1 6G R21 WID |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | RAN2/3/4 6G R20 SIDs |  |  |  |  |  |  | RAN2/3/4 6G R21 WIDs (with ASN.1) |  |  |  |  |  |  |  |  |  |  |  |  | 
5GA R20 |  |  |  |  |  | RAN1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  |  |  |  |  | RAN2/3/4 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 3: AI mobility
Current status:
  The evaluation on core use case i.e. RRM measurement prediction is almost finished after 2 rounds of simulation
    Generalization study will focus on RRM measurement prediction
  Evaluation on measurement event, RLF and SLS to verify HO performance is expected from Feb. 2025
  Mobility specific LCM will start in 2025 e.g. April
We prefer to have a work item in R20 with the following scopes:
  In general limited to the scope studied in Rel19
  What is agreed for AI/ML over air w.r.t. LCM will be reused as much as possible
  This WID will focus on mobility specific aspects
    For UE sided model:
      Including but not limited to data collection, inference configuration and report, monitoring, activation/deactivation etc.
    For network sided model
      Including but not limited to data collection, assisted information from UE for inference etc.
  RAN4 need focus on RRM measurement prediction
Something new for study at least can cover:
  LTM (intra-CU and inter-CU)
  Conditional LTM and conditional Handover
  Both Pcell change and PSCell change

## Slide 4: AI/ML over the air interface
A WI on AI/ML over the air interface depends on the output of R19 study
  CSI compression are evaluated and investigated for two releases (i.e., R18 and R19)
    Performance gain is observed for some cases
    The main controversial part how to alleviate the inter-vendor collaboration
  Some aspects needed to be considered carefully
  A well-managed scope with essential objectives and limited number of option(s)
  A good balance between 5G AI/ML and 6G AI/ML for the air interface
Potential WI on AI/ML over the air interface in R20
  CSI compression (two-sided model)
    Prefer Option 4-1 to facilitate inter-vendor training collaboration
      Option 4-1: dataset sharing from NW-side to UE-side for UE-side encoder offline training
      Benefits: less specification effort compared with other options and with comparable performance and more flexibility
    Performance monitoring for the CSI compression
      Support both NW-side and UE-side performance monitoring
      Consider intermediate KPI (e.g. SGCS) as monitoring metric
    Data collection
      For NW-side model training, specify mechanism/signaling for ground-truth reporting
      For UE-side model training, support UE requested RS configuration/transmission

## Slide 5: Ambient IoT
Rel-20 work item:
  Assuming all aspects studied in SI and needed for the market are included in the first WI
  Further support following:
    DO-A traffic
      For sensor data / event triggered applications)
    Positioning enhancement (RAN1/RAN2/RAN3)
      Only reader ID granularity is supported in Rel-19 foreseen, finer granularity is expected according to 38.848.
    Outdoor scenarios :
      To support outdoor use cases identified in 38.848.
      Further enhancements may be needed to improve coverage for outdoor-to-outdoor
rUC5: Outdoor inventory | 5.2 Medical instruments inventory management and positioning 5.4 Non-public network for logistics 5.7 Airport terminal / shipping port 5.16 Automated supply chain distribution
rUC6: Outdoor sensor | 5.3 Smart grids 5.19 Forest Fire Monitoring 5.22 Dairy farming 5.24 Smart manhole cover safety monitoring 5.25 Smart bridge health monitoring
rUC7: Outdoor positioning | 5.8 Finding remote lost item 5.9 Location service 5.12 Personal belongings finding
rUC8: Outdoor command | 5.11 Online modification of medical instruments status 5.17 Device activation and deactivation 5.26 Elderly Health Care 5.30 Controller in smart agriculture

## Slide 6: ISAC
ISAC is expected as the day-1 feature of 6G
  6G study will cover full set of use case and scenarios
  Overlapping of ISAC in 5G-A and 6G in RAN1 should be avoided
    All evaluations for ISAC are preferred to be included in 6G study
    Manageable workload for the group
Open for an item without Uu impact and UE involvement
  Sensing by reusing existing reference signal
  No spec impact from RAN1/2 perspective, i.e.,
    Reuse the existing design of waveform, reference signal and so on
  RAN3-led item
    Option1: a RAN3-led work item
    Option2: a RAN3-led study item followed by a RAN3-led work item