## Slide 1: Discussion to support Regenerative Payload without S&F operation
RAN#106
Madrid, Spain
Dec 09-12,2024
Agenda 10.3.1
RP-242813

## Slide 2
  IoT NTN WI Scope
  From IoT NTN WID in RP-242397 –
    Support of Store&Forward (S&F) satellite operation with full eNB as regenerative payload, therefore:
    Define the necessary enhancements into E-UTRAN (network & UE) to support S&F operation for delay-tolerant services [RAN3, RAN2]
      At least specify necessary enhancements e.g. related to S1 protocol, especially to address the feeder link switch over as needed [RAN3]
    Note: Strive to minimise UE impact.
    Note: Coordination with SA2 (Rel-19 SA2 led Sat-Arch ph3 SI) is needed on the detail requirements (e.g. traffic type, or QoS parameters for S&F), network architecture (e.g. whether consider (partial) core network on satellite) etc.; further coordination with CT1 might be required.
  IoT NTN WID mentions support only for eNB on board with regenerative payload and S&F operation.
  When the feeder link services are available, eNB with regenerative payload on satellite should be able to connect to MME on ground via S1 over feeder link without S&F mode, to serve legacy UEs. However, IoT NTN WID does not explicitly mention to support eNB on board with regenerative payload without S&F operation.
  LS from SA2 S2-2410918 to RAN mentions –
    SA2 would like to inform RAN3 that the conclusions for FS_5GSAT_Ph3 for “KI#1: Support of Regenerative-based satellite access” without Store and Forward in clause 8.1 of TR 23.700-29 apply to both E-UTRAN/EPS and NG-RAN/5GS and therefore the related RAN3 impacts can affect both S1 and NG procedures.
  SA2 conclusions for KI#1 also applies to E-UTRAN/EPS without S&F operation. Hence there is a mismatch between SA2 and RAN3 in the IoT NTN WI scope.

## Slide 3
  Proposed Update for IoT NTN WID
When feeder link services are available, eNB on board satellite with regenerative payload should be able to connect to MME on ground via S1 to serve IoT NTN UEs without Store and Forward operation.
Thus, we propose to update the IoT NTN WID to explicitly mention the support of regenerative payload with eNB on board without S&F mode
Proposal 1 : Support eNB on board satellite with Regenerative Payload without Store and Forward operation when feeder link services are available for IoT NTN. Agree to WID update in RP-242773.