## Slide 1: Views on UL Coverage Enhancements in Rel-20 5G-A
NTT DOCOMO, INC.
3GPP TSG RAN#106
Madrid, Dec 9 - 12, 2024
Source: NTT DOCOMO, INC.
Agenda item: 15.2
Document for : Discussion
RP-242819

## Slide 2: “Msg5” Coverage Enhancement
Motivation:
  Until Rel-18, repetition-based coverage enhancements are (to be) specified
    PUSCH after RRC connection
    Msg3 PUSCH
    PUCCH
    PRACH
  Meanwhile, “Msg5 PUSCH” doesn’t support repetition
    “Msg5 PUSCH” is a PUSCH after Msg3 PUSCH and before reception of dedicated PUSCH config
    From specification perspective, “Msg5 PUSCH” is included in “PUSCH scheduled by DCI format 0_0 with CRC scrambled by C-RNTI”
  Without repetition, Msg5 PUSCH can be a significant bottleneck, especially for NTN operation
View:
  Specify repetition for PUSCH scheduled by DCI format 0_0 with CRC scrambled by C-RNTI
Leading WGs: RAN1