## Slide 1: Rel-20 Mobility enhancements
Ericsson, Verizon, Docomo
3GPP TSG RAN#106
Madrid, ES
2024-12-09 - 2024-12-12
Agenda Item: 15.2
RP-242848

## Slide 2: Rel-20 Mobility enhancements Overview of proposed enhancements
Improved SCell handling in LTM
Support for L1-SINR measurement quantity for LTM
Coexistence of LTM and RedCap
Inter-CU Conditional LTM
N2/NG-based LTM
Steering stationary and low mobility UEs to frequencies and bands

## Slide 3: Improved SCell handling in LTM
Justification
  Rel-18/19 LTM provides basic support for carrier aggregation. SCells may be included in an LTM candidate configuration and may therefore be part of the target cell group configuration the UE applies at an LTM cell switch.
  However, this typically means the SCells are configured in RRC as deactivated and then activated in the target cell only after the switch (or possibly the other way around).
  This causes a delay before CA can be used in the target which reduces data throughput and frequency offloading, especially at frequent LTM cell switches for a UE dependent on CA for its services.
Objective
  Specify support for dynamic activation/deactivation of SCells during LTM cell switch, including
    L1 measurements and event-triggered MAC CE reporting on SpCells and SCells, including currently deactivated SCells [RAN1, RAN2, RAN4]
    Activation/deactivation of SCells of the target LTM candidate cell configuration via the LTM cell switch MAC CE [RAN2, RAN4]
    Inter-node network signalling to support the above [RAN3]
    Note: Supported scenarios include those already supported as of Rel-19

## Slide 4: Support for L1-SINR measurement quantity for LTM
Justification
  The L1-RSRP for a candidate cell resource may be high and yet the channel conditions are bad due to noise and interference. Between frequency layers the interference and noise levels are normally different. Hence, especially for inter-frequency neighbours, L1-SINR can be a good compliment to L1-RSRP as a basis for LTM execution decisions, for example that both L1-SINR and L1-RSRP are sufficiently good.
  To add support for L1-SINR measurement quantity for LTM was discussed in Rel-19 but was not agreed due to concerns with high workload.
Objective
  Specify support for L1-SINR measurement quantity for L1 measurements for LTM [RAN1, RAN2, RAN3, RAN4]
    L1-SINR measurements to be included L1 measurement reports, MAC CE event triggered reporting and used for triggering conditional LTM
    Support for inter-frequency and SSB has high priority
    Support for intra-frequency and CSI-RS has lower priority

## Slide 5: Coexistence of LTM and RedCap
Justification
  In Rel-19, support for coexistence of LTM and (e)RedCap is being discussed in RAN2
  However, even if it would be supported in Rel-19 from RAN2 point of view, the RAN4 requirements would need to be specified for this combination. But the current RAN4 workload does not allow to complete also the RAN4 part in the Rel-19 timeframe.
Objective
  Specify RAN4 requirements for coexistence of LTM and (e)RedCap [RAN4]

## Slide 6: Conditional LTM enhancements
Justification
  Conditional LTM being specified in Rel-19 is limited to intra-CU and non-DC scenarios and does not support security key change
  Inter-gNB mobility is an important scenario for combined mobility robustness and short interruption that remains to be specified
  NR-DC scenarios for intra-CU conditional LTM would likely not be supported in Rel-19 (subject to checkpoint at RAN#107)
Objectives
  Specify support for inter-CU conditional LTM [RAN2, RAN3, RAN4]
    Prioritize the cases when DC is not configured and when CU is acting as MN when DC is configured
    Note: Security aspects to be coordinated with SA3
  Specify support for NR-DC with intra-CU conditional LTM [RAN2, RAN3, RAN4]
    Prioritized scenario is CU is acting as MN when DC is configured

## Slide 7: N2/NG-based LTM
Justification
  Rel-19 inter-CU LTM relies on an Xn link between source gNB and target gNB. It does not support LTM preparation or execution via the core network.
  This means that currently, LTM cannot be used in scenarios like:
    there is no Xn connectivity between source gNB and target gNB (at the time of preparation, early sync and/or execution)
    the core network needs to be involved at LTM preparation, e.g. at change of AMF, PLMN or slice, or, possibly, to retrieve security information from the AMF
  In the above cases, the network is forced to use L3 HO via the core network, even for a UE configured with LTM. This results in longer interruption time and the UE need to be configured for L3 RRM measurement reporting for triggering L3 handover, in additional to those needed for LTM preparation and execution.
  To support LTM configuration and execution via N2/NG will be a natural next step making LTM on par with L3 HO on supported scenarios.
Objective
  Specify support for NG/N2 based LTM, including
    Configuration of LTM candidate cells via 5GC [RAN2, RAN3]
      Note: Security aspects to be coordinated with SA3
    LTM execution via 5GC, including packet forwarding [RAN2, RAN3]

## Slide 8: Steering stationary and low mobility UEs to frequencies and bands
Justification
  Mobility in higher frequencies, such as FR2, is quite challenging due large propagation loss and fast fading effects.
  A stationary UE, though, would benefit from a PCell on higher frequency bands, such as in FR2, as it allows for higher capacity but also helps the network to offload lower frequency bands (e.g., FR1).
  The current mechanisms, e.g. performing inter-band handover or providing UE dedicated cell reselection priorities per frequency in RRC Release, are not reliable unless the network knows, with a high degree of certainty, that the UE will be stationary or with low mobility, e.g. based on subscription or other stable/static information about the UE. This means that a UE which is stationary or with low mobility, even for a long time, would often be kept on lower frequencies even if it would benefit from being moved to higher frequency bands.
Objective
  Specify a mobility evaluation criteria for stationary and low mobility UEs, to be used for cell reselection priorities per frequency. [RAN2, RAN4]
    Note: The solution should be similar to the existing low-mobility criteria for RRM measurement relaxation.

## Slide 9: Steering stationary and low mobility UEs to frequencies and bands – more detailed justification
One of the main benefits of NR is that operators have the possibility to utilize the mmWave spectrum (i.e., FR2) thus allowing the UE to get better performance in terms of latency and capacity (including fast connection setup times from FR2).
Currently the higher frequency bands, such as FR2 bands, are mainly used for secondary carriers in MR-DC or CA
  This enables connection robustness as the mobility in higher frequencies is quite challenging with typically high RLF/HOF probability, due to e.g. large propagation loss and quick fluctuation
In specific cases, such as when the UE is expected to be stationary or with low mobility, using higher frequency bands, including FR2 bands, for the PCell is beneficial.
  Examples of stationary or low mobility use cases requiring higher data rates and traffic densities are Fixed Wireless Access (FWA), professional AV production, broadband access in a crowd (e.g. stadiums or concerts) and broadcast-like services
If a UE would already have been camping on the higher frequency in RRC_IDLE or RRC_INACTIVE, inter-band handover (such as FR1->FR2 handover) could be avoided after connection setup
  This would enable better offloading of lower frequencies, higher capacity and faster transition to RRC_CONNECTED
The existing solution is to use release with redirect, but this assumes that the network can reliably identify the UE as being stationary or with low mobility for a long time (e.g. as a FWA device).
There is already a low-mobility criteria specified since Rel-16 for RRM measurement relaxation. This was introduced for UE power saving and RedCap UEs and can be the basis for this work. If these criteria say the UE is low/no mobility the UE can apply the alternative frequency reselection priorities.