## Slide 1
0
CMCC
2024-12
Considerations on Rel-20 NES
3GPP TSG RAN #106 RP-242970
Madrid, ES, December 09-12, 2024
Agenda Item: 15.2
Source: CMCC

## Slide 2
Backgroud
During Rel-18/Rel-19, NES technique has been well studied and discussed, schemes for both RRC CONNECTED and RRC IDLE/INACTIVE UEs are further specified during WI phase
Techniques from time, frequency, spatial, power domain can provided significant NES gain according to the evaluation results captured in TR 38.864
  Time domain: Cell DTX/DRX, Common signal adaptation
  Frequency domain: SSB-less SCell, On-demand SSB SCell, On-demand SIB1
  Spatial domain: Adaption of spatial elements
  Power domain: Adaption of transmission power for PDSCH
  Higher layer power saving schemes including preventing legacy UEs camping on NES cells, CHO procedure enhancement(s), paging enhancement, RRM/RF core requirements
However, with the consideration that always-on signal still need to transmit in a short period (i.e. CD-SSB is transmitted per 20ms for initial cell selection), there is still room for NES gain
  With the transmission of CD-SSB, the gNB cannot enter deep sleep mode, which limits the NES gain
Observation: Further enhancement to faciliate reduced transmisson of CD-SSB of gNB while maintain in time response to UE is needed

## Slide 3
Motivation on OD-SSB for IDLE/INACTIVE UE
Indoor office scenario has the following characteristics
  The number of UEs served has obvious time varing characteristics. When there are no users, periodic broadcast SSB brings a lot of meaningless energy consumption to the network
      gNB can “turning-off” SSB (i.e. CD-SSB) for deeper sleep and larger NES gain
  While even in non-working hours, UEs will occasionally enter the service area, the base station needs to be woken up in time
    Wake up signals from UE to wake up gNB for normal SSB transmission when needed
  Such mechanism for IDLE/INACTIVE UE has significant benefits and should be supported in Rel-20
UE comes, it wakes up SSB transmission when needed
No UE, turning off SSB transmission
Indoor office scenario
Proposal: On-demand SSB for IDLE/INACTIVE UE is supported for Rel-20 NES

## Slide 4
Scheme on OD-SSB for IDLE/INACTIVE UE
The following cases can be considered on OD-SSB for IDLE/INACTIVE UE
  Case 1: Standalone case (OD-SSB operation works on NES Cell itself)
      UE pre-receives/configures WUS configuration and transmits WUS on NES Cell
      gNB can turn off TX part while periodically enabling RX part for WUS detection
  Case 2: Non-standalone case (OD-SSB operation works with the assistance of Anchor Cell)
      UE receives WUS configuration and transmits WUS via Anchor Cell
      Both TX and RX part in air interface can be turned off with the support of backhaul/Xn interface
Proposal: Support to study and specify both Case 1 and Case 2 under OD-SSB for IDLE/INACTIVE UE

## Slide 5
Potential objective
Study and specify on-demand SSB for UEs in idle/inactive mode [RAN1/2/3/4]
  Study and specify procedures and signaling method(s) for the following cases [RAN1/2]
    Case 1: UE pre-receives/configures UL WUS configuration, UE transmits UL WUS on NES Cell, UE receives on-demand SSB from NES Cell
    Case 2: UE obtains UL WUS configuration from Anchor Cell, UE transmits UL WUS on Anchor Cell, UE receives on-demand SSB from NES Cell
    Triggering method by uplink wake-up-signal
  Study and specify inter NG-RAN node signaling at least for the configuration of UL WUS [RAN3]
  Study and specify the corresponding core requirements for the feature [RAN4]
  Note 1:
    UL WUS: Uplink wake-up signal
    Anchor Cell: A cell that is periodically transmitting at least NES Cell’s UL WUS configuration
    NES Cell: A cell that may transmit on-demand SSB in response to UL WUS from a UE
  Note 2: The above mechanism should at least workable for CD-SSB

## Slide 6
Thank you!