## Slide 1: Proposal for RRM objective on relaxed RLM/BFD for Redcap
Ericsson, MediaTek inc., vivo
3GPP TSG RAN meeting #106 RP-242982
Madrid, Spain, December 9th – 12th, 2024

## Slide 2: Relaxed RLM and BFD for RedCap UEs
Background:
    The relaxed beam failure detection (BFD) and radio link monitoring (RLM) is specified for regular NR UEs as part of the Rel-17 UE power saving WI [RP-200938].
      Relaxation is in time-domain and applies to RLM evaluation period and BFD evaluation under good serving cell and/or low mobility conditions, see figure below.
Time
....
With relaxation
....
= Measurement occasion
Figure 1: Time-domain relaxation of RLM/BFD evaluation period
No relaxation

## Slide 3: Relaxed RLM and BFD for RedCap UEs
Justification
    UE power saving is even more critical for Redcap UEs than non-RedCap UEs.
      Scenario with low speed/quasi-static may be common for Redcap
    For 2 Rx RedCap, no substantial workload is expected since legacy Rel-17 work could possibly be reused.
    For 1 Rx RedCap, additional but not substantial work is needed.
    Relaxed RLM/BFD work for RedCap can be accommodated in the ongoing RRM phase 5 WI [RP-242380] or as a separate WID.
Proposed RAN4 objective for Rel-19 RRM extension:
  Specify relaxed RLM/BFD evaluation period requirements for 1 Rx and 2 Rx RedCap UEs based on the Rel-17 relaxed RLM/BFD requirements for non-RedCap UEs.
    Relaxation is in time-domain and relaxation criteria (i.e. good serving cell- and low mobility criteria) from Rel-17 relaxed RLM/BFD work for non-RedCap UEs shall be reused
    Relaxation condition (i.e. short DRX periodicity) from Rel-17 relaxed RLM/BFD requirements shall be reused.