## Slide 1
Motivation on further complexity reduction for eRedcap devices
enabling single SKU design (SAW-less)
Sony, Nordic Semiconductor ASA, Semtech, Sequans Communications, vivo, OPPO, Itron
3GPP TSG RAN Meeting #106
Madrid, Spain, December 9-12, 2024
RP-243007
Agenda item:9.1.4

## Slide 2: Motivation and Proposal
  Based on the 3GPP study in TR 38.875 Study on support of reduced capability NR devices [1], the duplexer is a major cost contribution in the RF frontend for an NR FDD device.
  Rel-17 Redcap enables HD-FDD operation in NR so that the duplexer can be omitted. However, to meet some RF requirements that have been defined for NR, band-specific SAW filters are still needed for HD-FDD Redcap which dilute the intended cost saving benefit.
  In Rel-18 eRedcap, the eRedcap HD-FDD UE with BW3/PR3 is defined, However, to meet all the RF requirements, it is still NOT possible for such a device to be implemented without any SAW filter (see later slide for detail).
    RAN4 has already had some preliminary discussions to enable SAW-less implementation for eRedcap in Rel-18 [2], but no conclusion was reached due to insufficient time. However, as concluded in RAN4#109, RAN4 agreed to consider discussion on SAW-less design for eRedCap in Rel-19 [3].
  For a further complexity reduction for eRedcap in Rel-19, especially for HD-FDD, we propose to resolve the barriers in 3GPP specs by specifying corresponding mechanism(s) to enable implementations without SAW filters (i.e., SAW-less).
    Note: Without SAW filters (i.e., SAW-less) does not imply “without filters”, since a few small and low-cost low-pass filters for harmonics rejection are still needed.
    Note: the proposed solution to enable the SAW-less implementation in Rel-19 shall ensure the spurious emission for UE co-existence level is not relaxed.
Conclusion for HD-FDD cost saving in TR 38.875
Multiband RF front-end design with SAW duplexers
Proposed global SKU design with SAW-less RF front end

## Slide 3: Benefits from device viewpoint
From the device viewpoint, the SAW-less design is one of the main options to achieve hardware complexity reduction while enabling a single SKU (stock-keeping unit) design for global operation.
  Removing the band/regional specific SAW filters reduce the complexity and the associated cost on RF front end.
    According to TR 38.875 “For Type A HD-FDD, a high proportion of the cost saving occurs because the duplexer can be replaced with a switch and a lowpass filter” [1].
  Removing the band/regional specific SAW filters enables a single SKU design for global operation, simplifying device procurement, development, verification, manufacturing and inventory management.
    All devices can be produced identically, which significantly simplifies logistics as well as the production process, and leads to cost savings.
    Reduce the number of implementation variations that are needed to support the different cellular networks across the world.
  Removing the SAW filter reduces the insertion loss which improves the power efficiency, and also reduces the form factor of the devices.
    Improved Tx power efficiency and Rx sensitivity due to the lower RF front end insertion loss.
    Reduced form factor due to the footprint size saving in RF front end by removing the SAW filters.
Power efficiency improvement
Footprint size reduction

## Slide 4: Benefits from network and ecosystem viewpoint
Further complexity reduction of eRedCap devices will also facilitate further network deployments and ecosystem growth.
  SAW-less design will allow significant complexity and cost reduction of devices, and thus more devices could be deployed to cover a wider range of applications, bringing more customers and higher service utilization of the network. Therefore, SAW-less design will facilitate the growth of the ecosystem.
  More economical eRedCap devices will accelerate the network migration and market move towards 5G technology and away from legacy alternatives that are available today e.g., CAT-1bis devices. This will unleash new use cases and verticals benefiting the whole industry including module makers and operators.
  A single SKU design for global operation simplifies worldwide IoT device deployments for customers.
    A single SKU also streamlines the IoT deployment process, where devices can be deployed interchangeably across different regions without needing region-specific models.
    A single SKU ensures a consistent customer experience, and users benefit from the uniformity of product features and capabilities, regardless of their geographic location.

## Slide 5: Limiting factors to enable SAW-less implementation
Major limited factors have been identified for SAW-less implementation in 38.101-1:
  Noise for UE-coexistence in SAW-less design with small frequency offset in specific bands
    3GPP requires Tx “noise” into the protected frequency bands to not exceed -50dBm/MHz – specified as “Spurious Emission for UE coexistence” in TS 38.101-1.This is a major SAW-less design challenge in 5G NR designs compared to LTE IoT using much narrower channel BWs (<1.4MHz).
    For 5MHz PUSCH (reduced baseband bandwidth eRedcap), the above requirement becomes more realistic for SAW-less design but challenging in some critical scenarios due to higher order IMD products falling into the protected Rx bands.
      The worst case is n13 Tx noise  B14 Rx band (protected): -9MHz offset from the edge of LOWEST channel BW, affected by IMD7. Our measurements on a few existing PA types show spurious emission of -45-50dBm at antenna – marginal/not sufficient to meet 3GPP spec.
  Additional blocking requirements in specific bands:
    In-band Blocking (IBB) spec for 5G NR includes very challenging requirements for n71 (Case 3). The spec is much harder than other IBB and OBB specs.
Measured PA emission at -9 MHz offset from the the edge of lowest channel BW
Example of additional blocking requirements for n71 v.s. Other blocking requirements

## Slide 6: Solutions to supporting SAW-less implementation in Rel-19
Allow reduced maximum output power (power back-off MPR) for eRedCap when operating in HD-FDD mode in problematic bands, e.g., n13.
  Specify the power back-off via hard coded MPR term (e.g., via ) to reduce PA IMD7 non-linearity products of n13 falling into the protected Rx bands (b14) to ensure the spectrum emission level meet the 3GPP requirements.
    Hard coded MPR instead of signalling controlled MPR, to ensure no relaxation on the spectrum emission level limits for the protection of victim bands.
  Limit the proposed power back-off only to the problematic RB allocations. For example, ONLY in the lower edge of n13  LCRB*12*SCS > 3.6MHz and RBstart*12*SCS is < 1.8 MHz.
Consider a relaxed IBB requirement for eRedCap when operating in HD-FDD mode in n71.
  In FCC R&O 14-50, the television signal strength received by the UE is estimated at -23 dBm with assumption of a UE Rx antenna gain of -8 dBi. The 3GPP specifications also account for the case where the antenna gain may be as high as 0 dBi for device types include fixed or nomadic devices, and therefore, a more stringent blocking signal level (-15 dBm) is specified in 3GPP.
  The 0 dBi antenna may not be relevant for eRedcap devices with compact form factors. A lower RX antenna gain, e.g., -8 dBi, as used in FCC R&O 14-50 may be more relevant. Therefore, we suggest 3GPP also to consider a relaxed IBB requirement in n71 as an option to facilitate the SAW-less implementation of eRedcap in Rel-19.

## Slide 7: Proposals
The proposed work offers clear commercial benefits. The related issues and potential solutions are already identified and therefore we believe that the effort required to complete the normative work is limited and can fit within the remaining of Rel-19 with 0.25 TUs per meeting as follows:
  Proposal 1: Include the following objectives in RAN4 work in Rel-19 to further reduce the complexity of eRedcap devices
    Study the limiting factors in UE RF requirements in TS 38.101-1 and specify the corresponding mechanism(s) to enable SAW-less designs for HD-FDD eRedcap in FR1 [RAN4]
      Focus on PC3 eRedcap with baseband bandwidth reduction BW3/PR3 device (IE supportOfERedCap-r18 is present and IE eRedCapNotReducedBB-BW-r18 is NOT present).
      The mechanism to enable SAW-less eRedcap designs shall guarantee the public safety band protection, and that the corresponding spurious emission for UE co-existence level shall not be relaxed.
      Note: examples of limiting factors are such as band specific transmitter out of band emissions and receiver out of band blocking.
  Proposal 2: The proposed work can be formed as a new WID or added into the ongoing WID of UE RF enhancements for NR FR1/FR2 and EN-DC, Phase 4 (NR_ENDC_RF_Ph4).
  Proposal 3: The estimated time unit for this work is 0.25 TU in RAN4#114, 0.25 TU in RAN4#114bis, 0.25 TU in RAN4#115, and 0.25 TU in RAN4#116.

## Slide 8: References
[1] TR 38.875 Study on support of reduced capability NR devices v 17.0.0
[2] R4-2318359 Views on further reduction of UE complexity for eRedcap Sony
[3] RP-233636 Status report for WI: Enhanced support of reduced capability NR devices; rapporteur: Ericsson