## Slide 1: OD-SIB1 feature discussion
Sources: Panasonic
3GPP TSG RAN #106
Madrid, Spain, December 9-12, 2024
Agenda: 9.3.1.5
TDOC: RP-243010
For: discussion

## Slide 2: Background
RAN2 discussed "R2-2410842 Considerations on OD-SIB1 feature Deutsche Telekom, Vodafone, Lenovo, Fraunhofer IIS", which propose following and it was concluded as noted.
  Proposal 1: Clarify that Cell A can also transmit the WUS configuration for itself in case it intends to become a SIB1-less cell.

## Slide 3: Discussion
In our interpretation, "stand alone" is the case where UE is able to access the cell without the help of other cells.
  The reason not to support stand alone cell for OD-SIB1 is to support it requires MIB and potentially PDCCH need to provide the SIB1 equivalent information. One approach would be slimmed SIB1 info to be send MIB and PDCCH. The other approach would be UE obtains it from stored upper layer information. Both requires more discussion.
To transmit the WUS configuration for itself in other than SIB1 is different from standalone cell. This does not require MIB and PDCCH change.

## Slide 4: Discussion
The slow transition between OD-SIB1 cell and normal cell should be at least possible.
  Example is day time is normal cell and night time is OD-SIB1 cell.
From OD-SIB1 cell to normal cell
  The cell only to support OD-SIB1 capable UEs when this transition happens.
  SIB1 is changed to periodic transmission for normal cell.
From normal cell to OD-SIB1 cell
  If this cell support OD-SIB1 capable UEs only, to transmit the WUS configuration for itself in other than SIB1 can be helpful.
  If this cell also support OD-SIB1 non-capable UEs, reconfiguration of the cell itself would be only solution.