## Slide 1
Motivation on introduction Power Class 8 (PC8) for FR2
3GPP TSG-RAN Meeting #106 RP-243021
Madrid, Spain, 09 – 12 Dec., 2024
Agenda Item: 9.1.4
Document for: Decision
Huawei, HiSilicon, CEPRI, OPPO, vivo, Xiaomi, CATT, Spreadtrum, Honor, TD Tech, StarPoint, SRTC

## Slide 2
  Recently the potential opportunity is observed for roll-out of FR2 (frequency range 2, millimeter wave) network in some regions, e.g., China. To meet such opportunity, companies started to further consider the design of FR2 devices.
    FR2 power class 3 (PC3) was introduced for handheld UE since Rel-15, which assumes 2 panels with1x4 array of dual polarized antennas and min peak EIRP of 22.4 dBm. But based on analysis, it is found that the cost of adding one FR2 band with PC3 is 2 times more than adding one FR1 band supporting 2Tx and 4Rx, and the power consumption with FR2 PC3 is 3~4 times more than FR1. Thus FR2 PC3 would be more suitable for high-end handheld UE.
    To promote FR2 deployment, it would be better to also enable FR2 for both low and middle-end UEs to enrich the FR2 applications and improve FR2 UE availability. Therefore, complementary to FR2 PC3, a new power class with simplified RF architecture is considered mainly for low and middle-end UEs and devices with small form factor but high data-rate demand.
  RAN4 was discussing such new power class, which is named power class 8 (PC8), since April 2024. The agreements were reached in October meeting, but companies debated again in November. To seek wider common understanding, the discussion was triggered in RAN.
  Trade-off between the cost/power consumption and the performance to grow FR2 to more prosperous industries.
    PC8 is proposed to reuse FR2 power class 7 UE RF architecture of a single panel with 1x2 array of dual polarized antennas and min peak EIRP of 16.4dBm, but it can support the larger bandwidth more than 100MHz, which is aligned with the regional regulation, and CA/UL MIMO features.
    The cost of adding one FR2 band with PC8 to the UE is almost the same as adding one FR1 band with 2Tx and 4Rx. The power consumption of FR2 PC8 is a bit higher than FR1 thanks to the reduced number of Rx beams.
    The performance of FR2 PC8 can support the downlink 300Mbps for 8K ultra-high resolution 3D displays and downlink 500Mbps for 8K cloud XR service in the hotspot scenario such as stadium or CBD area. The challenge is mainly for uplink performance. But at the cell edge the performance of PUCCH for ACK/NACK and CSI and PRACH would not be the bottleneck for FR1-FR2 Dual-connectivity (DC).
  Clarification on urgency to introduce FR2 PC8 to respond the questions from some company
    China (CCSA) is promoting FR2 innovation to catch up the opportunity for FR2 deployment. It is expected to finalize the draft of CCSA phase I specification for FR2 based on 3GPP Rel-15 and Rel-16 specifications by February 2025. Any updates to the phase I standardization is assumed starting 1.5 year or 2 year later after the phase I specification is released.
    CCSA standard is aligned with 3GPP and usually introduces the new technique after 3GPP specified it. In this regard, the RAN4 agreements are to introduce FR2 PC8 in TEI18 and in the release independent manner from Rel-15, which can match the scope and timeline of CCSA phase I specification for FR2.
Background and motivation

## Slide 3
Analysis of FR2 Power Class 8 – cost and power consumption
FR2 power class 3 (FR2 PC3): typical RF architecture
Typical requirements: EIRP 22.4dBm,
Spherical coverage (50%) 11.5dBm
RF chains：
Two AIPs + IF (Intermediate frequency)
FR2 UE selects one AIP(Panel) out of two, and for each AIP 8 RF analog chains work simultaneously for reception and transmission
Beam management (BM)：
Multiple Rx beams supported, e.g., 7 Rx beams/AIP
Assuming BS has 16 SSB Tx beams，FR2 PC3 UE needs to do measurements for around 160 pairs of Tx-Rx beams for each beam management at least.
Power consumption of FR2 PC3
  Due to multiple analog RF chains and complex BM, power consumption of FR2 PC3 is 3~4 times of FR1, which further may lead to overheating issue
FR2 power class 8 (FR2 PC8): typical RF architecture
Typical RF requirements：EIRP 16.4dBm,
Spherical coverage (50%) 5.5dBm
RF chain：
One AIP + IF (Intermediate frequency)
PC8 uses 1 AIP(panel) with 2 pairs of X-pol antenna elements
Beam management (BM)：
AIP has the spatial coverage like an omni-directional antenna
Assuming BS has 16 SSB Tx beams，FR2 PC8 UE needs do measurements for less than 20 pairs of Tx-Rx beams for each beam management, which is 1/10 of PC3.
RF2 RF architectures |  | FR power mW | Cost $
PC3 | Two AIPs | 3~4X | 2~3Y
PC8 | One AIP | 2X | Y
-- | FR1*200MHz 4-layer | X | Y
  PC8 vs PC3 cost and power consumption comparison
Cost of FR2 PC3
  Adding one FR2 band supporting PC3, the cost is more than 2 times and the power consumption is 3~4 times than adding one FR1 band
  The total price of IF + 2xAIP would be more than $15

## Slide 4
Analysis of Power Class 8 for FR2 – Performance
  During RAN4#112, RAN4 agreed the targeted scenarios and UE types, with corresponding detailed simulation assumptions [1] for FR2 PC8 performance evaluation:
System level performance evaluation (UPT)
  Observation:
    For DL, the max DL throughput 300Mbps and 500Mbps for target use cases for evaluation can be well achieved even at the cell edge [2]
    For UL
      For the cell edge: usually HARQ ACK/NACK and CSI feedback can be transmitted by PUCCH with robust performance
      DSUUU pattern can be used for service with heavy UL THP

## Slide 5
Introduction of FR2 PC8 – RAN4 agreements
  RAN4 agreement:
    From RAN4#110bis April meeting to RAN4#112bis Oct meeting, 4 RAN4 meeting cycles with more than half years extensive discussion and evaluations, RAN4 reached the following agreements in RAN4#112bis [4].
RAN4 agreed to introduce FR2 power class 8
Procedure suggested by RAN4
  TEI18 CRs -> New R19 WI -> Rel-18/19 CRs
The only left open issue is how to describe the new UE in the specification (Table 6.2.1.0-1 in TS 38.101-2)
Specific wording on the new UE description is discussed with interesting companies and reach consensus before RAN4#113 [5]
RAN4 reached common understanding on the procedure that is captured in the chairman notes

## Slide 6
Proposals based on RAN4 agreements
  Approve CRs [5~7] and send LS to RAN2 [8] with the procedure on which RAN4 has common understanding
  Approve the new Rel-19 WI for introduction of FR2 PC8 to facilitate RAN5 conformance testing WI
    The objectives are shown below
Objectives
  Introduce new power class 8 for FR2, with the UE RF architecture assumption of single panel, dual polarization, 1x2 array, min peak EIRP of 16.4 dBm
    Targeted bands: n257, n258 and n261
    Supported UE channel bandwidth are up to 400MHz for single carrier operation
    CA and UL MIMO are supported
    Specify the necessary RF requirements
    Specify the necessary RRM requirements
    Release independence is from Rel-15

## Slide 7
  [1] R4-2414420, WF on introduction of new FR2 power class 8, Huawei, HiSilicon, RAN4#112
  [2] R4-2415628, Discussion on introduction of new FR2 UE power class, Huawei, HiSilicon , RAN4#112bis
  [3] R4-2415629, Updated simulation assumptions for introduction of FR2 Power Class 8, Huawei, HiSilicon, RAN4#112bis
  [4] R4-2417183, WF on FR2 Power Class 8, Huawei, HiSilicon, RAN4#112bis
  [5] RP-243017, CR on introduction of RF requirements for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [6] RP-243018, CR on introduction of RRM requirements for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [7] RP-243019, CR on release independence for FR2 power class 8 [FR2_PC8], Huawei, HiSilicon
  [8] RP-243020, LS to RAN2 on introduction of FR2 power class 8, Huawei, HiSilicon
Reference