## Slide 1: Support of “E-UTRA TN to NR NTN” connected mode mobility
Agenda Item: 10.3.2
Source: CATT, Thales, Deutsche Telekom, Inmarsat, Viasat, SK Telecom, ETRI, Fraunhofer IIS, Fraunhofer HHI, BMW, CBN, vivo, LG Electronics Inc.
3GPP TSG RAN #106
Madrid, Spain, December 9-12, 2024
RP-243114

## Slide 2
Background
Analyses on necessary RAN2 Spec impact
Proposals

## Slide 3: Background
Current E-UTRA TN to NR NTN mobility WI (RP-240924) includes inter-RAT IDLE mode mobility enhancement only.
On including the support of inter-RAT CONNECTED mode mobility in this WI, discussions have been carried out in RAN#103 ~ RAN#105, summarized as follows:
  In RAN#103: a number of Sat. and TN operators first raised interests and proposals to include also support of inter-RAT connected mode mobility, when the WI scope was discussed.
    Nonetheless, what necessary Spec impact is needed was unclear to companies (See discussion on RP-240061)
  In RAN#104: there was operator’s proposal (RP-241324), but not treated due to no expectation on WI expansion.
  In RAN#105: the proposal to support multiple SMTCs for connected mode mobility was proposed by a number of companies (including Sat. and TN operators) but was concluded as not pursued (See RP-241954 and RP-241756)
Observation 1: There have been a large number of operator interests to support inter-RAT E-UTRA TN to NR NTN mobility in CONNECTED mode in Release 19.
Observation 2: Till now, it is not clear what necessary RAN2 Spec impacts are needed to support this inter-RAT connected mode mobility feature (other than multiple SMTCs)
What happened in the past RAN plenaries?

## Slide 4: Analyses on necessary RAN2 Spec impact
In current TS 36.331, measurement configurations for inter-RAT mobility to NR are specified separately from E-UTRAN (i.e. measObjectNR/ReportConfigInterRAT)
Based on our analyses, current E-UTRA specifications may not be able to support the “E-UTRA TN to NR NTN” handover, due to the lack of (at least) following necessary Satellite assistance information in inter-RAT measurement configuration:
  DL polarization information
    This information is needed to avoid 3dB loss for measurements due to antenna polarization mismatch
    It corresponds to NR NTN parameter ntn-PolarizationDL in TS 38.331, and agreed to be introduced for IDLE mode mobility
  Satellite Ephemeris information
    This information is needed for the UE to do frequency compensation when performing DL measurement (which is the case for both IoT NTN and NR NTN)
    Note that this is Irrelevant to location-based CHO specified for NR NTN in TS 38.331.
    Note: Support of Multiple SMTC is not within the scope (due to the conclusion of not pursuing it from RAN105).
Necessary RAN2 Spec change to support “E-UTRA TN to NR NTN” handover

## Slide 5: Proposals
Proposal 1: RAN agrees to add the objective of “support of E-UTRA TN to NR NTN handover” into Rel-19 LTE_TN_NR_NTN_mob WI, with the specific scope that E-UTRAN provides satellite assistance information (e.g. polarization information, Ephemeris data, etc.) into NR-specific measurement configurations.
Proposal 2: RAN agrees the proposed WID revision in RP-243115 [1]
Proposals and proposed WID update
[1] RP-243115 Revised WID - R19 E-UTRAN to NR-NTN mob enh CATT, Thales, Inmarsat, Viasat, Deutsche Telekom, BMW

## Slide 6
Notes: 万物互联，无限沟通
Universal Connectivity, Infinite Communication.