## Slide 1
Evolution of NR Duplex Operation - Phase 2
RP-243136
3GPP TSG RAN Meeting #106
Madrid, Spain, 9th to 16th December, 2024
Agenda Item: 15.2
Source: Tejas Networks
Document for: Discussion

## Slide 2
Duplex Phase 2: Adjacent Channel CLI handling to improve SBFD throughput
Motivation:
In the presence of intra/inter operator adjacent channel,
  The cell edge Uplink(UL) throughput degradation is worse than the average throughput degradation for SBFD.
  The UL throughput degradation is due to the inter-BS ACI introduced by TDD/ SBFD-DL which increases as grid-shift (BS-to-BS distance) decreases.
  For higher BS Tx power and lower grid-shifts the degradation is increased for cell edge throughput and average throughput.
Fig: SBFD UL median throughput loss at cell edge and cell centre for FR-1
Fig: Median throughput loss (%) with Adjacent Channel CLI for FR-1

## Slide 3
Duplex Phase 2: Adjacent Channel CLI handling to improve SBFD throughput
In release-20, for SBFD systems, adjacent channel CLI handling need to be considered.
  Enhancing signalling between inter-operator gNB’s for adjacent channel CLI handling.
    Example: Spatial coordination between gNBs of different operators.
  Applicability of co-channel gNB-gNB CLI handling schemes for intra-operator and inter-operator adjacent channel CLI handling.
  Network deployment (ex. grid shift between the two different networks) to suppress the adjacent channel CLI.
Proposals:

## Slide 4
Motivation:
In Rel-19, it was agreed that DCI formats and Slot Format Indicator cannot be used to revert SBFD symbol to non-SBFD symbols.
In Rel-19, it was also agreed that during SSB symbols, SBFD capable UE will decode SSBs in downlink sub band and will not be treated as non SBFD downlink slots.
This will result in following issues:
  Suboptimal utilization of Time-Frequency resources during SSB or any other critical messages such as SIB.
  Delayed reception of critical messages (ex: SIB 8)
Duplex Phase 2: Further enhancements in Tx/Rx/Procedures of duplex Systems
Lack of link indication for SBFD UE resulting in delayed reception of critical messages

## Slide 5
Duplex Phase 2: Further enhancements in in Tx/Rx/Procedures of duplex Systems
Proposals:
Signaling enhancements enabling:
  Optimal utilization of Time-Frequency resources.
  Timely delivery of critical messages.
SDT enhancements
Paging enhancements