## Slide 1
RP-243138
3GPP TSG RAN Meeting #106
Madrid, Spain, 9th to 16th December, 2024
Views on Scope for R19 and R20 “AI-ML for Positioning Enhancement”
Agenda Item: 15.2
Source: Tejas Networks
Document for: Discussion

## Slide 2
The release-19 of 3GPP studied the AI-ML for Positioning Enhancements but
  The studied was limited to timing information based Positioning only,
  AI-ML techniques were not considered for training and inference of angle information,
  In RAN-105, the case-2a and case-2b were deprioritized.
The reporting of timing information alone can’t meeting the positioning accuracy KPIs
  Target KPI:
    2D position error 20 cm for 90% of the users.
    Vertical position error 1.5m for 90% of the users.
The case-2a and case-2b should be discussed and the aspects related to AI-ML for Positioning Enhancement should be standardized.
Motivation
The impact of measurements beyond timing information (such as angle of arrival and departure, etc.) on positioning accuracy should be studied for “AI-ML for positioning enhancements”. Furthermore, the support of 3GPP standards should be extended for case-2a and case-2b.

## Slide 3
The performance of AI-ML-based positioning depends on the correlation between channel measurements collected from user equipment at different locations.
The more correlated and richer the channel measurements are, the easier it will be for the AI-ML model to make accurate inferences about the UE location and/or intermediate measurements (such as time of arrival, angle of arrival/departure, and the LoS/NLoS state).
Reporting channel measurements that include both time and angle information can offer better performance compared to using time alone.
Furthermore, it can reduce the number of TRPs required to achieve the positioning accuracy targets, resulting in reduced network overhead.
Angle and Time based AI-ML Positioning Enhancements
AI-ML Model
AI-ML Model
PDP information based positioning
PADP information-based positioning

## Slide 4
Work Item for the “AI-ML for Positioning Enhancements”:
  Extend the support for the Case-2a and Case-2b [If possible in Release 19; otherwise, in Release 20.],
  Based on angle measurements [A study to be performed, followed by the normative work in Release 20]
    For all the 5 AI-ML based positioning use-cases.
    Support for hybrid positioning schemes for AI-ML assisted positioning use-cases.
[RAN-1/2/3]AI-ML for Positioning Enhancement: Phase-2
Proposal
Reporting channel measurements that include both time and angle information can offer better performance compared to using time alone. Furthermore, it can reduce the number of TRPs required to achieve the positioning accuracy targets, resulting in reduced network overhead.
Observation