## Slide 1: [Offline][101] To prepare detailed wordings for Re-TX loop
LG

## Slide 2: [AT127bis][101][V2X/SL]
Scope: To prepare detailed wordings for Re-TX loop .
Intended outcome: MAC CR in R2-2409351 to be agreed in principle. LG will inform the offline discussion schedule later.
Deadline: Comeback in Thursday CB session.

## Slide 3: Background
RAN2 agreed to use Re-Tx loop for MCSt in Monday session.
RAN2 agreements are as follows:
  Re-TX loop will be considered.
  We need more accurate conditions when Re-TX loop will be used.
  Detailed wordings can be discussed offline until Thursday CB session.

## Slide 4: Discussion on the TP(1/2)
Agreed TP for initial Tx loop
5> else if the selected resource pool is not Dedicated SL-PRS resource pool:
6> randomly select the time and frequency resources for one transmission opportunity, or for more than one opportunities (if MAC entity decides a number of consecutive slots for Multi-consecutive slots transmission other than SL-PRS larger than 1), from the resources indicated by the physical layer as specified in clause 8.1.4 of TS 38.214 [7] which occur within the SL DRX Active time, if configured, as specified in clause 5.28.2 of the destination UE selected for indicating to the physical layer the SL DRX Active time above, according to the amount of selected frequency resources, the remaining PDB of SL data available in the logical channel(s), and the remaining SL-PRS delay budget of the SL-PRS transmission(s), if available, allowed on the carrier.

## Slide 5: Discussion on the TP (2/2)
TP for Re-Tx loop
use the Re-Tx loop, only for the case where “the number of selected transmission opportunities in the initial transmission loop (i.e., n_MCSt) < n_required_transmissions for a TB”.
  To avoid UE behavior which is entering the Re-Tx loop in case of “n_MCSt is equal to n_required_transmissions for a TB”
The change may be only applicable to blind retransmission case.
Consider RAN2 agreement for MCSt (i.e., “For a resource pool configured with PSFCH resource, UE can NOT select consecutive slots (i.e., MCSt) for transmissions of a single TB.”)
  There is a corresponding NOTE in the MAC specification as follows:
    “NOTE 3Ah:For a resource pool configured with PSFCH resource, UE cannot select consecutive slots for SL transmissions of a single TB for Multi-consecutive slots transmission.”
In conclusion, text related to 1) and 2) is captured in the Re-Tx loop.

## Slide 6: Draft_TP

## Slide 7: Conclusion