## Slide 1: [AT127bis][110][NES]

## Slide 2: [AT127bis][110][NES] (OPPO)
Scope: To calculate signalling overheads between option-a and option-b. To check companies’ opinion if P1 in R2-2407974 is ok or if option-a should be considered instead.
Intended outcome: Discussion summary in R2-2409372. OPPO will announce the offline discussion schedule via email.
Deadline: Comebacks in Thursday CB session

## Slide 3: Reference
R2-2407974, Report for [POST127][109][NES] (OPPO), OPPO
R2-2408238, Discussion on adaptation of common signals/channels transmissions, Huawei, HiSilicon
R2-2408562, Further discussion on common signal transmission adaptation, Apple
R2-2408102, Discussion on adaptation of common signal transmissions, vivo

## Slide 4: Q1: To calculate signaling overheads between option-a and option-b

## Slide 5: An example (Ns = 2, N = 4)

## Slide 6: PMO signaling OH @ Legacy
= Log2 (Nr-Of-Symbols-in-one-Frame * (T/N)) * Ns
  Where Nr-Of-Symbols-in-one-Frame is numerology specific
  “* (T/N)” allows PMO located out of the corresponding PF (but before the next PF)
  “* Ns” allows intra-PF PMO configuration, e.g., every 2 POs will use the same pattern

## Slide 7: PMO signaling OH @ Option-a
= Log2 (Nr-Of-Symbols-in-one-Frame * G) * Ns
  Where Nr-Of-Symbols-in-one-Frame is numerology specific
  “G” is “the number of frame of the gap (between PF:s) + 1”, i.e., G = 1 for consecutive PF:s (Note that G has to be signaled separately if not fixed)
  “* Ns” allows intra-PF PMO configuration, e.g., every 2 POs will use the same pattern

## Slide 8: PMO signaling OH @ Option-b: Baseline
= Log2 (Nr-Of-Symbols-in-one-Frame * G * H) * H * Ns
  Where Nr-Of-Symbols-in-one-Frame is numerology specific
  “G” is “the number of frame of the gap (between PF:s) + 1”,
  “H” is “the number of condensed PFs”. e.g., if we want to increase Ns from 2 to 8, then H = 4. Or we want to increase Ns from 4 to 8, then H = 2.
  “* H * Ns” allows PMO configuration for all POs, e.g., 8 PMOs can be configured (i.e., more configurability than option-a)

## Slide 9: Comparison: Option-b (Baseline) minus Legacy
G = 1 N=T/2 | Ns = 1 H = 2 | Ns = 2 H = 2 | Ns = 2 H = 4 | Ns = 4 H = 4
15kHz | 9 | 18 | 62 | 124
30kHz | 10 | 20 | 68 | 136
60kHz | 11 | 22 | 74 | 148
120kHz | 12 | 24 | 80 | 160
480kHz | 14 | 28 | 92 | 184

## Slide 10: Comparison: Option-b (Baseline) minus Option-a
G = 1 | Ns = 1 H = 2 | Ns = 2 H = 2 | Ns = 2 H = 4 | Ns = 4 H = 4
15kHz | 10 | 20 | 64 | 128
30kHz | 11 | 22 | 70 | 140
60kHz | 12 | 24 | 76 | 152
120kHz | 13 | 26 | 82 | 164
480kHz | 15 | 30 | 94 | 188

## Slide 11: Q2: To check companies’ opinion if P1 in R2-2407974 is ok or if option-a should be considered instead

## Slide 12: Discussion
Proposal 1: Select option-b as baseline for R19 NES paging enhancement.
Proposal 2: R2 further discuss the impact of RRC configuration (e.g., to restrict the value of Ns) and the impact of legacy UE for option-b.

## Slide 13: MoM
[Ericsson] see some restriction w.r.t the legacy UE handling. Tend to split between different R19 NES UE w.r.t using the legacy / new paging resources. Or if we optimize the signaling, it can be like option-a. [Huawei] it is an additional enh regarding the legacy/new paging resource. For the signaling OH calc, we understand option-a is the same as legacy, for option-b, the OH is related to the number of PMO we would like to additionally configure. [LG] Same as ER, only R19 paging resource is considered for option-a/b. [Ericsson] disagree with Huawei since the additional OH comes from the additional PMO to be configured. [Samsung] true option-b requires more bits. Yet do not see the problem for legacy UE handling. [OPPO] also tend to see legacy UE handling as an independent dimension.

## Slide 14: MoM
[vivo] calc is correct. Companies can consider ways to solve it, like to restrict max Ns value. [Apple, Qualcomm] calc is correct. Anyway we mainly target at low load scenario. ER seems concern on the PO collision issue, yet it should not be a big concern for low load scenario. [vivo, LG] if we can restrict Ns value, then fine with option-b. [Xiaomi] We see another way to optimize the signaling overhead for option-b [Qualcomm] the left issue depends on how we conclude on legacy UE handling. [ER] should allow legacy/R19 UE to share the PF or not.

## Slide 15: WF
Proposal 1: Select option-b as baseline for R19 NES paging enhancement.
Proposal 2: R2 further discuss the impact of RRC configuration, and aiming at signaling overhead minimization (e.g., Ns=8 and FFS for other larger values)
Proposal 3: R2 further discuss the impact of legacy UE for option-b (e.g., whether to allow legacy and R19 UE to co-ex in the same PF).

## Slide 16: Annex: Other way to optimize

## Slide 17: PMO signaling OH @ Option-b: Repetitive Pattern
= Log2 (Nr-Of-Symbols-in-one-Frame * G) * Ns
  Where Nr-Of-Symbols-in-one-Frame is numerology specific
  “G” is “the number of frame of the gap (between PF:s) + 1”, G = 1 for consecutive PF:s (Note that G has to be signaled separately if not fixed)
  “* Ns” means every 2 POs will use the same pattern (same as option-a)