3GPP TSG-RAN4 Meeting #111 R4-2407832 Fukuoka, Japan, May 20 – 24, 2024 CR-Form-v12.2 CHANGE REQUEST 38.133 CR draft rev Current version: 18.5.0 For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests.

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | [draftCR IR2] CR for inter-RAT EUTRAN measurements case b-1 without gap |
| --- | --- |
| Source to WG: | Xiaomi |
| Source to TSG: | R4 |
| Work item code: | NR_MG_enh2-Perf |  | Date: | 2024-5-22 |
| Category: | B |  | Release: | Rel-18 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | According to the agreed WF R4-2403543, a test case for inter-RAT EUTRAN measurements case b-1 with MG but no DRX configuration is needed (IR2) |
| Summary of change: | Define a test case for inter-RAT EUTRAN measurements case b-1 with MG but no DRX configuration. |
| Consequences if not approved: | The RRM requirements cannot be verified in realistic environment. |
| Clauses affected: | A.6.6.x |
|  | Y | N |  |  |
| Other specs |  |  | Other core specifications | TS/TR ... CR ... |
| affected: | X |  | Test specifications | TS 38.533 |
| (show related CRs) |  |  | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

| This CR's revision history: |  |
| --- | --- |

--------------START OF CHANGES #1--------------

#### A.6.6.x.y	 SA NR - E-UTRAN event-triggered reporting without gap under non-DRX in FR1

##### A.6.6.x.y.1	Test Purpose and Environment

The purpose of this set of tests is to verify that the UE makes correct event-triggered reporting of inter-RAT E-UTRAN measurements without gap as there are vacant RF chains available for UE measurements when operating in standalone (SA) operation with PCell in FR1. This test shall partly verify the cell search and measurement requirements in Clauses 9.4.8.

The serving frequency and the target frequency should be selected such that UE reports [nogap-noncsg] for the target frequency given the serving frequency.

##### A.6.6.x.y.2	Test parameters

In each test there are two cells: Cell 1 and Cell 2. Cell 1 is the NR PCell and Cell 2 is an inter-RAT E-UTRAN inter-RAT neighbour cell. In the measurement control information from the PCell it is indictated to the UE that event-triggered reporting with Event B2 (PCell becomes worse than threshold1 and inter RAT neighbour becomes better than threshold2) is to be used. Each test consists of two consecutive time periods, with durations T1 and T2, respectively. Prior to the start of time duration T1, the UE shall be fully synchronized to Cell 1. During T1, the UE shall not have any information on Cell 2.

Supported test configurations are shown in table Table A.6.6.3.2.1-1. General test parameters are provided in Table Table A.6.6.3.2.1-1. Test parameters for Cell 1 and Cell 2, valid for both time duration T1 and T2, are provided in Tables Table A.6.6.3.2.1-3 and Table A.6.6.3.2.1-4, respectively.

##### A.6.6.x.y.3	Test Requirements

Refere to the requirements in A.6.6.3.1.2.

----------------END OF CHANGES #1--------------

# Comments

The new requirements introduced in R18.

‘ncsg’ cases can be covered by existing requirements and TC

However, in this TC, the UE’s behavor to support nogap-noncsg will be overrided by the NW’s MG conifguation.

No EMW configuration needed.

Table A.3.11.1-1: SMTC.1: SMTC Pattern 1 for SMTC period = 20 ms and duration = 1 ms

| SMTC Parameters | Values |
| --- | --- |
| SMTC periodicity | 20 ms |
| SMTC offset | 0 ms |
| SMTC duration | 1 ms |

Need not if UE needs perform the interRAT LTE measurement within gap.