## Slide 1: MPS Priorities for Rel-20 5G-Advanced
Viqar Shaikh, Robert Streijl - Peraton Labs
Additional supporting companies: CISA ECD, AT&T, T-Mobile USA, Verizon.

## Slide 2: Outline
Study of the following topics:
  MPS priority for IoT communications
  MPS support in the 3GPP system with satellite

## Slide 3: Rel-20
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Study on MPS Rel-20 | On-demand MPS priority for IoT communications, primarily for data and messaging. Includes Cellular IoT (CIoT) and Narrow Band IoT (NB-IoT), both in 4G and 5G, and RedCap. This may, among other features, include enhancements to support priority for CP/UP CIoT Optimization and Non-IP Data Delivery (NIDD). MPS priority for IMS-based voice/video, data and messaging services in the 3GPP system with satellite. This may, among other features, include identifying enhancements to Store and Forward and discontinuous access for delivering priority treatment to MPS services. | MPS2, MPS_Sat | SA2 | Yes | SA3

## Slide 4: MPS priority for IoT
There is a need to provide MPS priority for authorized IoT communications during network congestion situations (e.g., during emergency and disaster events).
For example, MPS priority is needed to allow certain IoT devices to communicate with remote servers (such as a Government Agency server) during network congestion situations when normal IoT communication is not possible or degraded.
Stage 1 requirements for the support of MPS using IoT devices with MPS subscription is specified in TS 22.153 (SA1 Work Item: MPS2).
There is a need to provide a complete architectural solution including for on-demand activation/deactivation of MPS priority of IoT communications for IoT devices with a subscription for MPS.

## Slide 5: MPS support in the 3GPP system with Satellite
There is also a need to support MPS priority in the 3GPP system with satellite.
Support of MPS when the UE/IoT device has satellite access is important for priority communication backup during certain disaster scenarios such as when terrestrial access networks are unavailable or degraded. In some cases, satellite may be the only available access and is therefore critical for MPS communications.
Stage 1 requirements for the support of MPS in the 3GPP system with satellite is specified in TS 22.153 Release 20 (SA1 work item: MPS_Sat).
There is need to identify where stage 2 architectural enhancements are needed to provide a solution for MPS priority in the 3GPP system with satellite.