## Slide 1: Discussion of Multi-modality handling in NG-RAN for QoS flows
China Mobile, Interdigital, Huawei, Hisilicon
SP-241856
3GPP TSG SA Meeting #106
Madrid, Spain, December 10 – 13, 2024

## Slide 2: Multi-modality handling in NG-RAN for QoS flows
  The requirement of Multi-modal communication service has been specified in SA1.
    In TS22.261 clause 6.43. Tactile and multi-modal communication service, and clause 7.11 KPIs.
    5G system shall enable an authorized 3rd party to provide policy(ies) for flows associated with an application. The policy may contain e.g., the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information.
    In TS22.156（Mobile Metaverse Services）clause 5.1.1.2, the requirement of [R-5.1.1-002] , [R-5.1.1-004]
    5G system shall provide a means to associate and coordinate data flows related to one or multiple UEs.
  Observation1: 5G system should support to provide policy for flows which require the association and coordination transmission.
Media components | synchronization threshold (note 1) | 
audio-tactile | audio delay: 50 ms | tactile delay: 25 ms
visual-tactile | visual delay: 15 ms | tactile delay: 50 ms
NOTE 1: for each media component, “delay” refers to the case where that media component is delayed compared to the other. |  | 

## Slide 3: Multi-modality handling in NG-RAN for QoS flows
  Existing capabilities in 3GPP SA2:
  In Rel-18, SA2 has specified in TS 23.501 clause 5.37.2: The Multi-modality ID which is provided from AF to PCF to support the policy generation to handle the multi-modal service, which consists of several data flows that relate to each other and that are subject to application coordination.
  In Rel-18, the Multi-modality handling in NG-RAN has been discussed in study phase but not concluded.
  Requirement of Multi-modality handling in NG-RAN for QoS flows:
  In Rel-19, RAN2 has sent LS to SA2 that “RAN2 agreed that the multi-modality information (e.g., MMSID), can be used for joint admission control and QoS flow to DRB mapping “(R2-2409272).
  RAN3 has sent LS to SA2 that “it is technically feasible to enhance NGAP to provide the MMSID to NG-RAN node”(R3-245682)
  And SA2 also check with SA4 about the requirement, SA4 has sent LS reply (S4-242223) that “From an XR service perspective, it is generally desirable that the gNB should try to grant all associated QoS Flows for the XR service whenever possible”.
  Observation2: In order to improve the coordination QoS handling for multi-modal services, NG-RAN can do joint admission control for the QoS flows with considering the multi-modality information.
  Observation 3: It is 5GC can get the MMSID from AF to reflect the Multi-modal service requirement, and therefore it is suggested the 5GC can send the MMSID(e.g. together with other existing parameters) to NG-RAN.

## Slide 4: Multi-modality handling in NG-RAN for QoS flows
  Current Discussion status
  In Rel-19, this topic has been discussed in SA2 since May meeting in 2024.
  SA2 has discussed and exchange the LS with RAN2/3 for twice and SA4 for one time.
  In November meeting, this LS is objected by one company.
  Way forward proposal:
  MMSID can be provided to the NG-RAN over the control plane in N2 SM information and SA2 is requested to support the above feature and update its specification accordingly.
  NOTE: In TS23.501 clause 5.37.2, the MMSID is assigned by an Application Function, so it is not globally unique. Therefore, existing parameter (e.g., AF ID) may need to be provided along MMSID to NG-RAN. This is subject to further discussion at SA2.

## Slide 5: Annex
  The requirement of Multi-modal communication service is specified in SA1.
    In TS22.261 clause 6.43. Tactile and multi-modal communication service, and clause 7.11 KPIs.
    The 5G system shall enable an authorized 3rd party to provide policy(ies) for flows associated with an application. The policy may contain e.g. the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information.
    The 5G system shall support a means to apply 3rd party provided policy(ies) for flows associated with an application. The policy may contain e.g. the set of UEs and data flows, the expected QoS handling and associated triggering events, other coordination information.
    NOTE: The policy can be used by a 3rd party application for coordination of the transmission of multiple UEs’ flows (e.g., haptic, audio and video) of a multi-modal communication session.
    In TS22.156（Mobile Metaverse Services）clause 5.1.1.2, the requirement of [R-5.1.1-002] , [R-5.1.1-004]
    [R-5.1.1-002] The 5G system shall provide a means to associate and coordinate data flows related to one or multiple UEs e.g., associated with the same object in digital twin applications provided by the mobile metaverse service.
    [R-5.1.1-004] Subject to operator policy, the 5G system (including IMS) shall support a mechanism, including enabling one or more authorized third party(ies) to coordinate multiple service data flows of a single mobile metaverse service delivered to/from one or more UE(s). Multiple UEs may be associated with one user/location or different users at different locations potentially using different access networks, i.e., 3GPP and non-3GPP.