## Slide 1: Discussion for the introduction of EIF
China Mobile, NEC
S2-24xxxx
SA WG2 Meeting #S2-166
18 - 22 November, 2024, Orlando, USA

## Slide 2: EIF related function description
  Editor’s NOTE: It is FFS whether or not EIF will use network data analytics framework as defined in TS 23.288.
  1. The difference of the functionalities of EIF and NWDAF.
  The functions of EIF are mainly to do the energy related information collection, calculation and exposure the required granularities of energy consumption information. The 5GC can use the energy consumption information to assist the policy generation or NF selections.
  An NWDAF may contain the following logical functions: 1)Analytics logical function (AnLF): which performs inference, derives analytics information (i.e. derives statistics and/or predictions based on Analytics Consumer request) and exposes analytics.2) Model Training logical function (MTLF): which trains Machine Learning (ML) models and exposes new training services (e.g. providing trained ML Model).[TS23.288]
  Observation1: There is big difference between the EIF and NWDAF, so it is suggested to define the EIF independent from NWDAF.
  Observation2: NWDAF is a complicated NF which consisted of Analytics logical function and Model Training logical function, therefore the EIF services should not follow the NWDAF services description.
  Observation 3: Binding EIF to NWDAF leads to unnecessary NWDAF deployment for operators in some scenarios.

## Slide 3: EIF related function description
  Editor’s NOTE: It is FFS whether or not EIF will use network data analytics framework as defined in TS 23.288.
  2. The difference of description format.
  The request of NWDAF service description format as below
    Example:
    1) The consumer of these analytics shall indicate in the request or subscription:
    - Analytics ID = "Load level information";
    - Analytics Filter Information: S-NSSAI, DNN, etc.
  Observation 4 : the EIF processing is not “Analytic”, so it is suggested not to reuse the “Analytic” description format, and the EIF service description should follow the other NFs which should be captured in TS23.501/TS23.502.
  3. The SBA architecture (OAM also support the SBI interface) support the various consumers for different tasks, to retrieve the parameters with using the same service operation.
    Data collecting from 5GC NF or OAM do not need to be tied to NWDAF. The SBI interface support to expose information/data to different consumer NFs.
  Observation 5 : SBA support the data/information event exposure for different purpose, and more NF can be defined to retrieve the information, which should not bind with NWDAF.

## Slide 4: EIF related function description
  Editor’s NOTE: It is FFS whether or not EIF will use network data analytics framework as defined in TS 23.288.
  4. For future evolution, there maybe new energy consumption information e.g. from CP or from RAN, which can be collected, calculated and considered, so it is suggested there is an EIF function which is not combined with NWDAF, and this function can develop without the limitation of NWDAF framework.
  Observation 6 : the EIF may develop further and no need to bind with NWDAF.