## Slide 1: Discussion on termination of VFL training
SA2#166
ZTE

## Slide 2: Background
The following editor’s notes are captured in agreed S2-2411194 of NWDAF initiated VFL training:
Editor’s Note: Whether VFL Training termination Flag in the termination message is required is FFS.
Editor’s Note: Possible procedures to be executed at the end of the VFL training (to terminate a training session and to store/handle trained models) are FFS.

## Slide 3: Background
Here discusses two options of termination message :
Possible types of termination message: unsubscribe & request
Option 1: Using cause code in the existing ‘MLModeltraining_unsubscribe service operation’ or other new ‘Unsubsribe’ type service operation as well as in the existing ‘Nnwdaf_MLModelTrainingInfo_Request’ or other new ‘request’ type message, potential cause code are listed below: VFL Client NWDAF/AF is unselected by the VFL Server NWDAF for the VFL training process (TBD until VFL client re-selection is agreed) VFL process is suspended or finished. Nokia prefer Option 1.
Option 2: Using VFL termination flag in the existing ‘MLModeltraining_unsubscribe service operation’ or other new ‘Unsubscribe’ service operation as well as in the existing ‘Nnwdaf_MLModelTrainingInfo_Request’ or other new ‘request’ type message
Option 3: Using termination flag in ‘Nnwdaf_MLModelTrainingInfo_Request’ service operation or other ‘ request’ type service new, using cause code in the ‘MLModeltraining_unsubscribe service operation’ or other new ‘Unsubsribe’ type service operation

## Slide 4: Discussion on VFL termination message
Evaluation:
  The cause code is extendable and provide reasons to client for the termination of VFL training process.
  We did not introduce HFL termination flag in Rel-18
  Whether we include VFL termination flag is determined by the service operation we chosen.
  Main Spec impacts:
  Option 1 reuses the Rel-18 termination mechanism with new cause code that is future extendable.
  Option 2/3 introduces new VFL termination flag which is a new parameter.

## Slide 5: Discussion on Possible procedures to be executed after VFL training
The VFL Server and each VFL Client, stores the VFL correlation ID and latest information related to their locally trained Models. The VFL correlation ID will be sent by VFL server to VFL client at the start of inference. The VFL correlation ID will be used by VFL client to identify the trained ML Model information and conduct inference correspondingly.
The NWDAF and AF act as VFL client & VFL server optionally stores the trained ML Model to ADRF after VFL training process the stored ML model can be retrieved using ML Model ID during VFL inference if needed.(was proposed by Nokia, Ericsson suggested not include in this discussion topic)
If the VFL client and/or VFL server choose to store the trained ML model in ADRF, they need to locally maintain a mapping between the ML Model ID and the VFL correlation ID. Otherwise, the VFL client or server will be unable to retrieve the appropriate ML model when processing a VFL inference request.(Technical view raised by ZTE)
Alternatively, VFL server and client store the VFL correlation ID also in the ADRF along with the model(proposed by Nokia); However, this means that NWDAF and AF need to use VFL correlation ID to retrieve the ML Model from ADRF, which is a bit strange. (Technical view raised by ZTE)
Trusted AF and NWDAF can use Nadrf_MLModelManagement_StorageRequest to store the Model. Untrusted AF may store via NEF but the procedure is not clear.
Any other potential procedures?

## Slide 6: Way forward
Stable Agreement
We postpone the VFL termination flag discussion until we decide the service operation that is used in the VFL training process. Modify the first EN to: Editor’s Note: Whether VFL Training termination Flag in the termination message is required will be determined after we decide the service operation used in VFL training process.
The VFL server sends VFL training termination message to VFL Client if it decides to terminate the VFL training process. The VFL Server and each VFL Client, stores the VFL correlation ID and latest information related to their locally trained Models.
NOTE X: The VFL correlation ID may be used later for inference.
Delete 2nd EN based on the agreement
Other agreement proposal to be discussed:
The VFL Sever(i.e. NWDAF) and VFL Client (i.e. NWDAF and trusted AF) may optionally store the latest ML Model information to ADRF after VFL training process.
NOTE Y: The VFL server and VFL client need to locally maintain the mapping relationship between ML Model ID and VFL correlation ID locally if they stores the ML Model information to ADRF after VFL training process.