## Slide 1: Discussion On UE-Side Data Collection Reply LS to RAN
InterDigital Inc.
S2-XXX
SA2#166

## Slide 2: RAN2 email discussion
RAN2 is still working on the response to S2-2411191, to be provided in R2-2410504:
  Note that discussion isn’t finalized, but there is certain signs on commonality of views on for questions 3 to 6, as follows:
Question from SA2 | Preliminary views on RAN2 reply | Observations
Q3 - Impact on normal UE operation | “RAN2 has not evaluated/analyzed the impact on UE’s normal operation due to the full controllability of the data collection process” | Some companies question the meaning of “normal UE operation” 17 companies responded
Q4 - Whether standardized data content refers only to data collected according to measurement configuration | “Standardized data refers to data whose format/content is explicitly defined in 3GPP specifications, allowing the network to understand its content and meaning” | This version of the response was agreed by 17 companies
Q5 - Roaming considerations | “Roaming considerations are outside the scope of RAN2” | Although all 17 companies agreed on answer, not agreement on further RAN2 evaluation of roaming
Q6 - What is sufficient to consider visibility (e.g., if MNO need to verify the match between collected and transferred data) | “As stated in the LS sent from RAN, visibility of data content signifies that the MNO will be able to be aware of, access, and comprehend the content of the collected/reported data without the need of SLA. Thus, full visibility should allow the MNO to verify/match measurements configured and measurements reported” | Larger spread on replies was noted, with some companies questioning whether further work may be need by RAN2 or whether the question is a requirement issue not in scope of RAN2

## Slide 3: RAN2 email discussion
Unfortunately for Q1 and Q2, RAN2 did not find clear consensus:
  However, a certain need to separate measurement configuration and data transfer, in both Q1 and Q2, was detected:
Question from SA2 | Some preliminary views on RAN2 reply | Observations
Q1 - NG-RAN involvement | “For the beam management use case, the NG-RAN is involved in providing required measurement configuration (i.e., how to measure the reference signals), if needed. RAN2 has not reached a consensus on whether NG-RAN is involved in data transfer from UE to the server for data collection for UE-side model training/OTT server, as it depends on different UE-side data collection solution” | Based on preliminary responses, it would appear that RAN2 still requires time to further evaluate the question. E.g., “RAN2 has not reached a consensus on whether NG-RAN is involved in data transfer from UE to the server”
Q2 - Which entities and under what conditions controllability is performed | “SA2 can assume that the gNB is involved in providing required radio measurement configuration (if needed) for beam management use case and LMF is involved in providing required PRS measurement configuration (if needed). However, RAN2 has not agreed that the gNB/LMF is in charge of “initiating, terminating and fully managing data transfer”.” | There’s still no consensus on what question to answer: E.g., “Q2 is asking about data transfer, why should we mention data collection process here?”

## Slide 4: On the view of some SA2 companies regarding reply to RAN
There is no consensus on the feasibility of any of the options requested by RAN, but some common aspect may be highlighted:
Reply Proposal from: | Main aspects of proposal | Observations
CATT (S2-2411515) | For option 1b, Option 2 (UP), full/partial visibility of UE-side data collection for UE-side model training cannot be supported by the existing specifications Option 3(UP) not feasible, form SA2 perspective | More time required to study options
Qualcomm (S2-2411558) | For option 1b, SA2 needs to study further how to tailor and enhance the existing solution defined in clause 6.2.8 in TS 23.288 based on RAN’s requirement For option 2, if FTP is LMF, CP and UP solutions are feasible, for other UCs (i.e., CSI and beamforming) further study is required For option 3, UP solution requires further study in SA2 and for CP, SA5 needs to address it. | Feasibility is possible for some of the options, based on specific use cases, for other options, a study is required
Samsung (S2-2411752) | Controllability of MNO on data transfer for Option 1a and Option 1b should be marked as “Full controllability is not possible” Feasibility for option 2 and option 3 is FFS, as additional aspects need to be considered. | This proposal also suggests that additional work is FFS
Ericsson (S2-2411647) | For option 1b, full controllability and visibility of UE-side data when server is inside CN operator domain For UP solution for option 2 and 3, there is no indication that these options cannot work There are multiple way to trigger the UE to initiate data transfer, for both CP and UP | “…in TS 23.273 clause 5.10, support of Positioning over user plane connection between UE and LMF for non-regulatory service, similar mechanism maybe developed” This seems to indicate that work is need to develop such solution

## Slide 5: On the view of some SA2 companies regarding reply to RAN
There is no consensus on the feasibility of any of the options requested by RAN, but some common aspect may be highlighted:
Inputs that are not reply LS type
Reply Proposal from: | Main aspects of proposal | Observations
Apple (S2-2411716) | SA2 needs more time to study possible solutions for option 1b and option 2 before providing a feasibility analysis on the questions raised by RAN | More time required to study options
T-Mobile (S2-2412184) | Initial evaluation by SA2 indicates that the UP aspects of both options 2 and 3 are technically feasible SA2 would need further inputs from RAN2, and sufficient time as part of a full study, where concrete solutions are developed | Preliminary observation from some companies indicate UP aspects of both option 3 and option 3 are feasible. This is shared by other papers. More time is required to develop concrete solutions
InterDigital (S2-2412312) | Initial evaluation by SA2 indicates that the UP aspects of both options 2 and 3 are technically feasible, as are the possibility to address RAN requirements on data collection using option 1b, option 2 or option 3 SA2 would need further inputs from RAN2, and sufficient time as part of a full study, where concrete solutions are developed | We can conclude that all options are feasible, however a full evaluation is need and this will require a formal study
Tdoc from: | Main aspects of proposal
OPPO (S2-2411833) | Proposal 1: SA2 only need to focus on study and analyze the feasibility of MNO’s full controllability and full visibility and the feasibility of UP solution for option 2 and 3. Proposal 2: For option 2/3, full visibility is guaranteed so no need to have option B/C. For option 1b) full visibility can be supported for standardized data but cannot be supported for non-standardized data, and also a mix of standardized and non-standardized data.
LGE (S2-2411975) | For Option 1b, full controllability and full visibility for standardized data of UE-side data when data collection server is inside MNO domain.

## Slide 6: Way forward:
Work together to bring a formal SID on UE-Side Data Collection, as part of the Rel.20
  E.g., OPPO has already brought a discussion paper that highlights data collection as one aspect to be studied in Rel.20
Our reply to RAN could be as simple as:
  SA2 concluded that a full evaluation of all options would require an SA2 study, where concrete solutions may be developed.
  A formal SID on UE-Side Data Collection, will be proposed as part of the Rel.20