3GPP TSG-SA3 Meeting #116 	draft_S3-242046-r1

# Jeju, South Korea, 20th - 24th May 2024

# Source:	China Telecom

# Title:	Conclusion to KI#1

# Document for:	Approval

Agenda Item:	5.3

# 1	Decision/action requested

This contribution proposes to add conclusion to KI#1.

# 2	References

# 3	Rationale

The contribution proposes to add conclusion to KI#1.

# 4	Detailed proposal

It is suggested to approve the following change.

*************** Start of the change ****************

# 8	Conclusions

## 8.1	KI#1: Security for dedicated UPF interacting with PLMN through N4 interface

### 8.1.1	Analysis

The key issue#1 addresses the need to support topology hiding, malformed message blocking, wrong type message blocking, authentication and authorization between PLMN operational domain and PNI-NPN operational domain when dedicated UPF interacting with PLMN through N4 interface.

Three solutions have been presented in the study:

- 	Solution #1 proposes a Security Gateway deployed in the PLMN operational domain.

-	Solution #2 proposes a Customer InterWoking Function (CIWF).

-	Solution #3 proposes a Hosted NPN Security Protection Proxy (HNSPP). HNSPP may be deployed only in the PLMN operational domain, or deployed only in the PNI-NPN operational domain, or deployed both in the PLMN operational domain and the PNI-NPN operational domain.

The common ground is that all solutions introduce topology hiding and message inspection at the boundary of the domains.

Editors note: The analysis is for further study.

### 8.1.2	Conclusion

It is proposed to introduce topology hiding and message inspection at the boundary of the domains.

Editors note: Further conclusions are FFS.

*************** End of the change ****************