3GPP TSG-SA3 Meeting #116 	S3-242470

# Jeju, Korea  20 - 24 May 2024                                       merger of S3-242220 and S3-242194

# Source:	CMCC, Huawei, HiSilicon, ZTE Corporation, Nokia

# Title:	Solve EN for Key issue#1&2

# Document for:	Approval

Agenda Item:	5.3

# 1	Decision/action requested

It is proposed to approve the proposed changes for inclusion in TR 33.757 [1].

# 2	References

[1]	3GPP TR 33.757: Study of security for PLMN hosting a NPN

# 3	Rationale

This contribution tries to solve the following EN in key issue#1&2:

Editor’s Note: Whether the 5GS should support mitigation of DoS by compromised NF are FFS.

Some kinds of DoS attack by compromised NF may be caused by massive requests such as PFCP association deletion requests, PFCP session update/deletion requests etc., which can be mitigated with message inspection mechanism. Therefore, it is proposed to remove this EN, and update the related part in KI1&2.

# 4	Detailed proposal

It is proposed to approve the following changes for inclusion in TR 33.757 [1].

**** Start of 1st Change****

### 6.1.3	Potential security requirements

5GS shall support mutual topology information hiding of the PLMN and the NPN customer premises network.

5GS shall support the means to block malformed signaling messages sent from dedicated UPF in the customer premises and compromised SMF in the operator premises.

5GS shall support the means to block messages with wrong NF types sent from dedicated UPF in the customer premises or SMF in the operator premises according to 3GPP specifications.

Note: The mitigation of DoS by massive intentional PFCP signaling messages attempted by compromised NF in 5GS is left for implementation.

5GS shall support the means to authenticate and authorize the dedicated NFs in the customer premises and operator premises.

**** End of 1st Change****

**** Start of 2nd Change****

### 6.2.3	Potential security requirements

5GS should support mutual topology information hiding of the PLMN and the customer premises network.

5GS should support the means to block malformed signaling messages sent from NFs in the customer premises or operator premises over trust boundary.

5GS should support the means to block messages with wrong NF types sent from NFs in the customer premises or operator premises over the trust boundary according to 3GPP specifications.

Note: The mitigation of DoS by compromised NF in 5GS is left for implementation.

5GS should support the means to authenticate and authorize the NFs in the customer premises and operator premises over the trust boundary.

The 5G system shall support a mechanism for secure exchange of DNS queries/answers, when the dedicated NFs are in customer premises.

5GS should support the means to restrict access to services and information exchanged between customer and operator premises and vice versa.

**** End of 2nd Change****