## Slide 1: Cloud Native NF Data Streaming
15 May, 24
Source: Rakuten Mobile Inc [RMI]

## Slide 2: Motivation
MnF
  NF Data streaming in large scale cloud native deployment requires
                High performance for massive amount of data moving from cloud-native NFs to the management system (e.g. data from the CU-UPs, UPFs workloads in central cloud serving the entire city).
                High availability for strong resiliency and fault protection (e.g. a failure in central cloud could affect the entire city) .
                High scalability for the dynamic scaling of cloud-native NF workload.
                High efficiency for lower infrastructure cost and energy saving
WebSocket was originally designed for data streaming between a Web server and client (usually is the Web browser) . Although WebSocket can still be used with some add-on development effort, the complexity and cost for handling the scalability and resiliency in the cloud is high and the efficiency is low in some scenarios. It is not a best fit for all types of cloud deployment scenarios due to the highly diversified requirements.
There are newly developed technologies (e.g. Kafka) that were designed natively to tackle the challenges for data streaming in those cloud environments at much lower complexity, cost and provide higher efficiency.
There are requirements from operators that other data streaming options are needed through leveraging industry solutions not limit to WebSocket
Data consumer microservice
NF microservice
NF microservice
NF
Management System
WebSocket
NF microservice
Data consumer microservice
NF
Convention streaming architecture
(e.g. WebSocket in 3GPP 28.532)
Cloud-native streaming architecture
…
Single point-to-point connection based.
Traffic aggregation point is difficult to scale dynamically and to be efficient for cloud-native environment.
No data publishing and sharing.
Limited transport resiliency and fault tolerance.
Persistent websocket connection need to be maintained with keep alive messages and reconnection overhead.
Application layer manage all connection aspects for connections, parallel streaming, scaling, resiliency, load balancing etc -> huge development and maintenance cost for it to be adapted to cloud environment.
The coupling between producer and consumer side for scaling, resiliency introduce interoperability issue.
Multipoints-to-multipoints streaming to remove performance bottleneck at the aggregation point and improve efficiency.
High scalability is enabled by the streaming framework.
High availability with strong transport resiliency and fault tolerance.
Typically, a middleware streaming framework is used for handling the complexities to manage the streaming connections, message routing, scaling, resiliency and load balancing etc.
The decoupling between consumer and producer thanks to the streaming middleware framework also improve interoperability.
Streaming framework
Management system

## Slide 3: More data streaming framework choices for operators to meet different deployment requirements
c

## Slide 4: More data streaming choices for operators to meet different deployment requirements
Multiple options and solutions can be allowed and can coexist.
Different solutions can be used in different cloud environment, e.g. edge cloud VS regional cloud VS central cloud, private cloud VS public cloud, and for different types for network functions:
  In central cloud, microservices in RAN or CN NFs may send data directly to microservices for NF management using message bus technology rather than via doing multiple stages of conversion, e.g. message bus (microservices within NF) ->WebSocket (NF to management functions)->message bus (microservices within management functions).
  In central cloud, microservices in RAN or CN NFs may still send data to the management functions via WebSocket as long it meet the cloud deployment requirements.
  In edge cloud, NF may send data to central management system via WebSocket first, which is then distributed to other microservices in the management system via message bus.
  In edge cloud, NF may also send data to central management system via message bus to leverage the benefit of recently developed message bus technologies. It is up to the implementation.
There is no one fit all solution. Exact which solution to choose can be left to vendors and operators' choice depending the actual deployment scenario.
WebSocket can still be the only mandatory streaming method in standard for guaranteed interoperability, while the other technologies are optional alternative transports.
Choice of alternative transports, e.g. Kafka, gRPC and HTTP, can be implementation specific and based on handshake between MnS producer and consumer
Data collection and transport technology is one of the most important areas to be optimized for cloud-native NF applications.

## Slide 5: Proposed Solution
The MnS consumer send request to the MnS producer to establish a logical streaming session containing the consumer’s streaming endpoint information, rather than establishing a persistent WebSocket connection (today’s solution).
The MnS producer start reporting the management data to the endpoint(s) provided by the MnS consumer using a pre-selected transport protocol (based on pre-agreement or runtime handshake between consumer and producer).
There are multiple options of streaming transport protocols can be used not limit to WebSocket, e.g., Kafka, HTTP and gRPC etc, for different cloud environment and different operator deployment requirements.
There is no impact to application layer and any other management services. It is purely data transport optimization for cloud-native NFs.
WebSocket can still be the only mandatory streaming method required by the standard for backward compatibility and guaranteed interoperability, while the other technologies are optional alternative transports.
Choices of alternative transports is implementation specific and based handshake between MnS producer and consumer.
Solution today (WebSocket only)
Additional solution proposed

## Slide 6: Message bus streaming support in modern cloud
  Message bus-based streaming, e.g. Kafka, is a good candidate as one of the optional alternative transports
  It is supported in all modern clouds for cloud-native applications.
    AWS
    Google Cloud
    Azure