## Slide 1: DP on “floor remote request“ in emergency communication
Andreas Platzer, BDBOS
3GPP TSG-SA WG6 Meeting #64
Orlando, USA, 18th – 22nd November 2024
SP-245023

## Slide 2: Use case for “floor remote request“
A first responder initiates an MCPTT emergency communication, but is then NOT able to use the UE any further. (i.e. can NOT press the PTT button and is NOT able to talk anymore)
A dispatcher, not receiving any voice (needs to check whether this is a false alert or a serious situation), will override the ongoing emergency group call, trying to contact the first responder.
As the first responder cannot press the PTT button, the floor will go to idle. Resulting that the dispatcher will not receive any voice (= no audio).
In such a situation the dispatcher needs a solution to remotely re-activate the microphone for this first responder (who is still in an emergency state) in order to listen to activities at the location of the remote user.
Notes: Activities similar to discreet / ambient listening need to be in compliance with legal / law enforcement regulations, which, in case of a life threatening situation, may take too long.

## Slide 3: Stage 1 requirements
existing Stage 1 requirements in TS 22.280:
6.15.3 Remotely initiated MCX Service Communication
[R-6.15.3.2-001] The MCX Service shall provide a mechanism for an MCX Service Administrator and/or authorized MCX User to cause an MCX UE that is within their authority to initiate an MCX Private Communication to the MCX Service Administrator and/or authorized MCX User and then begin transmitting to the MCX Service Administrator or authorized MCX User.
[R-6.15.3.2-003] The MCX Service shall provide a mechanism for an MCX Service Administrator and/or authorized user to cause an MCX UE that is within their authority to initiate an MCX Service Group Communication and then to begin transmitting to the Affiliated MCX Service Group Members.

## Slide 4: Dispatcher sends a “floor remote request” (during an ongoing emergency communication)
t
1. Emergency call initiated
Mic may re-open automatically
MC User, in emergency state sends audio
2. Dispatcher overrides
4. Mic stops / timer expired
6. Dispatcher sends a “floor remote request”
3. Dispatcher stops talking
Dispatcher talks
Possibly no impact on standards / client feature
this CR
remotely activate Mic
floor idle
5. Floor is idle

## Slide 5
Thank you
Questions?