## Slide 1: SM Service Discovery
Michel Roy
InterDigital

## Slide 2: Introduction
TS 23.437 v0.3.0 has the following EN in clause 9.6.5 – SM service discovery
Editor’s Note: Whether the SM service discovery procedure is defined in 3GPP TS 23.437 and whether CAPIF API discovery filters in 3GPP TS 23.222 [7] can be enhanced to support discovery of an API provider with specific spatial map coverage is FFS.
2 options are proposed to resolve this EN :
  OPTION #1 –SM service discovery via SEAL SM
  OPTION #2 – SM service discovery via CAPIF

## Slide 3: OPTION #1 –SEAL SM procedure via SEAL SM
Related contribution  S6-245076
Proposal:
  Add SEAL SM procedure for SM service discovery
  SEAL SM server uses the area of interest in the discovery request to identify SM services with spatial map coverage areas that include the requested area of interest
Notes:
  This approach is similar to service discovery procedures defined in other SA6 services, such as EAS discovery for example.
  This approach does not exclude discovery of the service API via CAPIF.

## Slide 4: OPTION #2 – SEAL SM discovery via CAPIF
Related contribution  S6-245077
Proposal:
  Enhance CAPIF publish and discovery APIs to support spatial map coverage areas
  Add service coverage area to the service API information provided by API provider
    E.g., spatial map coverage area
  Add area of interest to the query information provided by API invoker
    E.g., area where a spatial map (with coverage) is required by the requestor
Notes:
  This option introduces in CAPIF a dependency on coverage area and area of interest which may be information specific to SM (e.g., defined in SM specification).

## Slide 5: Summary
Two options are proposed
  OPTION #1 – Service-specific specifications (e.g., SEAL SM)
  OPTION #2 – Service discovery frameworks (e.g., CAPIF)
Recommendation
  For service discovery proceed with Option #1 (e.g., keep CAPIF independent from SM specific information)
  Use CAPIF to retrieve service APIs