## Slide 1: Discussion on various options of XR API at NRM
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
Several key && attractive network features for XR service
Various options for XR API at NRM
Current proposal

## Slide 3: Several key && attractive network features to XR service
Bitrate guarantee: requested maximum bitrate, requested guaranteed bitrate and requested packet error rate
Alternative bitrate guarantee for e.g., adaptive bit rate at the application layer
PDU set handling mechanism – this is used for optimization and provide certain level of user experience in limited network resource case
L4S marking – enable the AS have a more accurate network congestion status
QoS monitoring && QNC – make the AS aware of the QoS satisfaction status, and the performance e.g., UL packet delay, DL packet delay-trip delay, congestion (i.e., a percentage of congestion level), DL and/or UL data rate, packet delay variation.
NOTE: Not all the XR related are listed in this page, only the ones have distinct benefits to the XR service

## Slide 4: How to design the XR API at NRM based on those features ?
Several principles:
Single purpose/benefit
Aggregates network APIs for the same purpose/benefit
Simple and easy to use
Input/output parameter name follows AS familiar terms
Link the input/output parameters to the benefits to be achieved
…..
However, there are several options to meet .
Option 1: purely single purpose, individual API per purpose/benefit
NRM
VAL AS
API #1: bitrate guarantee API
API #2: Monitoring API
API #3: limited network resource optimization API
API #4: Network congestion marking
Pros: Flexible API invocation combination per requirements
Cons: If more than one requirements then multiple APIs invocation interacting
Option 2: one API with variable/selective input and output
NRM
XR API：
 bitrate guarantee input <> output 1
 Monitoring input <> output 2
 limited network resource optimization <> output 3
 Network congestion input <> output 3
VAL AS
Pros: Single service API invocation
Cons: one API service different purpose per input/output may confuse the APP developer/service provider
Option 3: multiple APIs per different purpose/benefit combinations
NRM
VAL AS
Pros: Single service API invocation
Cons: Too many choices for the APP developer/service provider
API #2: bitrate guarantee && Monitoring API
API #1: bitrate guarantee API
API #3: bitrate guarantee && network resource optimization API
API #n:…..
…….
Which one to go ???

## Slide 5: Current proposal
Go with Option#1. easy to evolve into Option#3.