## Slide 1: R19 MC GWUE fixup
Cuili Ge
Huawei, Hisilicon

## Slide 2: Content
Issues in R19 with current form
How to resolve ?

## Slide 3: What is in SA6 scope ?
Any interface/reference point between the MCX functional entities (and application enabler layer entities in non-MC WIs) are within SA6 scope and defined by SA6!!!
Some examples:
MCPTT-3 interface, CSC interface between the CSC servers, CSC server –MCX server are the Server-Server interfaces, and the physical link bears the MCPTT-3 traffic is the fixed connection like fiber optics, but the MCPTT -3 interface are still defined by SA6.
Even in MC GW UE, the MC/CSC client on the non-3GPP device UE use the Non-3GPP access connecting to the GW UE and then to the server, i.e., the MCPTT-1 interface is over non-3GPP access+3GPP access. But the MCPTT-1 is still in SA6 scope.
In other topics, like SEAL, EDGEAPP, CAPIF the server-server interface are also defined by SA6.
In PIN, the interface PIN-2, PIN-3, PIN-4 are also over non-3GPP access, but the interface are defined by SA6.
So, as long as two MC functional entities are the SA6 defined functional entities, the interface between them are in SA6 scope regardless of the physical link between them!!!

## Slide 4: Issues in R19 current form
Issues
  A peer application layer functional entity is required in the MC gateway UE to handle the signallings from the MC client hosted by the non-3GPP device.
  The identity of the MC service user is not aligned with existing identity management mechanism
Observation#1 – No peer application functional entity in MC gateway UE and reference point to the MC service client and CSC client @non-3GPP device
Observation#2 – There are signaling exchanged between the MC gateway UE and the MC service client and CSC client @non-3GPP device
Observation#3 – Identity of the MC service user is not correct
Information element | Status | Description
GW MC service ID | M | The GW MC service ID of the requesting MC service user

## Slide 5: How to resolve ?
New application functional entity in MC gateway UE
New reference points
3. The MC service client has already obtains its identity during the identity authentication interactions with IDM server where the MC gateway UE transparently forwarding those messages b/w MC client and the IDM server.
so the identity of the MC service user should be the MC service ID.
Information element | Status | Description
GW MC service ID | M | The GW MC service ID of the requesting MC service user
GW-local-1
GW-local-2
MC client proxy
Location management messages
MBMS related messages
Handle the signallings from MC client

## Slide 6: Security aspects
The network layer (i.e., non-3GPP access) part should be established but not in SA6 scope.
After the network layer is secured connected, the application layer connection between the MC service client the MC client proxy is established with security mechanism.
The application layer connection security mechanism should be defined by SA3.
GW-local-1
GW-local-2
MC client proxy
S6-241010 core part：
SA3 answer #1: SA3 has discussed the procedures specified in clause 11.5.1.2.3 and clause 11.5.1.3.3 of TS 23.280 and would like to provide the following feedback:
- Any MC related identities SHALL only be provided by the Identity Management Server according to TS 33.180.
- The connection (and related security) between the non-3GPP device and the MCGWUE is out of scope of 3GPP.
- Guidance on MC Gateway UE authentication, non-3GPP device authentication and MC service authorisation can be found in attached CR.
- The authentication of the MCGWUE to the 3GPP network shall follow TS 33.501 or TS 33.401.
- MC Client authentication and authorization shall follow TS 33.180 (whether allow to access the MC service regardless of whether the client is located in the MCGWUE or in the non-3GPP device).

## Slide 7
In the attached CR
5.X.1 General
There are two distinct authentication and authorization mechanisms required in order to allow an MC Client residing on an MC gateway UE or an MC Client residing on a non-3GPP device (connecting via an MC gateway UE) access to MC Services. The first mechanism is 3GPP network device authentication and the second mechanism is MC Client authentication and authorization.
The MC gateway UE requires authentication by the 3GPP network prior to obtaining MC Services. If the 3GPP network authentication procedures are successful and the MC gateway UE is granted 3GPP network access and connectivity, then the MC gateway UE may provide the non-3GPP device access to MC Services via MC Clients.
Two different types of non-3GPP devices are supported, those which can host MC Clients and those which cannot host MC Clients. Regardless of whether the MC Client is hosted on the MC gateway UE or on the non-3GPP device, every MC Client shall follow the authentication and authorization procedures defined in clause 5.1 in order to access MC Services.
NOTE: How information is protected in transit between the non-3GPP device and the MC client when the MC Client resides on the MC gateway UE is out of scope of 3GPP.

## Slide 8: Proposals
The corresponding CR should be agreed.