## Slide 1: Data Collection for RAN Offline Model Training SA aspects
Source: Qualcomm Incorporated

## Slide 2: Summary of RAN1/2 discussions on Model Training for UEs
Based on RAN1#112 agreement, the model training can be performed at the UE-side or neutral site.
Motivation
  The training cannot practically happen in the UE for the lack of training environment including but not limited to availability of data, data storage capacity, computational capacity, and compilation capabilities.
  RAN2 has agreed that only offline training is supported in Rel-18.
RAN2 is not the right place to discuss system level solutions:
  SA2 is the natural places for such system level designs and architecture discussions.
RAN2#121bis-e agreement:
“R2 will deprioritize aspects of on-line/real-time training for the whole SI (unless R1 identifies that it is needed for one of the studied use cases).”

## Slide 3: RAN defined terminology
“UE-side model” and “UE-part of two-sided models”
  Refer to models designed for performing inference at the UE/device.
“UE-side training location” is a training entity under the control of the UE vendor.
  It is NOT training at the UE device.
“Neutral site training location” is a neutral training entity that is not under the control of the UE vendor or network vendors.
  The “neutral entity” can be an operator or any third-party authorized and monitored by the operator, able to train models for a particular UE.

## Slide 4: RAN requirements
For offline model training at the UE-side and neutral site, the data collection solution should:
  Allow data to reach “the UE-side or a neutral site” (ie Over The Top)
  Collect a large amount of data, sufficient for model generalization
  Collect non-standardized data, to develop different models for different UE internal conditions (e.g. UE computational / memory resource constraints, doppler, etc.)
An SA2 defined framework of “UE data collection” is more flexible while maintaining operator’s capability to authorize and monitor the data collection, and therefore better suited for that purpose

## Slide 5: Data collection requirements for RAN offline model training
Proposal 1: SA2 to study a standard data collection solution that enables an offline model training at the UE-side or a neutral-site in Rel-19.
Proposal 2: The standard data collection solution shall:
  Terminate at a network server allowing data to reach “the UE-side or a neutral site”
  Be capable of collecting a large amount of data sufficient for model generalization
  Be capable of collecting non-standardized data, to develop different models for different UE internal conditions