## Slide 1: Satellite Access: SA Rel-19 topics & priorities
Novamint, Thales, TNO, Airbus Defence and Space, Avanti, b-com, CEWiT, Gilat, EDF, ESA, Eutelsat, Gatehouse, Hispasat, Hughes, Inmarsat, Intelsat, IRT Saint Exupéry, Ligado, Lockheed Martin, OneWeb, OQ Technology, Sateliot, SES, ST Engineering iDirect Ireland, Terrestar Solutions, TTP

## Slide 2: Outline
Where we are:
  SA2 5GSAT_Ph2 is now completed in Release 18. The main topic covered was support of discontinuous coverage.
  New capabilities have been addressed in SA1 5Gsat phase 3 for Release 19:
    Store and Forward Satellite operation for delay-tolerant communication services
    UE-Satellite-UE communication (without going through the ground network):
    GNSS independent operation
    Positioning enhancements for satellite access
  The 2 first capabilities are implicitly requiring a regenerative payload (non transparent) approach (R17 and R18 assumed transparent mode satellite access.)
What is expected:
  To consolidate a R19 SA2 study able to enhance and complete the 5GC/EPC architecture to support new capabilities important to support new use cases or to optimise network operation, all relevant for the market.
  This should be done in accordance with RAN scoping
  In addition, there is a need to ensure that the SA6 enablers are supporting Satellite access
  The next slides are listing the candidate features for R19 SA2 5GSAT_Ph3 as well as for a SA6 study on satellite access both representing the views from the satellite community

## Slide 3: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
1 | Integration of satellite components in the 5G architecture Phase III (See next slides for more details) | The study aims at investigating on further 3GPP core network functions enhancements to support satellite access based for the new uses cases as introduced in TR 22.865 and RAN workshop with the following architectural considerations and tasks: Key Work Tasks includes the following aspects | Yes, | SA2 | Yes, Alignment | SA3 for security, SA5 for charging
 |  | 1/ Regenerative payload generic architecture study | TR 22.865 (June 23) TS 22.261 (Dec 23) | SA2 | Yes, Alignment | 
 |  | 2/ Store and Forward Satellite operation | TR 22.865 (June 23) TS 22.261 (Dec 23) | SA2 | Yes, Alignment | SA3 for security, SA5 for charging
 |  | 3/ UE-Satellite-UE communication, 5GS. | TR 22.865 (June 23) TS 22.261 (Dec 23) | SA2 | Yes, Alignment | SA3 for security, SA5 for charging
 |  | 4/ Dual access/steer, TN-NTN and GSO/NGSO, 5GS. | TR 22.841 (Sept 23) TS 22.261 (Dec 23) | SA2 | No | SA5 for charging
 |  | 5/ GNSS independent operation | TR 22.865 (June 23) TS 22.261 (Dec 23) | SA2 | Yes, Alignment | 
 |  | 6/ Multicast and Broadcast Service via satellite. | TR 22.865 (June 23) TS 22.261 (Dec 23) | SA2 | Yes, Alignment | 
 |  | 7/ 5GC supporting IoT NTN |  | SA2 | Yes, Alignment | 

## Slide 4: Overall View on Rel-19 Content
S.NO. | Title | Brief Description and Key Objectives | Related Stage-1 Study/Work Item | Lead Stage-2 WG | RAN dependencies | Other WG dependencies
2 | Application enablement for Satellite access enabled 5G Services | The study aims at assessing what would be needed for the 5G vertical application enablers (e.g. V2X, UAS), enabler frameworks (e.g. SEAL, EDGEAPP) and Mission Critical service developed by SA6 for supporting satellite access and at defining potential enhancements associated: leveraging benefits of providing services in un-served/under-served areas, temporary outage/total destruction of the terrestrial-network also enabling use case that weren’t possible today with just terrestrial networks. Key Work objectives includes the following aspects: Identify the impacts and the necessary changes to the SA6 enabler specifications for supporting satellite access. Identify key issues and solutions to support multiple services using satellite access Possible deployment models for SA6 enablers with satellite access integrated 5G System Enhancements from Rel-19 (e.g. supporting Store and Forward Satellite operation, UE-Satellite-UE communication…) also need support at the enablement layer. | Yes, TS 22.261 TR 22.865 (June 23) | SA6 | No | SA2

## Slide 5: #1.1 Regenerative payload - Architectures
Justification
  Added value services for the user refer to the following capabilities
    Support of delay sensitive and/or delay tolerant services in areas without NTN gateways (not deployed or temporary not operational)
    Enable reduced user and/or control plane latency
    Support communications (unicast, multicast and broadcast) between 2 or more UEs via satellite without going through the ground network (loop back)
    Support of edge computing on board
  Benefits for the network operation include the following capabilities:
    Flexibility in the deployment of the ground segment/NTN gateways wrt to the deployment of the space segment and/or to cope with feeder link service availability issues
    Improving efficiency (incl. signalling overhead) of radio interface radio resources on the feeder links
    Flexibility in the routing of the traffic generated by a group of user equipment to a specific feed link to meet specific national regulations/sovereignty requirements
    Support of multiple core networks per country operated by different operators
    Improving efficiency of radio interface radio resources on the service links thanks to beam scheduling on-board the payload
    Capability to provide simultaneously access and backhaul service

## Slide 6: #1.1 Regenerative payload - Architectures
Problem statement:
  Different architectures are possible to support regenerative payload (eNB + part of EPC, gNB + UPF , gNB + UPF + part of AMF (Dynamic AMF & gNB attachment), gNB-DU + UPF…)
    Note: this is relevant for GSO and NGSO and Inter Satellite Links are assumed for gNB/(eNB) configurations
  Some of those architectures have impacts on the different protocols
    Note: An architectural assumption is that regenerative payload with full eNB and part of the CN functions (e.g. MME) could already be supported with no specification changes – this needs to be confirmed;
  At least 1 payload configuration should be considered for supporting the real extensions needed (i.e. Store and Forward Satellite operation, local switching for UE-Satellite-UE communications, etc.).
Areas for study:
  Minimum necessary set of 3GPP core network functions to be embedded in the satellite for the new uses cases, and study the different possible architectures if any.
  Core network impacts on interfaces, protocols (mobility management, paging) of having “flying” embedded 3GPP functions.

## Slide 7: #1.2 Store and Forward Satellite operation
Justification
  Store and Forward Satellite operation (S&F) allows for delay-tolerant IoT NTN services to be offered in areas visited by the satellites but with no need to have NTN gateway infrastructure (e.g. mid-sea, remote areas)
  Along with support for discontinuous coverage, support for S&F Satellite operation is key to facilitate cost-effective deployment of IoT NTN services and enable an immediate operational service with (1) sparse LEO constellations and (2) reduced ground segment infrastructure.
  The support of S&F puts the 3GPP IoT NTN solution on par with other non-3GPP solutions intended for massive satellite IoT, which natively already supports S&F services
Use cases and requirements addressed under SA1 Release 19
(TR 22.865 v1.1.0, June 2023)
Service link
Feeder link
Core Network
IoT NTN device
Store and forward connectivity service for delay-tolerant IoT NTN applications
Regenerative payload satellite with full eNB onboard and part of CN functions (e.g. MME)
NTN gateway

## Slide 8: #1.2 Store and Forward Satellite operation
Problem statement:
  Store & Forward Satellite operation implies to introduce new parameters and functions related to the Storage and forwarding aspects such as
    Authentication needed
    Storage data (U/D)
    S&F data retention period
    S&F data storage quota
    Policies and priorities (forwarding priority, acknowledgement policy…)
Areas for study:
  Specific impacts on interfaces and protocols of the S&F communication scheme, for both 4G and 5G:
    Store user data on the satellite when the feeder link is unavailable and forward when the feeder link is available
    Definition of the parameters needed to characterize S&F operation from a service perspective (e.g. Authentication, Store UL/DL data and forward, S&F data retention period, S&F data storage quota, forwarding priority, acknowledgement policy) and specification of the related capabilities necessary to enforce them
    Mobility and paging optimizations for S&F operation
    New architectural extensions for S&F operation (e.g. distributed satellite-ground EPC functions for S&F)

## Slide 9: #1.3 UE-Satellite-UE communication
Justification
  The capability to support UE-Satellite-UE communication without going to the ground allows reducing drastically the latency
  It enables to provide services in areas where no gateway can be deployed (e.g. maritime areas or remote areas).
  The communication path can then be done between UEs via one or multiple serving satellites extended across several satellites (through ISL).
Use cases and requirements addressed under SA1 Release 19 (TR 22.865 v1.1.0, June 2023)

## Slide 10: #1.3 UE-Satellite-UE communication
Problem statement:
  At least 1 payload configuration should be considered implementing Inter Satellite Links with routing on board, each satellite may support loop back (UE to UE communications via the space segment) or the support of communications to UE where no gateway can be deployed (e.g. maritime areas or remote areas)
  It is important to define how to activate UE-satellite-UE communication and the impacts on session management to support service continuity when the satellite serving the UE changes
Areas for study:
  Activation of UE-Satellite-UE communication
  Impacts on session management
  Service continuity when the satellite serving the UE changes
  Impacts on possibly regulated services
  QoS control and charging.

## Slide 11: #1.4 Dual Steer
Justification
  Dual Steer implies the support of traffic steering, splitting and switching of UE’s user data (pertaining to the same data session), across two 3GPP access networks solely considering a single PLMN subscription
  At least one of 3GPP access networks can be Satellite Access
  Dual NR satellite access is possible too (e.g. using same or different NTN orbits, e.g., GEO/MEO/LEO)
Areas for study:
  Impacts of NTN specificities on the architecture, interfaces, protocols, in the context of these dual steer use cases.
  Note that this topic might be covered in dedicated dual steer related SID.
Use cases and requirements addressed under SA1 Release 19 (TR 22.841 v1.1.0, June 2023)

## Slide 12: #1.5 GNSS independent operation
Justification
  5G NR NTN and IoT NTN specifications in Release 17 and Release 18 assume that the UE uses its GNSS coordinates i.e., UE position - see TS 38.300 Section 16.14.2.2 and TS 36.300 Section 23.21.2.2 (together with the ephemeris of the serving satellite and additional information about the feeder link delay) to pre-compensate the time and frequency shift.
  In most locations and at most times, GNSS provides a highly accurate position and time reference. However, evidence has been shown that GNSS jamming (leading to denial of service) and spoofing (leading to incorrect location reporting and potentially denial of service) may occur. Also, a terminal, or group of terminals attempting to connect over access channels or once connected to the network, could also cause denial or degradation of service for all other users in the cell if using an altered GNSS position.
  Additionally, GNSS handling may cause delays to the UE operation due to positioning acquisition time (e.g., for a GNSS "cold start") and additional energy consumption.
  Therefore, NTN UEs of all types including handheld terminals and mobile VSAT (*) devices do require an alternative means of achieving and maintaining successful uplink time and frequency synchronization in NTN based access. (*) It is assumed that for a stationary device (e.g., fixed VSAT, static IoT device), the UE position can be pre-configured.
Areas for study:
  impacts on 5GC/EPC of UE location determination (going further from R18 verification) by network only method(s)

## Slide 13: #1.6 Multicast and Broadcast via satellite
Justification
  Non-Terrestrial networks are well suited to support Multicast and Broadcast Services. Such services can provide substantial improvements, especially regarding efficient resources usage and user experience.
  This applies to all types of Non-Terrestrial Networks (GSO and NGSO) operating in all frequency bands.
Problem statement:
  While the features enabling the provision of Broadcast/Multicast communication service have been defined in previous releases for a mobile network deployment scenario characteristic, the provision of MBS over GSO and NGSO NTN would require addressing additional points:
    Addressing NTN moving radio nodes (NGSO) causing the need to ensure service continuity over a given area when the gNB and/or the cell coverage areas are moving
    Location dependent MBS service: Enabling distribution of different content data to different MBS service areas
    User group dependent MBS services: Enabling wide area MBS services addressing a specific user group over a large geographic area and different regulatory regions
    Service subscription with SIM-card less support for broadcast service provider subscriptions, different from MNO services
    MBS could also be provisioned over a joint TN access and NTN MBS reception simultaneously.
Areas for study:
  enhancements to support multicast over a downlink only NTN (Receive Only Mode) and support for a heterogeneous return path (3GPP or non-3GPP access)
  need for architectural enhancements for 5G multicast-broadcast services via NTN

## Slide 14: #1.7 5GC supporting IoT-NTN
Justification
  Rel-17 IoT-NTN is supported by EPC only.
  With potential implementation of integrated NR-NTN and IoT-NTN in one network there is a need to enable 5GC support for IoT-NTN.
  There is indeed 5GC support for terrestrial NB-IoT/eMTC in Rel16, although not deployed mainly due to the existence/availability of legacy EPC.
  In the case of NTN, it will be new deployment and there is no existing EPC and therefore it is important to have 5GC support of IoT to have integrated NR-NTN and IoT-NTN services.
Areas for study:
  specific impacts, if any, on interfaces and protocols of 5GC supporting IoT-NTN

## Slide 15: #2 Application enablement for Satellite access enabled 5G Services
Justification
  SA6 developed several 5G vertical application enablers (e.g. V2X, UAS), enabler frameworks (e.g. SEAL, EDGEAPP) and Mission Critical service to work over terrestrial 3GPP networks. Whether all these specifications work for Satellite access is not know.
  Important aspects to consider: Latency, Limitation of Bandwidth, QoS, Discontinuous Coverage, Location service performance, Store and Forward Satellite operation…
  Service enablers defined by SA6 should also take advantage and ensure that these enablers support satellite access.
Areas for study:
  Impacts and necessary changes to the SA6 enabler specifications for supporting satellite access.
  Review and identify the Satellite access integrated aspects (e.g. service continuity, roaming, federation, broadcast, multicast…) to support SA6 enablers.
  Possible deployment models for SA6 enablers with satellite access integrated 5G System
  Enhancements from Rel-19
NG-RAN
Satellite Access

## Slide 16: Summary Satellite SA-led Rel-19 topics
Topics | SA1 requirements | SA impacts | Stage 3 Impacts | Market Relevance
1. Integration of satellite components in the 5G architecture Ph3 |  | SA2 |  | 
1.1 Regenerative payload architecture | ***** | SA2 | RAN3, RAN2, CT1, CT4 | HIGH (1) (2)
1.2 Store & Forward Satellite operation | ***** | SA2, SA3, SA5, SA6 | RAN3, RAN2, CT1, CT4 | HIGH (1) (2)
1.3 UE-Satellite-UE communication (Local switching) | ***** | SA2, SA3, SA5, SA6 | RAN3, RAN2, CT1, CT4 | HIGH (1) (2)
1.4 Dual Steer | ***** | SA2, SA5, SA6 | CT | HIGH (4)
1.5 GNSS independent operation | *** | SA2, SA6 | RAN1, RAN2, CT1, CT4 | HIGH (1) (2)
1.6 Multicast and Broadcast via satellite | *** | SA2, SA6 | RAN | HIGH (1) (2)
1.7 5GC supporting IoT-NTN | N/A | SA2 | RAN | HIGH (1) (3)
2. Application enablement for Satellite access enabled 5G Services | ***** | SA6, SA2 | RAN, CT | HIGH (4)
key capability needed to support commercial deployments planned in the (very) short term
already supported by non 3GPP solutions
5G key core function to support massive IoT
Will enable new business opportunities/new services