## Slide 1: Views on Rel-19 NG-RAN AI/ML
Qualcomm
Sep 11th to 15th, 2023
Bangalore, India
3GPP TSG RAN Meeting #101
RP-231825
Agenda Item: 8A.2.09

## Slide 2
R18 NG-RAN AI/ML work item introduced the following use cases for non-split NG-RAN architecture
    Load Balancing
    Energy Savings
    Mobility Optimization
    Only Xn Interface enhancements specified
In this paper, QC views are presented for R19 NG-RAN AI/ML Enhancements for following cases.
  R19 further enhancements to R18 identified use cases
  New use cases for R19
Introduction

## Slide 3
Rel-19 Enhancements to Rel-18 Use Cases
AI/ML based Mobility Optimization
Rel-18
UE Trajectory Prediction to assist in determining handover targets
Collect feedback on UE Trajectory Prediction from first hop target node
Rel-19 Proposal 1 :
Further enhance Rel-18 Mobility Optimization to include
UE Traffic Prediction and QoE Prediction to further assist in determining handover targets
Collect feedback on UE Trajectory Prediction from all subsequent target nodes
Selection of targets
Minimizing Handover failures
Preparation of CHO candidate cells
RRM resource allocation and optimization
Admission Control
Blind handovers etc.
Objective
RRM Actions
Optimize RRM resources in RAN to enhance mobility performance for the UE
Minimization of Handover Failures
Motivation

## Slide 4
Rel-18
Actual Energy Cost exchanged among neighbors
Rel-19 Proposal 2:
Further enhance Rel-18 based Energy Savings to include
Predicted Energy Cost exchanged among neighbors
Energy Savings actions sent over Xn
Cell Activation and Deactivation
UE offloading
Carrier switching on and off
Admission Control etc.
Objective
RRM Actions
Optimize Energy Consumption in RAN
Motivation
Rel-19 Enhancements to Rel-18 Use Cases
AI/ML based Energy Savings

## Slide 5: Supporting AI/ML in split gNB architecture
AI/ML training / inference located only in CU-CP and/or in OAM
  Not in DU or CU-UP
  AI/ML related data exchange over F1AP and E1AP not considered
R18 Limitation: does not support AI/ML training/inference in disaggregated gNB Architecture
AI/ML training/ inference can be located in DU and/or CU-UP in addition to the CU-CP
New procedures needed over F1AP and E1AP to exchange AI/ML predicted data
Rel-18 Use cases on Mobility Optimization, Load Balancing and Energy Savings to be adopted in Disaggregated architecture in Rel-19
Proposal 3: Enable support for AI/ML in Disaggregated NG-RAN Architecture for R18 AI/ML use cases and R19 new use cases.
CU-CP
(AI/ML Training / Inference)
DU
(AI/ML Training / Inference)
F1AP: AI/ML
Information Exchange
E1AP: AI/ML
Information Exchange
CU-CP
(AI/ML Training / Inference)
DU
CU-UP
No AI/ML Related Information Exchange over F1AP and E1AP
CU-UP
(AI/ML Training / Inference)
Rel-18 AI/ML in Disaggregated gNB
Rel-19 AI/ML in Disaggregated gNB

## Slide 6
Rel-19 AI/ML new use case : QoE Prediction
QoE Prediction per UE for maintaining user experience as per QoS Requirement
Optimize RRM resource allocation to improve/enforce QoE at UE/UE group level
Xn Interface: Exchange QoE prediction and UE Traffic prediction
Internal gNB actions:
  Internal Resource reallocation at cell and UE level for QoE enforcement
  Handover decisions based on target cell with good QoE Prediction
  Admission Control on PDU session/DRB
Objective
RRM Actions
Interaction between RAN and Core Network would enhance the AI/ML based QoE prediction
RAN and 5GC dependency
Enable the RAN to proactively enhance and enforce a UE’s QoE
Motivation
RLC buffer occupancy
MCS
CQI distribution etc.
Predicted or actual data for the following
RVQoE
Cell Resource Status
DL/UL PRB usage
Inputs
DL/UL UE Throughput
PDCP SDU Data Volume
Packet loss/drop Rate
Proposal 4 : Enhance NG-RAN Interfaces to support AI/ML Information exchange for UE Traffic Prediction and QoE Prediction.

## Slide 7
Rel-19 new use case : RAN Slicing Resource Management
AI/ML based slice resource allocation at both cell and UE level
Slice SLA metric and KPI predictions
Xn Interface: Exchange Predicted Slice level resource status over Xn
Internal gNB actions:
  Slice Resource reallocation at cell and UE level
  Slice resource aware Handover decisions
  Cell activation/deactivation for Slice SLA assurance
  Slice aware Cell Reselection for Idle Mode mobility
  Slice aware UE admission/rejection
Objective
RRM Actions
Slice is a Core level concept; hence this use case will work better when RAN and Core interwork together
RAN and 5GC dependency
Proactively manage resources to meet SLA requirements and enhance KPIs
Motivation
PDCP SDU Data Volume
Average UEs per cell/slice
Packet loss/drop Rate
Predicted or Actual:
Cell Resource Status at Slice level
DL/UL PRB usage
DL/UL UE Throughput
Inputs
Proposal 5 : Enhance NG-RAN Interfaces to support AI/ML Information exchange for RAN Slicing Resource Management.

## Slide 8
Rel-19 new use case
RAN and 5GC Collaboration: RAN Predictions exchange to Core
AI/ML based Slice Resource Management
AI/ML based QoE Management
AMF stores the AI/ML data received from RAN and transfers it back to RAN when requested.
Use Cases
RAN and 5GC dependency
Why
Predicted QoE
Predicted Slice Resource availability
Predicted Slice SLA
Predicted Slice KPIs
What
RAN Prediction exchange to the Core Network
Assist Core Network and Application layer for better RRM decision
AMF
RAN
Shares QoE and Slice related Predictions
Stores and Shares AI.ML data
Slice/ QoE Optimization
Proposal 6: Enhance NGAP Interface to support AI/ML Information exchange between RAN and 5GC.

## Slide 9
Rel-19 RAN and Core Collaboration: Continuous Data/Measurement Collection from UE
What
Use Cases
Why
AMF allocates persistent UE Identifier which can help NG-RAN to identify the UE across RRC states upon request from NG-RAN
AMF provides the same AI/ML UE Identifier to different NG-RANs wherever the UE goes into RRC Connected state
Currently, NG-RAN can only track UEs while in Connected mode
For AI/ML use cases like Mobility Optimization, QoE Prediction etc the AI/ML function in NG-RAN needs to be trained with long duration UE specific data
Rel18 AI/ML use cases have requirement to identify and correlate the UE measurements in Connected and Idle state for AI/ML training
AI/ML based Mobility Optimization
AI/ML based QoE Prediction
UE Traffic Prediction
UE Trajectory Prediction
MDT Report correlation from Connected and Idle State etc.
RAN and 5GC dependency
AMF stores the UE’s AI/ML context including predictions when UE goes to Idle
AMF sends the AI/ML context and predictions to Target RAN node when UE comes back to Connected
AMF assists RAN in UE identification across RRC state transitions for collecting continuous data from UE(s) for AI/ML training
AMF assists in sending feedback to the source node which executed AI/ML Inference
Proposal 7 : Specify solution for continuous collection of UE data/measurement across all RRC states
AMF
RAN
Shares UE AI/ML Context
RAN
Sends UE AI/ML Context
UE  Idle
UE  Connected
Stores UE AI/ML context
Continuous Data Collection
Sends UE Measurements

## Slide 10
Summary of R19 NG-RAN AI/ML Proposals
Proposal 1 : Further enhance Rel-18 Mobility Optimization to include
  UE Traffic Prediction and QoE Prediction to further assist in determining handover targets
  Collect feedback on UE Trajectory Prediction from all subsequent target nodes
Proposal 2: Further enhance Rel-18 based Energy Savings to include
  Predicted Energy Cost exchanged among neighbors
  Energy Savings actions sent over Xn
Proposal 3: Enable support for AI/ML in Disaggregated NG-RAN Architecture for R18 AI/ML use cases and R19 new use cases.
Proposal 4 : Enhance NG-RAN Interfaces to support AI/ML Information exchange for UE Traffic prediction and QoE Prediction.
Proposal 5 : Enhance NG-RAN Interfaces to support AI/ML Information exchange for RAN Slicing Resource Management.
Proposal 6: Enhance NGAP Interface to support AI/ML Information exchange between RAN and 5GC.
Proposal 7 : Specify solution for continuous collection of UE data/measurement across all RRC states