## Slide 1: Proposal on LP-WUS WI in Rel-19
RP-232199

## Slide 2: Introduction
During Rel-18 Study on low-power Wake-up Signal and Receiver for NR [1][2], RAN1 has discussed/analyzed on;
  System impacts for introducing low-power WUS/WUR
    Coverage, network power consumption, system overhead
  Potential UE power saving gains compared to the existing Rel-15/16/17 UE power saving mechanisms
    LP-WUS/WUR for Idle/Inactive mode (paging, RRM measurement)
    LP-WUS/WUR for Connected mode (connected mode DRX)
  Low-power WUR architectures
    OOK, RF envelope detector
    OOK, heterodyne/IF envelope detector
    OOK, homodyne/zero IF with BB envelope detector
    FSK, parallel heterodyne/homodyne with/without frequency to amplitude conversion
    OFDM-based detector with/without FFT
  Candidate waveforms for Low-power WUS/WUR
    OOK, FSK, OFDMA-based waveforms
In this contribution, we propose our preferred work scopes if LP-WUS WI is introduced in Rel-19
[1] RP-222644 Revised SID on low-power WUS WUR for NR
[2] TR38.869 Study on low-power wake up signal and receiver for NR
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Waveform for LP-WUS
Motivation
  In SI phase, several options for LP-WUS waveform generation have been identified and analyzed in terms of power consumption, spectral efficiency, resource overhead, complexity, impact to the existing NR transmitter, etc.
  Each waveform option has its own pros and cons. However, supporting multiple waveform types and a receiver architecture capable of detecting multiple waveforms will increase NW and UE complexity as well as specification efforts.
  Compared to the existing Rel-15/16/17 UE power saving mechanisms, significant power saving gain can be achieved via new physical layer signal and the corresponding receiver.
  The dedicated synchronization signal can be helpful to the receiver for LP-WUS, which can ensure the main radio is in sleep mode and reduce the power consumption as much as possible.
Proposal
  Specify new physical layer signals for low-power wake-up signal (LP-WUS) and low power synchronization signal (LP-SS) with consideration of the corresponding receiver architecture.

## Slide 4: Operation based on LP-WUS
Motivation
  In SI phase, several options for LP-WUS based operation in RRC Idle/Inactive mode and RRC Connected mode have been identified and analyzed in terms of power saving gain, latency, network overhead, etc.
  By using LP-WUS in RRC Idle/Inactive mode, the main radio can be transitioned to ultra-deep sleep state which has lower power consumption than deep sleep state with existing I-DRX operation. During SI, significant power saving gains have been observed by adopting LP-WUS for RRC Idle/Inactive mode compared to existing I-DRX operation with or without Rel-17 PEI
  Moreover, LP-WUS based operations in RRC Connected mode have been identified and analyzed, for example, LP-WUS replacing Rel-16 DCP and LP-WUS cooperating with Rel-17 PDCCH monitoring adaptation indication. During SI, significant power saving gains have been observed by adopting LP-WUS for RRC Connected mode compared to Rel-15 long/short C-DRX operation, Rel-16 DCP and Rel-17 PDCCH monitoring adaptation
Proposal
  Specify LP-WUS based operation in RRC Idle/Inactive mode to wake up UE’s main radio from ultra-deep sleep state
  Specify LP-WUS based operation in RRC connected mode to trigger/adapt UE’s PDCCH monitoring

## Slide 5: RRM supported by LP-WUR
Motivation
  Even though LP-WUS is adopted for RRC Idle/Inactive mode, UE power saving gain cannot be guaranteed with existing RRM measurement by the main radio in RRC Idle/Inactive mode.
    For example, if serving cell measurement by the main radio is not offloaded to LP-WUR, a UE with LP-WUR should wake up to perform serving cell measurement every I-DRX, thus the power saving benefit of ultra-deep sleep state cannot be fully utilized.
  During SI, significant power saving gains have been observed by adopting serving cell measurement offloading to LP-WUR compared to I-DRX and eDRX.
Proposal
  Specify offloading of RRM measurements of serving cell by LP-WUR.

## Slide 6: Summary
Specify new physical layer signals for low-power wake-up signal (LP-WUS) and low power synchronization signal (LP-SS) with consideration of the corresponding receiver architecture
Specify LP-WUS based operation in RRC Idle/Inactive mode to wake up UE’s main radio from ultra-deep sleep state
Specify LP-WUS based operation in RRC connected mode to trigger/adapt UE’s PDCCH monitoring
Specify offloading of RRM measurements of serving cell by LP-WUR