## Slide 1: Inmarsat-Viasat operator priorities for NTN Evolution in Release 19
RP-232467, RAN123-led items
11-15th Sept 2023, 3GPP TSG RAN#101, Bangalore

## Slide 2: Introduction and General Views
NTN is a reality now, with networks being deployed as we speak.
Initial focus of deployments and product has been NB-IoT NTN in FR1, but system will evolve in time
Devices are being released to the market, even before the Release 17 and 18 work has been fully finalized
  NB-IoT NTN was arguably rushed to market with a shorter Work Item phase in R17, this meant some aspects were missed.
We must focus on:
  Features that ensure better system efficiency based on learnings from field
  Features that facilitate deployment and ROI
Release 19 is likely the last chance to improve what’s missing before too many products are already on the market.

## Slide 3: Overall Key Priorities (RAN123 and 4)
IoT NTN (specifically NB-IoT NTN)
  Network Capacity Enhancements – NB-IoT NTN Deployments are capacity limited, severely limited by the DL signalling overhead. Improving system capacity via reduced DL signalling and techniques such as CBS PUR and OCC is critical to meet the capacity demands and ensure economic viability.
  UE Location Reporting for NB-IoT - The lack of support of UE location reporting for NB-IoT NTN is a significant limitation of Rel-17 & 18 for IoT NTN that was missed in Rel-17 due to wrong assumptions. All satellite operators deploying NB-IoT NTN would need this critical feature for mobility and resource management.
  HPUE - For all FR1 IoT NTN bands including especially for NB-IoT NTN, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm).
NR NTN
  NR less than 5 MHz – At least enabling support for 3 MHz channel BW and 12 PRB transmission, as already specified by RP-232467also for NTN bands. This is critical to enable NR NTN deployments within the context of existing non-3GPP services, as well as to support EIRP limited satellites and maximize frequency reuse efficiency.
  UL Capacity/Throughput enhancements – NR NTN deployments will be severely UL limited, Rel-18 focused on UL Coverage enhancements using repetitions. Use of PRB sharing and OCC can lead to huge capacity increase whilst maintaining coverage gains. This is crucial to make NR NTN economically viable.
  HPUE – For all FR1 NTN bands, with support for PC2 (+26 dBm), PC1.5 (+29 dBm) and PC1 (31 dBm), reusing existing TN assumptions for FDD HPUE

## Slide 4: RAN123 Priorities
IoT NTN (specifically NB-IoT NTN)
  Network Capacity Enhancements – NB-IoT NTN Deployments are capacity limited, severely limited by the DL signalling overhead. Improving system capacity via reduced DL signalling and techniques such as CBS PUR and OCC is critical to meet the capacity demands and ensure economic viability.
  UE Location Reporting for NB-IoT - The lack of support of UE location reporting for NB-IT NTN is a significant limitation of Rel-17 & 18 for IoT NTN that was missed in Rel-17 due to wrong assumptions. All satellite operators deploying NB-IoT NTN would need this critical feature for mobility and resource management.
  MBS - This is specifically the ability to support group messages and calls, emergency warning/messages or delivery of data and software to a large number of UE population in a radio resource efficient way (multicast-over-unicast is too inefficient over satellite). For NB-IoT, the current SC-PTM implementation requires a dedicated carrier, not usable for Unicast.
NR NTN
  UL Capacity/Throughput enhancements – NR NTN deployments will be severely UL limited, Rel-18 focused on UL Coverage enhancements using repetitions. Use of PRB sharing and OCC can lead to huge capacity increase whilst maintaining coverage gains. This is crucial to make NR NTN economically viable.

## Slide 5: IoT NTN Network Capacity Enhancements
NB-IoT NTN is already being deployed live at this very moment.
Current NB-IoT NTN UL system capacity is actually limited by the corresponding system DL capacity, due to the larger signalling overhead in the downlink (up to ~53%), and the tight coupling between UL and DL signalling. This impacts also predominantly UL-driven traffic, such as Mobile Originated (MO) transmissions, which are the primary target of massive IoT and initial emergency messaging use cases supported by IoT NTN. Therefore, in order to unlock the additional UL capacity potential, there is a need to identify methods to de-couple the UL from the DL as much as possible.
In the past 3GPP had considered the specification of Contention-Based schemes for PUR with Shared resources (CBS PUR), with the specification of additional signatures, based on CDM orthogonal cover codes, additional DMRS configurations, etc, which had shown the potential for massive gains in UL capacity.
Proposed Objectives:
Specify enhancements to increase the UL system capacity, primarily for Mobile Originated (MO) data transmissions and remove dependency on DL signalling, such as:
  Optimization of DL signalling and reduction of the dependency between DL signalling and UL data transmission, in order to reduce the impact of DL signaling overhead on UL uplink capacity. [RAN2-led]
  Additional UL capacity enhancements techniques that would reduce the dependency on DL signalling, such as PUR with contention-based and contention-free shared resource (CBS PUR, CFS PUR), including with the introduction of a unique signature acting as Orthogonal Cover Codes (OCC). FFS whether CDM based, DMRS based, etc. [RAN1-led]
    UL transmission time/frequency resource pool to be configurable across one or more anchor/non-anchor carreirs. [RAN2-led]
  Combination of NPRACH and CBS PUR based NPUSCH to achieve similar functionality as 2-Step RACH or equivalent procedure for NB-IoT NTN. This could allow to avoid the assumption that the UE must have a valid TA. [RAN2-led]

## Slide 6: IoT NTN UE Location Reporting
Current NB-IoT NTN specification does NOT support efficient ways for the UE to report its location to the network efficiently.
During the Release-17 analysis, concerns were raised to implications related to user privacy when reporting coarse UE location to the network. However, the existence of concrete user privacy concerns when reporting of coarse UE location at a level of granularity equivalent to a terrestrial cell (5 km or larger) is highly questionable, given that such concerns do not exist in terrestrial networks (the network knows the UE is at least within the area of the serving cell or within an area in which it’s capable of measuring and possibly attaching to a number of neighbor cells, which can be even smaller than 5 km).
The lack of support of UE location reporting for NB-IoT NTN is a significant limitation of Rel-17 & 18 for IoT NTN that was missed in Rel-17 due to wrong assumptions. All satellite operators deploying NB-IoT NTN would need this feature for mobility and resource management.
Proposed Objectives
Specify a mechanism for UE location reporting as early as possible during the initial access procedure for NB-IoT NTN devices, including those devices with support for CP CIoT EPS Optimization only. [RAN2-led]
  At least coarse UE location on the order of 50-100 km shall be supported;
  Coarse UE location on the order of 5-10 km is desirable.
  Specify a method to broadcast the request for Coarse UE Location to a group of UE or to all UE within a cell. [RAN2-led]
  AS security should not be assumed.

## Slide 7: NR NTN UL Capacity Enhancements
In Rel-18, UL coverage enhancements have been specified as part of NR NTN Enhancements, such as repetitions and DMRS bundling. However, the use of repetitions by itself has the effect of significantly reducing the system capacity and the individual user throughput, by reducing the resources available for data both for individual users, as well as for the whole system. The use of repetitions will also increase UE transmission time, therefore driving higher utilization of UL resources in the time domain, before they can be released to other users.
Some companies have suggested that, when operating at low coding rate, the use orthogonal cover codes (OCC) to multiplex multiple UEs in the same PRB and the use of sub-PRB allocations per-UE could yield uplink capacity gains of up to 10x, whilst maintaining enhanced UL coverage.
Proposed Objectives
Specify link-level enhancements w.r.t. uplink physical channels [RAN1-led]
  E.g. link-level techniques to reduce the required decoding SNR and benefit the uplink capacity/throughput, i.e. antenna switching
Specify link and system-level enhancements to support the increased capacity for uplink access, e.g. [RAN1-led]
  Sub-PRB allocations per UE
  Orthogonal Cover Codes
  Other potential techniques to increase the capacity of initial access and sporadic access to a pool of UL resources.

## Slide 8: Thank You!