## Slide 1: The motivation to specify AI Mobility NR OPPO, CAICT, China Unicom, China Telecom, Interdigital
TSG RAN#106
Madrid Spain 9~12 Dec. 2024
Agenda item:15.2
RP-242793

## Slide 2: AI mobility working scope [1]
The study will focus on mobility enhancement in RRC_CONNECTED mode over air interface by following existing mobility framework, i.e., handover decision is always made in network side. Mobility use cases focus on standalone NR PCell change. UE-side and network-side AI/ML model can be both considered, respectively.
Study and evaluate potential benefits and gains of AI/ML aided mobility for network triggered L3-based handover, considering the following aspects:
  AI/ML based RRM measurement and event prediction,
    Cell-level measurement prediction including intra and inter-frequency (UE sided and NW sided model) [RAN2]
      Inter-cell Beam-level measurement prediction for L3 Mobility (UE sided and NW sided model) [RAN2]
    HO failure/RLF prediction (UE sided model) [RAN2]
    Measurement events prediction (UE sided model) [RAN2]
  Study the need/benefits of any other UE assistance information for the network side model [RAN2]
  The evaluation of the AI/ML aided mobility benefits should consider HO performance KPIs (e.g., Ping-pong HO, HOF/RLF, Time of stay, Handover interruption, prediction accuracy, and measurement reduction) etc.) and complexity tradeoffs [RAN2]
    NOTE: Simulation assumption and methodology can leverage TR 38.901, 38.843 and 36.839. And leave the detail discussion to RAN2
  Potential AI mobility specific enhancement should be based on the Rel19 AI/ML-air interface WID general framework (e.g. LCM, performance monitoring etc) [RAN2]
    NOTE: This would only be treated after sufficient progress is made in the Rel-19 AI/ML air interface WID
  Potential specification impacts of AI/ML aided mobility [RAN2]
  Evaluate testability, interoperability, and impacts on RRM requirements and performance [RAN4]
    Study the impacts on requirements based on RAN2 assumptions, and coordinate with RAN2 if needed
    Study the testability and interoperability based on RAN2 framework (e.g., number of cells to measure, beams etc.)
    NOTE 4: Leverage the work from “AI/ML for NR air interface” led by RAN1 and avoid the duplicate study for testability and interoperability.
    NOTE 5: Avoid the overlaps with RAN2 work for evaluation
NOTE 1: RAN1/3 work can be triggered via LS
NOTE 2: To avoid duplicate study with “AI/ML for NG-RAN” led by RAN3
NOTE 3: Two-sided model is not included
[1] RP-242393 Revised SID on AIML for mobility in NR

## Slide 3: SID current status
SID completion level:
  50% is completed
Evaluation:
  RRM measurement prediction
    2 rounds of simulation results are collected and evaluated
    Simulation assumption of generalization is concluded
      Evaluation of generalization is expected in Feb. 2025
  Measurement event prediction
    Simulation assumption is concluded
    Evaluation is expected in Feb. 2025
  SLS
    Simulation assumption is concluded
    Evaluation is expected in Feb. 2025
  HOF is down prioritized
  RLF: simulation assumption is concluded
LCM:
  It is expected to kick off From April 2025
RAN4:
  some initial conclusion on core requirement and testability is achieved
Case number | Prioritization | Evaluation scenario combination | Methodology
1 | Low | FR1 to FR1 intra-frequency temporal domain case A | Intra-cell
2 | High | FR1 to FR1 intra-frequency temporal domain case B | Intra-cell
3 | High | FR1 to FR1 inter-frequency (frequency domain) for sub case 1 and 3 | Inter-cell
4 | High | FR2 to FR2 intra-frequency temporal domain case A | Intra-cell
5 | Low | FR2 to FR2 intra-frequency temporal domain case B | Intra-cell
6 | Middle | FR2 to FR2 intra-frequency spatial domain | Intra-cell
[1] R2-2410186 Text proposal of 38.744

## Slide 4: Some initial observations on AI gain vs non-AI
RAN2 concluded in #128 meeting:
  For FR1 intra-frequency temporal domain case B, when PW is short, the performance between AI and sample-and-hold is not significant. However, when PW becomes larger, AI outperforms sample-and-hold.
  In frequency domain prediction cases (2GHz and 4GHz), cell-based approaches achieve limited gain compared to pathloss offset without the help of neighbor cell measurement. The cluster-based shows better performance compared to pathloss offset.
  For intra-frequency temporal domain case A, AI can provide gains (in terms of L3 cell RSRP difference) compared to sample and hold. The gain improves with UE speed.
Chart: FR2 Temporal domain case A
| 60km/h/sub-case1 | 120km/h/sub-case1 | 60km/h/sub-case2 | 120km/h/sub-case2
 | 0.20928 | 0.2251 | 0.42791 | 0.47275
[1] R2-2410799 Evaluation on RRM measurement prediction ZTE
Chart: 
| MRRT:50% | MRRT:60% | MRRT:66.7%
UE speed: 30km/h | 0.086419 | 0.066784 | 0.072544
UE speed: 90km/h | 0.13188 | 0.1461 | 0.16727
FR1 Temporal domain case B
AI vs non-AI gain (30km/h, 90km/h)
AI vs non-AI gain

## Slide 5: FR2 temporal domain case A
Observations:
  The model for FR2 temporal domain case A reflects how much in advance that a model can predict in temporal domain
  Other aspects like observation window length or filtering option etc. will also impact the result, but prediction window and UE speed is the most critical parameter
  Assuming an acceptable threshold is 1.5db, for UE speed 90 and 120km/h, the PW length could be up to 200ms while for 60km/h, it could be up to 350ms
    Considering majority users will be much slower than UE speed in the Figure, it can be foreseen longer prediction window or a lower threshold is feasible
ftp://3gpp.org/Email_Discussions/RAN2/[Misc]/R19%20AI%20MOB%20Simulation%20Results/RRM%20Prediction/Scenario%204

## Slide 6: FR1 Temporal domain case B
Observations:
  The model for FR1 temporal domain case B reflects how much percentage measurement can be saved without or with minimum impact on handover performance e.g. handover failure rate
  Other aspects like filtering option or skipping pattern etc. will also impact the result, but MRRT and UE speed are the most critical parameters
  Assuming an acceptable threshold is 1.5db, at least 50% measurement can be saved for sure.
    Considering majority users will be much slower than UE speed in the Figure, it can be foreseen MRRT>= 67% is also feasible
ftp://3gpp.org/Email_Discussions/RAN2/[Misc]/R19%20AI%20MOB%20Simulation%20Results/RRM%20Prediction/Scenario%202

## Slide 7: FR1 Inter-frequency
Observations:
  The model for FR1 frequency domain reflects the measurement on another frequency can be simply saved without or with minimum impact on handover performance e.g. handover failure rate. It means a measurement gap can be saved and hence user throughput can be improved.
  The figure show an interesting phenomime that the prediction performance is not impacted by UE’s speed almost
  Assuming an acceptable threshold is 1 db, the outcome of the simulation show it is feasible to skip measurement on another frequency carrier based on measurement on one frequency carrier
ftp://3gpp.org/Email_Discussions/RAN2/[Misc]/R19%20AI%20MOB%20Simulation%20Results/RRM%20Prediction/Scenario%203

## Slide 8: Debrief of AI mobility discussion in RAN#102
  During discussion of AI mobility scope in RAN#102 plenary meeting, both LTM and conditional HO are interested in majority company
  LTM is not in Rel19 scope is mainly because LTM itself is still under enhancement in Rel19 and RAN2 would like to focus on legacy handover procedure at starting point
    In Rel19, LTM WID including inter-CU LTM, L1 event and conditional LTM(intra-CU) progress well
  The concern on conditional handover is due to limited TU allocation and RAN2 work load
[1] RP-233111 Moderator's summary on new SI Study on Artificial Intelligence (AI)/Machine Learning (ML) for mobility in NR

## Slide 9: Proposal for AI Mobility
Normative work on AI Mobility:
  Reuse solution for AI/ML over air w.r.t. spec impact e.g. due to LCM procedure as much as possible
    AI mobility specific aspect need be added if deem necessary
  Both UE sided model and network sided model will be covered
  Both FR1 and FR2 will be covered
  At least cover RRM prediction, measurement event prediction and RLF prediction.
  Temporal domain, spatial domain and frequency domain are covered
  3 sub-use cases are covered
  Final scope is subject to future evaluation and consolidation based on RAN2/4 progress
Potential new area in R20 at least cover:
  LTM (intra-CU and inter-CU)
  Conditional LTM and conditional Handover
  Both Pcell change and PSCell change