## Slide 1
Motivation for high-speed train enhancement in Rel-17 NR MIMO
CMCC
3GPP TSG RAN Meeting #86 RP-192729
Sitges, Spain, December 9-12, 2019
Agenda Item: 9.1.1

## Slide 2: Scenario and Requirement
Requirement of HST scenario
  Consistent passenger experience, high data capacity, and critical reliability.
High speed train Scenario
  One of the most important scenarios for high speed train deployment is the SFN deployment scenario captured in Section 6.2 of 3GPP TR 36.878 and Section B.3A of 3GPP TS 36.101.
  Multiple RRHs/TRPs connected to one BBU with fiber and share the same cell ID as illustrated in the following Figure in order to reduce the number of handovers and improve user experience as much as possible. It is anticipated that the SFN deployment will still be the most important scenario for NR high speed train.
RRH4
RRH2
RRH0
RRH1
RRH3
RRH5
BBU
+1.1 kHz
-1.1 kHz
Experienced data rate (DL) | Experienced data rate (UL) | Area traffic capacity (DL) | Area traffic capacity (UL) | Overall user density | Activity factor | UE speed
50 Mbps | 25 Mbps | 15 Gbps/train | 7,5 Gbps/train | 1 000/train | 30% | Users in trains (up to 500 km/h)

## Slide 3: Issues and potential enhancements
Issue 1: UE simultaneously experiences two significant different or even opposite Doppler shift
  TRS and PDSCH are transmitted from coordinated TRPs in SFN manner. Doppler shift from one TRP is about +1.1 kHz, from the other TRP is about -1.1 kHz
  Potential enhancement: Doppler shift pre-compensation at each TRP for PDSCH transmission, Details see P4
Issue 2: Spectrum efficiency / cell capacity need to be improved
  UEs near the window are usually experience LoS-like better channel condition, and the spectrum efficiency for these UEs could be further improved.
  Potential enhancement: Details see P5
Issue 2: Robustness for UEs, especially far from the window in the train, need to be improved
  UEs far from the window in the train are usually experience NLoS-like channel condition, and the robustness need to be further improved.
  Potential enhancement: Details see P6
RRH4
RRH2
RRH0
RRH1
RRH3
RRH5
BBU
+1.1 kHz
-1.1 kHz

## Slide 4: Enhancements on Doppler shift pre-compensation
Consideration on issue 1:
  UE modulates carrier frequency of UL signal based on the carrier frequency received from gNB.
  However, the estimated carrier frequency by the UE based on SFN based TRS transmission is a composite value with two different or even opposite Doppler shift from multiple TRPs.
  Therefore, network cannot estimate the Doppler shift pre-compensation value for each TRP.
Potential enhancement to enable Doppler shift pre-compensation for each TRP
  Different TRPs transmit separate TRS.
  UE modulates the carrier frequency of UL signal only based on the carrier frequency of TRS from one of TRPs.
  Network estimates the Doppler shift pre-compensation values for each TRP.
TRS1
TRS2
TRS0
RRH4
RRH2
RRH0
TRS4
TRS5
TRS3
RRH1
RRH3
RRH5
BBU

## Slide 5: Enhancements for spectrum efficiency
Consideration on issue 2
  UEs near the window are usually experience LoS-like better channel condition, and the spectrum efficiency for these UEs could be further improved.
Potential transmission scheme enhancement for spectrum efficiency
  Scheme: enhancement based on Rel-16 Single-DCI based Multi-TRP transmission
    Independent MCS adjustment for layers from each TRP, i.e., 2 CWs for rank=<4
    Ports corresponding to the same CW should be transmitted from the same TRP

## Slide 6: Enhancements for robustness
Consideration on issue 3
  UEs far from the window in the train are usually experience NLoS-like channel condition, and the robustness need to be further improved.
Potential transmission scheme enhancement for robustness
  Scheme 1: enhancement based on SFN transmission, similar to SDM based scheme 1c discussed in Rel-16 for multi-TRP for URLLC
    TRS is transmitted separately from each TRP
    Multiple TCI states are indicated to UE, each of them corresponds to the TRS of one TRP
    Doppler profile of each TRP can be estimated independently
    Single-port DMRS (SFN) is used in PDSCH
    Pros
      Better channel estimation performance might be obtained compared with baseline
      No extra DMRS overhead
    Cons: Composite channel is still estimated from 1-port DMRS
  Scheme 2: enhancement based on SFN transmission, similar to SDM based scheme 1c discussed in Rel-16 for multi-TRP for URLLC
    TRS is transmitted separately from each TRP
    Multiple TCI states are indicated to UE, each of them corresponds to the TRS of one TRP
    Doppler profile of each TRP can be estimated independently
    Each TRP uses an independent DMRS port in PDSCH
    Pros
      Composite channel can be estimated based on multiple DMRS ports
      Best channel estimation performance can be expected
    Cons: Higher DMRS overhead
Note: For reference (SDM based scheme 1c discussed in Rel-16 for multi-TRP for URLLC)
  One transmission occasion is one layer of the same TB with one DMRS port associated with multiple TCI state indices, or one layer of the same TB with multiple DMRS ports associated with multiple TCI state indices one by one.

## Slide 7: WI Proposals
Based on the email discussion of draft WI for Rel-17 NR MIMO, the following proposals in red should be considered
…
Enhancement on the support for multi-TRP deployment, targeting both FR1 and FR2:
  Identify and specify features to improve reliability and robustness for channels other than PDSCH (that is, PDCCH, PUSCH, and PUCCH) using multi-TRP and/or multi-panel, with Rel.16 reliability features as the baseline
  Identify and specify features to enable inter-/intra-cell multi-TRP operations (e.g., enhancements targeting support of inter-cell delays of more than CP in FR2)
  Evaluate and, if needed, specify enhancements for simultaneous multi-TRP transmission with multi-panel reception, including group-based beam reporting, priority rules in case of multiple QCL-TypeD, and BFR/RLM
  Identify and specify features to enable Doppler shift pre-compensate at each TRP and improve spectrum efficiency/robustness of PDSCH for SFN based high-speed train scenario (i.e., Multi-TRP with ideal backhaul), e.g., enable independent MCS adjustment for Rel-16 single-DCI based Multi-TRP transmission, enable SDM based scheme 1c discussed in Rel-16 multi-TRP for URLLC.
…

## Slide 8
Thank you!