## Slide 1: On DC location reporting for intra-band UL CA
Huawei, HiSilicon
RP-201746
3GPP TSG-RAN meeting #89-e
Sep 14th – 18th, 2020
Electronic meeting

## Slide 2: Background
In Rel-15:
  DC location is allowed to signal with 3300 or 3301 for intra-band CA which is agreed in R1-1900849 and R4-1915361
    For the case of intra-band CA with some CCs activated/deactivated, resulting in variable UE TX DC location.
  CRs on carrier leakage and IQ image measurements for 3300 or 3301 indicating is approved in RAN4:
    In TS 38.101-1, it is specified “In case the parameter 3300 or 3301 is reported from UE via txDirectCurrentLocation IE (as defined in TS 38.331 [7]), carrier leakage measurement requirement in clause 6.4.2.2 and 6.4.2.3 shall be waived, and the RF correction with regard to the carrier leakage and IQ image shall be omitted during the calculation of transmit modulation quality.‘’
In Rel-16:
  RAN4 introduces intra-band UL CA RF requirements, and have discussion on DC location reporting solution for intra-band UL CA
  RAN4 agrees to introduce UE capability of “additional DC location reporting for intra-band UL CA”, and already add it to RAN4 feature list.
  RAN4 sent LS R4-2011906 to RAN1 and RAN2, the LS providing 2 solutions which are under discussion in RAN4:
    Report TX DC location after every activation of BWP’s including CC activation, BWP switching procedure, etc.
    Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
  RAN4 targets to implement additional DC location reporting for intra-band UL CA in Rel-16 with the possible solution between the 2 solutions.
  RAN2 has not included UE capability of “additional DC location reporting for intra-band UL CA” into their spec considering the functionality is still under discussion between two options.

## Slide 3: Why current DC location signalling cannot serve for intra-band UL CA
DC location reporting indicates the frequency of LO leakage
The current DC location signaling is indicated per Cell and per BWP with RRCConfigurationComplete
For intra-band UL CA, the real DC location is derived per active BWP pair; when the active BWP pair update, the location may change
  Since 16 permutations of possibly simultaneously activated BWPs when configured for two cells, it leaves 16 possible TX DC locations
CC1
CC2
BWP11
BWP12
BWP13
BWP14
BWP21
BWP22
BWP23
BWP24
DC location for CC1
CC1
CC2
BWP11
BWP12
BWP13
BWP14
BWP13 and BWP24 are both active:
BWP11
BWP12
BWP13
DC location for CC2
DC location for CC1
CC1
CC2
BWP11
BWP12
BWP13
BWP14
BWP14 and BWP21 are both active:
BWP21
BWP22
BWP23
BWP24
BWP24
DC location for CC2
CC1
CC2
BWP11
BWP12
BWP13
BWP14
BWP21
BWP22
BWP23
BWP24
BWP13 and BWP24 are both active:
CC1
CC2
BWP11
BWP12
BWP13
BWP14
BWP21
BWP22
BWP23
BWP24
DC location
BWP14 and BWP21 are both active:
Note: example for one implementation, 16 permutations for 2UL CCs
Current DC location signaling Per cell per BWP
Real DC location for intra-band UL CA
Observation1 : current DC location reporting cannot correctly indicate the real location of FR1 intra-band UL CA.

## Slide 4: DC location for intra-band UL CA-con’t
Generally，FR1 UE adopts zero-IF architecture which makes LO leakage an unavoidable issue in nature.
In Rel-16, RAN4 completes FR1 intra-band UL CA RF requirements up to 256QAM，LO leakage will have big impact on 256QAM UL performance.
If reuse the current mechanism of allowing UE indicate with 3301(undetermined location) in Rel-16, it may lead to that all the Rel-16 UEs cannot support intra-band UL CA 256QAM well.
gNB could eliminate/cancel the LO leakage impact if UE can indicate clear DC location.
Observation 2: DC location reporting for FR1 intra-band UL CA is highly urgent for Rel-16 UE. Whether it is correctly indicated will highly impact FR1 UL 256QAM performance and commercial deployment.

## Slide 5: Advantage and disadvantage for solutions
    Solution1: Report TX DC location after every activation of BWP’s
    including CC activation, BWP switching procedure, etc.
    Solution2: Report each TX DC location based on permutations of all possible simultaneously activated BWPs within configured BWPs
Solution 1 is not clear on which layer the signaling is carried.
Potentially, Both RAN1 and RAN2 specs are impacted considering BWP switching can be DCI and RRC triggered.
Range of 0~3301 needs 12bit number, L1 signaling can not contain 12bit additional information
Need to Report DC location frequently which depends on BWP activation command
Since RAN4 targets for fulfill in Rel-16, there is
NO enough time for RAN1 to revise L1 signaling.
When UL CC number increase, the permutations of all possible simultaneously activated BWPs will increase with multiplying C41
  But, RAN4 agrees that maximum UL CC number is 2 for Rel-16 FR1 intra-band UL CA
  Although FR2 intra-band UL CC number can be up to 8, only 64QAM requirement is specified for FR2
  FR2 adopts superheterodyne architecture, LO leakage is not severe compared with FR1
It is not urgent to report DC location for FR2 intra-band UL CA
Solution2 is indicated by RRC signaling, it only has impact on RAN2 spec. Solution 2 can be fulfilled in Rel-16.
Proposal 1: The mechanism of Additional DC location reporting for intra-band UL CA should be fulfilled in Rel-16.
Proposal 2: Adopt solution 2 for intra-band UL CA DC location reporting in Rel-16, target RAN2 to complete in #112-e meeting.
Proposal 3: DC location reporting enhancement can be further discuss in Rel-17.