## Slide 1
Agenda Item: 9.0.3
Source: Samsung
Title: Multi-RAT Multi-Connectivity (MR-MC) for 5G-Advanced
Document for: Discussion
3GPP TSG RAN Meeting #93-e
Electronic Meeting, September 13 – 17, 2021
RP-211798

## Slide 2: Motivation of MR-MC
Scenarios: Aggregation of multiple frequency bands, multiple distributed units (DUs), multiple RATs
Limitation of Rel-17 Dual-Connectivity (DC) and Carrier Aggregation (CA)
  DC supports only two independent scheduling entities connected with non-ideal interface
  Within a single scheduling entity (i.e. Carrier Aggregation), all the cells are connected with ideal interface.
Multi-RAT Multi-Connectivity (MR-MC) aims to break the limitation of co-located deployment of scheduling entity and using ideal interface for peak throughput, and further reduce interruption by fast SN changes.
Multi-RAT Dual Connectivity (MR-DC) in Rel-17
Extension of
Multi-RAT Multi-Connectivity (MR-MC)
in Rel-18

## Slide 3: Key Features
Support triple connectivity
  Define two secondary cell groups and two PSCells
  Define two secondary nodes (SNs) and direct SN RRC
  Extension of radio bearer type to cater massive data
    Split bearer with three RLC entities for throughput aggregation
    Other bearer types, e.g. SCG-only split bearer, for NW flexibility
Split bearer with three RLCs
SCG only split bearer
SN1-terminated SCG2 bearer

## Slide 4: Key Features
Support two active uplink cells with triple connectivity to avoid uplink coverage loss due to power sharing
  Require coordination of UL switching time
  Assume non-ideal inter-DU interface
  Require UL sync. Maintenance
Enhancements on RAN interface for coordination
  Serving node selection
  Uplink timing coordination in time/frequency/spatial domain
  User plane data forwarding
Inter-node
I/F
for coordination
FR1
FR2
> 52 GHz

## Slide 5: Works To Do
Potential scope
  Support more than two cell groups (more than two nodes) [RAN2, RAN3, RAN1]
    Procedures for configuring more than two cell groups, e.g., addition/modification/release
    Active cell group switching e.g. UL cell group switching with at most two active UL, DL cell group switching
    User plane enhancement, e.g., data forwarding
    UE capability management
  Support of new bearer types [RAN2, RAN3]
    Enhancement of bearer types, e.g., split bearer operation with three RLC entities
    New SRB type considering multiple nodes