## Slide 1: Motivation of 3Tx handheld UE
OPPO
3GPP TSG-RAN Meeting #93-e RP-211812
Electronic Meeting, 13-17 September, 2021

## Slide 2: Big imbalance b/w UL and DL
UL for handheld UE is limited to 2T and 2CC, max combined capability is 2layer x 2CC (when less than 200MHz contig UL CA)
  UL MIMO and CA can’t be supported simultaneously other cases, like inter-band CA, non-contig CA, EN-DC
DL can reach much higher MIMO and CA capabilities
  Now RAN4 supports up to 4 bands in DL CA, and each band can support 8CC in theory, i.e. max CA capability is 32 CC
  Up to 4layer MIMO in each CC, i.e. max MIMO capability can achieve 16 layers
  The achievable DL MIMO+CA capability is much higher than UL
Handheld UE UL performance is quite limited and no more can be enhanced if stay with current 2Tx assumption
  Max achievable power is 26+26
  Max MIMO and CA is 2layer+200MHz CC, and no MIMO in non-contig CA and inter-band CA
  EN-DC is 1T+1T
  Max concurrent Bands is two

## Slide 3: Introduction of 3Tx in handheld UE
Evolution from current 2Tx to 3Tx
  3Tx means 3Tx chain, and 3PAs activated
Target following 3Tx cases
  1 band/cc with 3Tx
  2 bands/cc with 3Tx
  3 bands/cc with 3Tx
Evolution
CC
CC
CC
CC1
CC2
CC2
CC1
CC2
CC3
Case 1
Case 2
Case 3

## Slide 4: Power enhancement with 3Tx
3Tx can support higher than 29dBm total output power ->RAN4 impact
  3x26 = 30.8dBm ->PC1
  23+2x26 = 30dBm ->PC1.3?
  3x23 / 23+26 = 27.7dBm ->PC1.7?
Different approaches can be considered to support higher or new power capabilities than current power class
  New power class
  Remove upper limit
  Power boosting
PC1 | PC1.3? | PC1.5 | PC1.7? | PC2 | PC3 | PC5
31 | 30 | 29 | 28 | 26 | 23 | 20

## Slide 5: MIMO enhancement with 3T
3 layer MIMO can be supported in 1CC or 2 contig CC -> RAN1 and RAN4 impact
  New 3 ports codebook or reuse 4 ports codebook
  More than 50% throughput gain can be achieved with 3Tx comparing to current 2Tx UL MIMO (see Annex)
2 layer MIMO can be supported in non-contig UL CA, inter-band UL CA, or EN-DC at one CC ->RAN4 impact
  Similar feature has been introduced in RAN4 Rel-17, i.e. contig UL CA+MIMO up to 200MHz aggregated CBW
  No impact to RAN1 and RAN2
TxD with 3Tx can be supported if necessary -> RAN4 impact
CC1
CC2
Cont CA
MIMO
CC2
CC1
CC2
CC1
CC1
SA
MIMO
CC1
CC1
CC1
CC2
CA/ENDC
MIMO
CC2
CC1
SA
TxD
CC1
CC1

## Slide 6: 3 bands Tx simultaneously
3 bands with 1Tx in each band concurrent transmission can be supported, e.g. in UL CA or EN-DC
->RAN4 impact
  MPR evaluation with 3PA
  MSD to cover 3 bands harmonics/IMD/cross band isolation, etc.
  3 bands Tx fall back to 2 bands Tx and 1 band Tx behavior and requirements
Band X
Band Y
Band Z

## Slide 7: Tx switching transmission enhancement
With 3Tx, low band and high band concurrent transmission can be achieved，i.e. no Tx switching is needed in these band combinations including Rel-16 and Rel-17 use cases
However, for power consumption/heating reasons Tx switching transmission might still happen, and in such case 0us Tx switching and no DL interruption can be achieved.
->RAN2 and RAN4 impact
0us Tx switching for Rel-16/17 cases
LB
HB
HB

## Slide 8: UE implementation impact
RFIC needs to support 3Tx chain with 2LO or 3LO
  3Tx chain+2LO can support up to two frequencies concurrent Tx
    3Layer@1CC
    1Layer@CC1+2Layer@CC2
  3Tx chain+3LO can support up to three frequencies concurrent Tx
    3Layer@1CC
    1Layer@CC1+2Layer@CC2
    1Layer@CC1+1Layer@CC2+1Layer@CC3
RFFE needs to support 3PA
  Current UE supports 1PA for low/mid band, and 2PA for high band, and has two PA power supply (ATP/ET)
  To support 1T CC1+2T CC2 case
    No more PA is needed, but one more PA power supply needs to be added
  To support 3T@1CC case
    One more PA is needed for high band, and also PA power supply
Antenna: Reuse existing DL 4Rx antennas, no issue is expected in isolation or implementation
SAR/heating
  Keep total power to existing PC1.5/PC2/PC3 and reuse SAR solutions
  Introduce higher power class (e.g. PC1) to handheld UE in certain bands with further duty cycle restrictions
  With Tx time reduced, heating or SAR is expected not to be a key issue
LO1
LO2
LO1
LO2
LO3
LO1
LO2
Evolution

## Slide 9: Proposal
Introduce handheld UE with 3Tx in Rel-18 and support following features
  Higher or new power capabilities
  3layer and TxD for single CC, and contiguous UL CA
  CA/EN-DC +UL MIMO
    Band A 1T + Band B 2T
    Non-contiguous UL CA: CC1 1T+CC2 2T
  3 bands or 3CC transmission simultaneously
    Band A 1T + Band B 1T + Band C 1T
    Non-contiguous UL CA: CC1 1T+CC2 1T+CC3 1T
  0us Tx switching transmission and no DL interruption

## Slide 10: Thanks !

## Slide 11: Annex 1: UE 3Tx port vs 2Tx port
More than 50% max throughput gain can be observed for UE with 3Tx comparing to UE with 2Tx, no matter codebook or non-codebook based scenario in LLS.
Codebook based
non-Codebook based

## Slide 12: Annex 2: LLS assumptions
Parameters | Values
Channel model | CDL-C 100ns delay 8x2, 8x3 UE antenna space 0.5L with vertical polarization
Carrier frequency | 3.5 GHz
Waveform | CP-OFDM
SCS | 15k
UE speed | 3km/h
UE antenna configuration | 2 port/3port
Number of RBs | 24 RBs
Precoder | Case 1: non-codebook based (wideband eigenvector) Case 2: 2 ports / 3 ports full coherent codebook
SRS | Ideal estimation
DMRS | 1 symbol/type 1 Practical estimation
Rank | Adaptive
MCS | Adaptive (up to 64QAM)
PUSCH | 12 symbol