## Slide 1: Discussion on UL Enhancements in R18
5G Team / Lenovo Research / MBG
3GPP TSG RAN#93 RP-212070
Electronic Meeting, Sep 13-Sep 17, 2021
Agenda Item: 9.0.2
Source: Lenovo, Motorola Mobility
Document for: Discussion

## Slide 2: R18 Uplink Enhancements - Motivation
Rel-16/17 enhancements on UL MIMO focused on improve of coverage as well as reliability
  Full power UL Tx for coverage enhancements
  PUSCH/PUCCH repetition in multi-TRP scenario for higher reliable transmission
More UL capacity is required
  Real-time video surveillance in industrial and healthcare application
  Vehicular application and VR/XR applications
Diversification of UE types
  Handheld UE still dominates
  Non-handheld UE (CPEs, stationary application, vehicular application) with relaxed size & power constraints will become more important
Further improvements in throughput (eMBB) and reliability (URLLC) are needed

## Slide 3: Proposal for UL Enhancements
Work item for UL enhancements with the following objectives:
  Identify and specify features for UL transmission for UE with more than 4 antennas
    High resolution codebook and corresponding TPMI indication for UE with 6 or 8 antennas
    Support of higher rank UL transmission
  Identify and specify features for frequency-selective UL precoding at least for FR1
  Identify and specify additional features for multi-TRP/multi-panel UE
    UL beam management to enable simultaneous multi-panel UE transmission for UL transmission
  Identify further enhancement to UL coverage
    Leftover channel from R17 coverage enhancement WI

## Slide 4: >4Tx transmission
Mainly target non-handheld UE such as CPE/FWA, stationary/industrial/vehicular applications
Goal is to enhance reliability and system UL throughput
The scope shall include
  High resolution codebook for 6/8 Tx
  Up to 8 layer for multi-panel UE. For single panel UE, >4 layer if study shows performance gain
  CB-based and non-CB based PUSCH
  Codeword to layer mapping
  Related enhancement to DMRS and SRS
  FR1 and FR2

## Slide 5: Enhancement to multi-TRP and multi-panel UL
Multi-panel operation
  Simultaneous PUSCH/PUCCH transmission from multiple panels to multiple TRPs
    Improve throughput and/or reliability
    Target intra-cell in FR2
  UE initiated fast panel/beam switching
Multi-TRP/Multi-beam
  Separate TAs, power control and default beams for inter-cell multi-TRPs
  Extend R17 TCI framework to M>1, N>1
  Target both intra-cell and inter-cell
  Target both FR1 and FR2
Overlapping areas between multi-panel and multi-TRP shall be treated together
This topic is closely related to DL multi-TRP/multi-beam. Better combined with DL in a same AI.

## Slide 6: Uplink Frequency-selective Precoding - Initial evaluation
Parameters | Value | Parameters | Value
Carrier frequency, SCS, System BW | 4GHz, 30kHz, 100MHz | Precoding granularity | For sub-band, 4RB per RBG
Channel model | CDL-C in TR 38.901 with 300ns delay spread | Configuration of UE antennas | 4T4R with (M, N, P) = (1,2,2), (dH, dV) = (0.5, 0.5) λ,
UE speed | 30km/h | Configuration of gNB antennas | 4T4R with (M, N, P) = (1,2,2), (dH, dV) = (0.5, 0.5) λ,
Rank, precoders and MCS | Fixed rank-1, TPMI and MCS are adaptive | DMRS configuration | Additional DMRS symbol=2

## Slide 7: Coverage Enhancement
PRACH enhancement
  Identified in R17 as need enhancement
  Identify PRACH coverage gap for FR2/FR1
  Study PRACH repetition to enhance PRACH coverage
  Study beam association for PRACH repetition