## Slide 1: Title: Further discussion on BWP operation without bandwidth restriction Source: OPPO Agenda Item: 9.12 Document for: Discussion
3GPP TSG RAN #99
Rotterdam, Netherlands, March 20-23, 2023
RP-230383

## Slide 2: Background: RAN4 agreements
RAN4#104bis-e
Agreed to perform high-level analysis from the following 4 aspects/criteria on options for UE performing RLM/BFD/BM when CD-SSB is outside active BWP:
  RRM requirements impact (Spec impact) / workload in RAN4
  Mobility performance impact
  Throughput impact (Data interruption)
  UE power consumption / UE complexity
RAN4#105
  Agreed to discuss the following options
  Option A) Perform BM/RLM/BFD based on CSI-RS within active BWP
      Option B-1-1) Using larger BW covering SSB outside active BWP without interruptions
      Option B-1-2) Using larger BW covering SSB outside active BWP with interruptions
      Option B-2-2) Dedicated MG or NCSG for RLM/BFD/BM measurements
  Option C) NCD-SSB approach which would work with existing UE hardware architectures (FG6-1) and be compatible with existing RAN4 specifications for BM/RLM/BFD
RAN4#106
      Agreed that for Option A, existing BM/RLM/BFD requirements defined in TS 38.133 is complete and no new or additional requirements are needed.
      UL timing error requirements based on the SSB shall apply for the UE supporting option A.
      FFS if any clarifications on the existing requirements is needed, e.g., applicability of requirements, conditions of gap configuration etc.

## Slide 3: Background: Highest-level analysis
Highest-level analysis on options:
Options | RRM requirements impact/workload in RAN4 | Power consumption | UE complexity | Mobility performance impact | Throughput impact (Data interruption)
Option A) | Low | Low | Low | Low | None
Option B-1-1) | Low | High | Low to medium | Low | None
Option B-1-2) | Low or Medium | Medium | Low to Medium | Low | Low to Medium
Option B-2-2) | NCSG: Low or Medium MG: Medium | Low | Medium | Low | NCSG: Low to Medium MG: Medium
Option C) | Low | Low | Low | Low | None
Note : “Low”/ “Medium” correspond to the low/medium negative impact

## Slide 4: OPPO’s Views
  In last RAN#98 meeting, RAN can’t make decision due to lack of consensus. As moderator suggested, 2 combos of options can be considered:
    Combo1： Option B-1-1 (wide bandwidth w/o interruption), option B-2-2 (NCSG) and option C (NCD-SSB) to be decided.
    Combo2：Option B-1-1 and option C, with both are optional
  Based on our analysis，we think
  Option B-1-1 has less RRM requirements impact and similar UE complexity，compared to Option B-1-2 or B-2-2 with either interruptions or NCSG.
  Option A has the lowest impact to both RRM requirements and UE implementation.
  Option C seems has low impact but companies especially NW vendors have different views.

## Slide 5: Proposals
    In this RAN meeting，OPPO would like to propose:
    Specify at least option B-1-1，and option B-2-2 under the umbrella of WI eFeRRM.
    Approve revised WID for eFeRRM based on the conclusion in RAN#99, and related work can be started in RAN4#106-bis if agreed.
Options | RRM requirements impact/workload in RAN4 | Power consumption | UE complexity | Mobility performance impact | Throughput impact (Data interruption) | OPPO’s views
Option A) | Low | Low | Low | Low | None | ☆☆☆☆☆
Option B-1-1) | Low | High | Low to medium | Low | None | ☆☆☆☆
Option B-1-2) | Low or Medium | Medium | Low to Medium | Low | Low to Medium | ☆☆
Option B-2-2) | NCSG: Low or Medium MG: Medium | Low | Medium | Low | NCSG: Low to Medium MG: Medium | NCSG：☆☆☆ MG：☆
Option C) | Low | Low | Low | Low | None | ☆☆