## Slide 1: Views on UL Enhancements in Rel-18
Agenda Item: 4.2
Source: FGI, Asia Pacific Telecom
Document for: Discussion
3GPP TSG RAN Rel-18 workshop RWS-210192
Electronic Meeting, June 28 - July 2, 2021

## Slide 2: Justification
After three releases of evolution for New Radio, fundamental architecture has been developed for supporting various applications. From now on, the up coming releases (i.e., R18) may further consider on supporting more advanced applications with more strict reliability, throughput and latency requirements, such as XR, machine vision, vision-based factory detection (e.g., 3-dimensions enabled sensor), remote medical service and live video. It is observed that the uplink data rate required by 2025 will be increased to 10 times.
How to increase the uplink spectrum and the UL data rate to meet the strict requirements for the advanced applications is an important step for Rel-18 to meet the commercial needs. Unlike a base station, a UE’s capability is also considered to be limited due to the design limitation. Enhancing UE’s UL capability is one way to go. In addition, further increasing uplink spectrum efficiency which enabled the novel services is also required. Furthermore, it will be beneficial to extend the dual connectivity architecture to use more than two diverse frequency ranges. In conclusion, mechanisms to supporting a higher UL bandwidth or a higher UL data rate are desired to be investigated in Rel-18.

## Slide 3: Objectives (1/2)
Enable UEs aggregation to enhance UL capability, including: [RAN1/RAN2]
  Achieving UL data transmission via two devices
    Basic Procedures for UE aggregation
      Setup/Modification/Release procedures
      More than two devices for aggregation can be considered
    Introduce mechanism for data flow control
      Path selection and data forwarding mechanism among aggregated devices
      Negotiations among aggregated devices
    Supporting mobility of aggregated devices
      Service continuity of the aggregated devices can be considered
PDCP
RLC
MAC
PHY
PDCP
RLC
MAC
PHY

## Slide 4: Objectives (2/2)
Introduce more uplink spectrum and flexible usage, including: [RAN1/RAN2]
  Support triple connectivity
    Consider triple connectivity to use diverse frequency ranges
  Reducing the signaling delay on carrier activation and deactivation
    Introduce mechanism for fast activation/deactivation configured radio resource (e.g., SPS and CG)
    Further enhancement on dynamically adjust configuration of CA and DC
  Other enhancements of UL transmission mechanism
    Introduce higher modulation order (e.g., 1024-QAM) to increase uplink spectrum efficiency
    Consider Enhancements on UL multi-TRP joint receiver

## Slide 5: Conclusion
According to the objectives:
  Enable UEs aggregation to enhance UL capability
  Introduce more uplink spectrum and flexible usage
We made following proposals:
  Proposal #1: Potential solutions for supporting higher UL bandwidth and a higher UL data rate should be studied in Rel-18.
  Proposal #2: Considering UE aggregation as one of the potential solutions for UL enhancements in Rel-18.