## Slide 1: enhancements for FRMCS
3GPP TSG RAN Rel-19 workshop RWS-230053
June 12 - 16, 2023
Agenda: 4 (High-level overview proposals for Rel-19)
RWS-230053 – June 2023

## Slide 2: UIC Proposal DC/CA
To further enhance the capabilities of 5G for FRMCS and hence its attractiveness, UIC would like to request support of DC and CA for n100 with n101 in Release 19:
  To improve handover between cells
  To improve the network coverage
  To improve the peak datarate
Description: Inter-band DC/CA for 5G NR SA for n100 FDD and n101 TDD with simultaneous Tx/Rx
  Downlink:
    DC/CA for n100 CBW 5MHz with n101 CBW 10MHz;
    DC/CA for n100 CBW <5MHz 20RB with n101 CBW 10MHz;
    DC/CA for n100 CBW <5MHz 12 or 15RB with n101 CBW 10MHz;
    DC/CA for n100 CBW 5MHz with n101 CBW 5MHz;
    DC/CA for n100 CBW <5MHz 20RB with n101 CBW 5MHz;
    DC/CA for n100 CBW <5MHz 12 or 15RB with n101 CBW 5MHz.
  Uplink:
    For both PC3 and PC1;
    The same DC/CA band combinations as mentioned for Downlink.
RWS-230053 – June 2023

## Slide 3: UIC Proposal other features
For the deployment of FRMCS UIC expects that several other 5G NR features that exist in Release 18 will be needed. Hence UIC would like to see those supported for all different channel bandwidths in the bands n100 and n101:
  Conditional Handover (CHO)
  Uplink MIMO (UE supporting 2 Tx antenna ports and both non- and full-coherent UL transmission)
  Support of interference handling capabilities, including:
    enhanced measurements and reporting (e.g., reference signals in support of COMP techniques)
    enhanced Multi-TRP Scheduling (e.g., in support of COMP techniques)
    enhanced demodulation performance requirements (i.e., in support of MMSE-IRC receivers at BS)
RWS-230053 – June 2023