## Slide 1: Single Frequency Network Support for NR MBS
June, 2023
Shanghai Jiao Tong University
RWS-230129

## Slide 2
Motivations
RWS-230129
To enable resource–efficient delivery of multicast/broadcast services, 3GPP has developed NR Multicast/Broadcast Services (MBS) from Rel-17 [1].
Single Frequency Networks (SFN) can provide improvements in coverage, quality of service (QoS), and spectral efficiency[2][3]. The use of SFN is very beneficial for NR broadcast network with macro sites.
NR MBS SFN transmission could be improved from the following two aspect:
  Currently adopted numerologies with normal CP limited the reachable coverage of SFN. Extended CP for 15 kHz and 30kHz subcarrier spacing should be considered.
  Although SFN for NR MBS could be support based on network implementation, SYNC protocol could be specified to provide content synchronization.

## Slide 3
Enhanced CP for 15 KHz and 30kHz SCS
NR MBS is based on the numerologies and cyclic prefix (CP) types (Normal/Extended) as defined in TS 38.211 [4]. TS 38.211 only allows normal CP for 15 kHz and 30 kHz subcarrier spacing (SCS), which limit the reachable coverage of SFN transmission
Extended CP for 15 kHz SCS will increase the theoretical maximum ISD from 1.4 km to 5.0 km. For 30 kHz SCS, the increase will be from 0.7 km to 2.5 km.
The introduction of extended CP can allow for reasonably sized SFNs to improve the special efficiency for NR MBS transmission and to cater the use cases of public safety, software update, advertisement preload, etc.
Support of Extended CP has been motivated and discussed as in [2], [3], and [5].
RWS-230129

## Slide 4
Extended CP for 15 KHz and 30kHz SCS
Changes to TS38.211:
  Table 4.2-1: Supported transmission numerlogies
  Table 4.3.2-2: Number of OFDM symbols per slot, slots per frame, and slots per subframe for extended cyclic prefix
 | [kHz] | Cyclic prefix
0 | 15 | Normal, Extended
1 | 30 | Normal, Extended
2 | 60 | Normal, Extended
3 | 120 | Normal
4 | 240 | Normal
5 | 480 | Normal
6 | 960 | Normal
 |  | Cyclic prefix
0 | 15 | Normal, Extended
1 | 30 | Normal, Extended
2 | 60 | Normal, Extended
3 | 120 | Normal
4 | 240 | Normal
5 | 480 | Normal
6 | 960 | Normal
0 | 12 | 10 | 1
1 | 12 | 20 | 2
2 | 12 | 40 | 4
0 | 12 | 10 | 1
1 | 12 | 20 | 2
2 | 12 | 40 | 4
RWS-230129

## Slide 5
Extended CP for 15 KHz and 30kHz SCS
Changes to TS38.213 [6]:
  If a BWP in the serving cell is configured with 0, 1, or 2 and with extended CP, the UE expects , , or .
Other parts of the specifications are already written to support extended CP for 60 kHz SCS.
The introduction of extended CP for 15 kHz and 30 kHz SCS can be easily implemented by scaling based on the extended CP for 60 kHz SCS for NR MBS.
RWS-230129
Proposal 1 | Extended CP for 15 kHz and 30 kHz subcarrier spacing should be specified by scaling based on the extended CP for 60 kHz SCS for NR MBS.

## Slide 6
SYNC Protocol for Content Synchronization
All gNBs in the SFN area have a synchronized radio frame timing such that the radio frames are transmitted at the same time.
All gNBs have the same configuration of RLC/MAC/PHY for each multicast/broadcast service.
MB-UPF and UPF send multicast and broadcast data with the SYNC protocol to each gNB transmitting the service in SFN area.
The SYNC protocol provides additional information so that the gNBs identify the transmission radio frame(s).
Each gNB buffers multicast and broadcast data and waits for the transmission timing indicated in the SYNC protocol.
RWS-230129
Proposal 2 | SYNC protocol should be specified to provide content synchronization for NR MBS SFN transmission.

## Slide 7
References
[1] RP-220428 Revised WID: Core part: NR multicast and broadcast services
[2] RWS-210446, NR multicast broadcast enhancements, Huawei, HiSilicon, RAN Rel-18 workshop, E-Meeting, June 28 – July 2, 2021.
[3] RWS-210330, MBS and related spectrum bands in Rel-18, Ericsson, RAN Rel-18 workshop, E-Meeting, June 28 – July 2, 2021.
[4] TS 38.211 NR; Physical channels and modulation (Release 17), v17.5.0 (2023-03).
[5] R1-2305964 Rel-18 TEI proposal on eCP support for NR MBS Technical Enhancements and Improvements.
[6] TS 38.213 NR; Physical layer procedures for control (Release 17), v17.5.0 (2023-03).
RWS-230129

## Slide 8
Thanks!
RWS-230129