## Slide 1: Proposal on sidelink communication enhancements in Rel-19
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - June 16, 2023
RWS-230199

## Slide 2: Enhancement for beam-based sidelink operation
Motivation
  Some sidelink use cases require wide channel bandwidth which can be found in FR2. Such use cases include raw sensor data sharing in V2X and high definition video and XR streaming among devices.
    RAN1 is conducting sidelink beam management study in Rel-18.
    It should be noted that 63.72 – 65.88 GHz band is harmonized for ITS in Europe.
  As many regions have an ITS band in FR1, assistance from FR1 needs to be supported for efficient sidelink operations in FR2.
  A directional sensing operation needs to be supported to improve sensing accuracy, and a restriction of resource selection procedure should also be studied by considering the relationship between sensing beam and selectable transmission beam(s).
Objective
  Enhancements for the beam-based sidelink operations [RAN1, RAN2]
    Support of sidelink beam management, by taking Rel-18 study outcome as the starting point
      The operation scenarios include FR2 standalone operation and FR1 assisted FR2 operation.
    Study the impact of beam management on the sensing operation and specify necessary resource allocation enhancements if any
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 3: Enhancement for sidelink carrier aggregation
Motivation
  RAN decided to activate sidelink carrier aggregation objective in Rel-18, but some features supported even in Rel-15 LTE were excluded due to the time limitation.
    No support of mode 1, handling of limited TX capability, etc.
  To fully address the V2X requirements and potentially make the sidelink CA more useful in other applications, at least Rel-15 LTE features need to be specified.
  Inter-band CA, including aggregation of FR1 and FR2 bands, also needs to be supported, e.g., for assistance from FR1 for efficient sidelink operations on FR2.
Objective
  Enhancements for sidelink carrier aggregation [RAN1, RAN2]
    Enhancements for mode 1 operations under sidelink carrier aggregation, at least including SL HARQ feedback report to gNB
    Handling limited transmission/reception capability of a UE
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.

## Slide 4: Sidelink power saving in frequency domain
Motivation
  With increasing bandwidth of sidelink in unlicensed band and FR2, UE power consumption can be an issue. A frequency domain power saving mechanism is necessary so that a UE can shrink its sidelink operation bandwidth when there is no active traffic.
    In order to avoid bandwidth fragmentation, such a narrowband operation should be able to share resources with a wideband operation.
Objective
  Sidelink power saving in the frequency domain [RAN1, RAN2]
    Study and specify a mechanism which enables a UE operating sidelink on a narrowband sidelink to share resources with another UE operating sidelink on a wideband sidelink.
Notes: 현재 PSI 정보를 기반으로는 discard 만 수행할 것이다. 하지만 이걸로 충분하지 않고 PSI 기반의 reliability 및 prioritization을 해야 한다.
한줄로 표현될 수 있도록 하자. 기고의 observation 같이.