## Slide 1
Huawei, HiSilicon
Sub-7GHz MIMO evolution in Rel-19
3GPP TSG RAN Rel-19 workshop RWS-230320
Taipei, June 15 - 16, 2023

## Slide 2: Overviews of Sub-7GHz MIMO Evolution in R19
Massive MIMO further evolution
FDD: CSI-RS and CSI enh. for supporting 64Tx
TDD: SRS enh. for channel prediction and interference mitigation
Receiver: Interference measurement for data, and low complexity 8Rx
Hybrid Beamforming (HBF) enhancements
Hybrid beamforming for Sub-7GHz:
CSI overhead reduction for multiple analog beams
CSI-RS overhead reduction and beam sweep latency reduction
Sub7GHz MIMO evolution should consider enhancements to accommodate more use cases, advanced BS and UE antenna architectures and more practical network deployment, including:
Multi-TRP Enhancements
CJT/JR with non-ideal backhaul
UE assisted scheduling and precoding alignments
Data alignment for TRPs, and UE assisted calibration
UL MIMO Enhancements
Interference suppression for UL DMRS
Sub-band precoding for UL
High resolution of UL precoding

## Slide 3: Massive MIMO: FDD Massive MIMO Evolution
Extend the number of CSI-RS ports, e.g., 64 ports, without extra frequency-time resource
32 port CSI-RS with different orientation directions
64 CSI-RS ports in a CSI-RS resource
Higher accuracy of CSI feedback for 64 ports
Beam for 32Tx
Beam for 64Tx
Introduce statistical eigen bases instead of DFT, where the bases and coefficients are reported at long and short period, respectively. And utilize time correlation for further overhead reduction
64 CSI-RS Ports
Parameters | Value
Frequency | FDD, 2.1GHz
Bandwidth | 10 MHz with SCS 15kHz
Deployment | 21 cells
BS antenna | 64Tx
Traffic model | Full Buffer
UE distribution | 80% indoor (3km/h), 20% outdoor (3km/h)
MIMO scheme | MU-MIMO with Rank1
The performance of Massive MIMO is based on the number of antennas. With a larger antenna array and more RF chains for FDD systems, higher efficiency could be expected. Deployments already have 32 ports, increasing to 64 ports is beneficial for the FDD system performance, which also shown in the following simulation results.
Proposal 1: Support 64 Tx for FDD Massive MIMO in R19.
Evaluation
Evaluation
Parameters | Value
Frequency | FDD, 2.1GHz
Bandwidth | 10 MHz with SCS 15kHz
Deployment | 21 cells
BS antenna | 64Tx
Traffic model | Full Buffer
UE distribution | 80% indoor (3km/h), 20% outdoor (3km/h)
MIMO scheme | MU-MIMO with Rank1
Baseline: The R18 CJT codebook can be used for the CSI measurement of 64Tx array, and its payload is 4X compared with R19 single TRP codebook enhancement
CSI Enhancement for 64 ports

## Slide 4: Massive MIMO: TDD Massive MIMO Evolution
In TDD Massive MIMO, system performance relies on accuracy of SRS based channel measurement. However, there are two critical issues for SRS, which are channel aging on SRS measurement and inter-cell SRS interference.
Proposal 2: Support SRS enhancements for channel prediction and interference mitigation in TDD Massive MIMO.
Key aspects
  SRS based channel prediction enhancement
    Channel Doppler information UE feedback, e.g. Doppler taps information
    UE feedback aided random phase alignment to enable channel prediction with SRSs from different timing
  gNB performs SRS based channel prediction with feedback information
Beam under 64Tx
More tolerant to channel aging
Sharper beam under 128Tx
More sensitive to channel aging
36% gap under 30km/h vs. 3km/h @ gNB 64Tx, with even more performance loss for 128Tx and higher velocity.
Beam mismatch due to channel aging
SRS1
u=0
SRS2
Key aspects
u=0
u=1
  Extend current 30 sequence groups to 60 sequence groups to reduce the interference with same sequence group u
  In practical network in dense urban area, there exists strong inter-cell interference with same sequence group u (same PCI%30)
  When group hopping is enabled, there exists certain probability that sequence group collision occurs in neighbor cell
Large IoT from SRS with same u
~2dB gain @ 0.8
~3.5dB gain @ 0.9
20% IoT>4dB
10% IoT>8dB
UE feedback aided SRS channel prediction
SRS interference management

## Slide 5: Massive MIMO: Enhancements on receiver for MIMO
MIMO Evolution also includes receiver part. There are two key issues in the practical scenarios that need to be addressed, one is the inaccurate interference measurement for data decoding due to the mismatch of interference on DMRS and the data. Another issue is that the complexity and cost for 8Rx is high to be deployed.
Proposal 3: Support interference measurement enhancement for data decoding and complexity reduction for 8Rx.
Enh. on Interference meas. for Data Decoding
Complexity reduction for 8Rx
Cell1
Cell2
Case 1
Case 2
Case 3
Interference misalignment in time domain
Interference misalignment in frequency domain
19% gap
DMRS based interference measurement vs. ideal interference measurement
    Challenge: 8Rx are already specified in current specification. However, 8Rx could also introduce very high processing complexity.
Key aspects
High resolution interference measurement for PUSCH/PDSCH MIMO detection, e.g., new interference measurement resource, e.g. ZP interference measurement RS
  Performance degradation caused by inaccurate DMRS based interference meas.
Key aspects
Implement low-complexity 8R receiver by twin 4Rx receivers/demods, e.g., SRS configurations, precoding design, etc.

## Slide 6: Hybrid Beamforming (HBF) for sub-7GHz Band
64 Ant
256 Ant
512+ Ant
Hybrid beamforming MM for Sub-7GHz
Size of antenna array can be increased with fixed number of TRx
Massive MIMO transmission (e.g. 64TRx +) is supported with hybrid beamforming
More friendly in cost and power consumption
larger antenna array for sub-7GHz can provide enhanced coverage and user experience
Hybrid Beamforming is a good tradeoff between cost and performance
Background of HBF MM
Hybrid Beamforming for Sub-7GHz uses more TXRUs and wider analog beam width, which is different from hybrid beamforming in FR2.
It is beneficial to use multi-beam reporting for better MU-pairing and better UPT.
Chart: 
| Burst@60% RU(0.5Mbyte) | FullBuffer
Serve UE only with its best beam | 1 | 1
Serve UE with both optimal and non-optimal beams | 1.3 | 1.4
Observation 1: Hybrid Beamforming with multi-beam reporting is a good trade-off between cost and spectrum efficiency for Sub-7GHz massive MIMO

## Slide 7: Enhancements for HBF for sub-7GHz
DAC
Analog antenna port0
Analog Antenna port1
Analog Antenna port2
Analog Antenna port3
Channel measurement for analog antenna ports in a RF chain
Channel of arbitrary beam can be calculated by the UE with NW-configured beam weight
CSI compression for HBF: Joint CSI compression for multi beam CSI feedback, while the common parts of CSI for each beam could be compressed.
Beam1
Beam2
Beam3
Joint PMI reporting
CSI-RS overhead reduction for HBF: CSI-RS is used for analog antenna ports measurement instead of beam-sweeped channel measurement, RS overhead and latency is reduced.
Enhancements for HBF for Sub-7GHz
3D Uma
4 analog beams with HPBW 11°
CSI-RS overhead not included
For Hybrid beamforming for sub-7GHz, two key issues need to be addressed in R19, one is CSI-RS overhead and the latency for CSI measurement, another is the CSI feedback overhead.
Proposal 4: Support CSI-RS overhead reduction and CSI compression for multi-beam reporting for HBF.
Element-wise channel estimation
Beam-domain channel calculation
Calculated channel with NW-configured beam weight

## Slide 8: M-TRP: Coherent joint Transmission for non-ideal Backhaul
In current deployments, IP-RAN structure is widely deployed in Europe and some Asian areas, which is with non-ideal backhaul. To enhance the system performance with coherent joint transmissions / receptions in such scenarios, we need to address the issues of latency and misalignment. With the help of UE side, the scheduling, precoding and data could be well aligned, and then the CJT/JR could be used.
Proposal 5: Support CJT/JR for non-ideal backhaul scenario to facilitate multi-cell CJT/JR with UE assistance.
Rel-18 CJT/JR for ideal backhaul
Rel-19 Proposal: CJT/JR for non-ideal backhaul
Ideal backhaul
Non-Ideal backhaul
Relative performance of LT-CJT
(TDD, 3.5GHz, 64Tx)
Baseline
R19
Relative performance of LT-CJT
(FDD, 2.1GHz, 32Tx)
Relative performance of LT-JR
(TDD, 3.5GHz, 64Rx)
Key issues of LT-CJT
Scheduling alignment
Data alignment
Clock synchronization
Distributed joint precoding
Key issues of LT-JR
Scheduling alignment
Clock synchronization
Baseline
R19
Baseline
R19
Performance gain of the Latency Tolerant (LT) CJT/JR with non-ideal backhaul is shown, compared with legacy CJT/JR solutions.

## Slide 9: M-TRP: Example solutions for CJT/JR for non-ideal Backhaul
Scheduling alignment
1
Distributed joint precoding (CJT only)
4
Data alignment (CJT only)
2
For CJT/JR, time-frequency resource, MCS, TB size, and data mapping need to be aligned for coordination TRPs, but high latency with non-ideal backhaul. UE-assisted scheduling information exchange by air interface could help to address the issue.
UE-assisted CJT precoding could be used to address the precoding alignment between TRPs and interference suppression.
DL data to be transmitted have to be synchronized for coordination TRPs, e.g., the same data is buffered in these TRPs, which could be by DL L2 processing.
Initial precoding
Interference information
Precoding update
Interference information
CSI-RS
CSI-RS
UL：JR
PUSCH
PUSCH
time
DCI indicating RA and MCS
UCI forwarding
SR
SR
Scheduling
DL：CJT
PDSCH
PDSCH
time
DCI indicating RA and MCS
UCI forwarding
Scheduling
Initial precoding
Precoding update
time
PDSCH
PDSCH
Clock synchronization
3
Clock synchronization can be guaranteed by UE-assisted synchronization and calibration for coordination TRPs for CJT/JR.
TRP1
UE
TRP2
DL-RS#1
DL-RS#2
Parameter
Estimation
Parameter
Reporting
CJT & JR
CJT
CJT
CJT & JR

## Slide 10: Enhancements on UL-MIMO
UL MIMO enhancements are also important to improve the UL data rate. In Rel-18, 8Tx are already supported, while some DL codebooks are reused for UL 8Tx transmissions. To further enhance the UL performance, especially to enable UL MU-pairing, two key enhancements could be included in Rel-19, one is interference mitigation for UL DMRS, and another one is sub-band precoding for UL transmissions.
Proposal 6: Support UL sub-band precoding and interference mitigation for UL DMRS.
Interference suppression for UL DMRS
Enhancements on UL Precoding
Channel spatial correlation matrix feedback to assist DMRS channel estimation
Conventional scheme:
delay domain channel estimation
SRS/UE feedback based scheme
spatial + delay domain two-dimensional channel estimation with the aid of channel spatial correlation matrix from SRS or UE feedback
Channel Sparseness in both delay domain and spatial domain
Uplink sub-band precoding and high-resolution precoding, considering overhead reduction for precoding indication, e.g., UL precoding indication via CSI-RS
Initial evaluation results for sub-band and high-resolution precoding

## Slide 11: Conclusions
In this contribution, we discuss the enhancements of MIMO for sub-7GHz. We have the observations and proposals as follows:
Observation 1: Hybrid Beamforming (HBF) with multi-beam reporting is a good trade-off between cost and spectrum efficiency for Sub-7GHz massive MIMO
Proposal 1: Support 64 Tx for FDD Massive MIMO in R19.
Proposal 2: Support SRS enhancements for channel prediction and interference mitigation in TDD Massive MIMO.
Proposal 3: Support interference measurement enhancement for data decoding and complexity reduction for 8Rx.
Proposal 4: Support CSI-RS overhead reduction and CSI compression for multi-beam reporting for HBF.
Proposal 5: Support CJT/JR for non-ideal backhaul scenario to facilitate multi-cell CJT/JR with UE assistance.
Proposal 6: Support UL sub-band precoding and interference mitigation for UL DMRS.