## Slide 1: views on Rel-19 RAN4 topics
Xiaomi
3GPP TSG RAN Rel-19 workshop
Taipei, June 15 - 16, 2023
RWS-230328
Agenda Item: 6
Source: Xiaomi
Document for: information

## Slide 2: Overview of potential Rel-19 RAN4 package
RF | UE RF FR1 further enhancement
 | UE RF FR2 further enhancement
 | BS RF further enhancement
RRM | RRM further enhancement
 | Measurement gap further enhancement
DEM | Demodulation further enhancement
test | MIMO OTA
 | SISO OTA
Others | NTN
 | Others
The following areas could be considered for Rel-19 for non-spectrum WI/SI

## Slide 3: FR1 RF further enhancement
Motivation
  Increasing the transmit power of UE has significant benefits on extending cell coverage area and improving the experience of cell edge users. The potential PC1.5 could be considered for intra-band CA and inter-band CA
  6Rx for UE had been discussed as one of candidates for Rel-18 scope, it could be studied in R19.
  Objectives
  High power UE related issue
    PC1.5 for intra-band CA
    PC1.5 for inter-band CA
  Study on 6Rx for UE on high bands

## Slide 4: FR2 RF further enhancement
Motivation
  CA
    The inter-band CA has been introduced from R17. However, due to limited timeline, there are some restrictions: i.e. only FR2-1 band is involved and only based on IBM.
  Others
    The remaining issue from R18
Objectives
  CA
    Inter-band CA enhancements in FR2-1
      Define the RF requirements for inter-band CA based on CBM in FR2-1
      Define the RF requirements for inter-band and intra-band DL/UL CA/DC RF enhancement in FR2-1
    Inter-band CA between FR2-1 and FR2-2 based on CBM/IBM
      Define the RF requirements for support of CA/DC between FR2-1 and FR2-2 based on CBM/IBM
        The example band combinations based on operator’s demand
  Other remaining objectives from R18 if needed

## Slide 5: MG further enhancement
  Pre-MG, NCSG and concurrent gaps for MR-DC
    Motivation: The applicable scenario of concurrent MG, Pre-MG and NCSG is limit to NR SA, while in MR-DC scenarios, the work on requirements for the joint configuration of pre-configured MG, concurrent MG and NCSG was deprioritized in Rel-18.
    Define RRM requirements for UEs configured with a combination of pre-configured MGs, and/or concurrent MGs and/or NCSG in MR-DC
  Enhancement on gap features
    Motivation: In Rel-18, several gap related features are supported, i.e. Pre-MG, concurrent MG, NCSG, NTN gap, MUSIM gap and ePOS gap. While, no RRM requirements and UE behavior to support the joint configuration for gap features.
    Define RRM requirements for joint configuration of gap features.

## Slide 6: MIMO OTA potential enhancement
Motivation
  The MIMO OTA WID of Rel-18 is on-going and mainly focus on the FR2 performance requirement definition with hybrid method including simulation and measurement method.
  The FR1 MIMO OTA enhancement to reflect the UE UL MIMO throughput has not been considered yet while the UL enhancement with higher throughput and better UL coverage is under discussion in Rel-18 WID.
  The FR2-2 test methods have been discussed in the Rel-17 SID of FR2 test method enhancement while the MIMO OTA test method is not covered.
Objectives
  FR1 MIMO OTA enhancement
    New bands requirements
    Phantom based MIMO OTA test method
    UL MIMO with new test method and new FoM can be studied
      Study on dynamic channel model
  FR2 MIMO OTA enhancement
    New bands covering FR2-2 can be studied
      Potential new test method/enhancement
  More FR2-1 bands to be considered with agreed framework

## Slide 7: Thanks