## Slide 1
On GNSS for Sidelink Positioning
3GPP TSG RAN Rel-19 workshop
June 12 – June 16, 2023
Agenda Item: 5
RWS - 230362

## Slide 2: Motivation
Positioning in 5G has multiple use cases and achieved important milestones: basic positioning with LTE (Rel-15), native NR (Rel-16), and latency/accuracy enhancements (Rel-17 NR). Release 18 aims to enhance accuracy, integrity, power efficiency, sidelink, and RedCap support;
Sidelink positioning provides a new positioning method that fits new 5G use cases, especially from automotive industries and public safety community (RP-210040, RP-210036, SP-200575);
Very challenging relative and absolute positioning accuracy, especially Set B, which may not be achievable with SL-positioning only even with 100 MHz bandwidth (TR 38.859).
To meet Set B targets, the expectation is that UEs need to fuse RAT-dependent methods with GNSS and other sensors. Therefore, it would make sense to consider studying Sidelink signalling aspects related GNSS methods in Release 19.
Set A (TR 38.859) | Set B (TR 38.859)
1-1.5m for 90% of UEs (absolute or relative) | 0.2 – 0.5m for 90% of UEs (absolute or relative)

## Slide 3: Current situation: A-GNSS support in NR systems on Uu interface
1Observation Space Representation (OSR): observed code/carrier at a certain location. Differential positioning technique errors are removed by double-differencing: reference station(s) and moving receiver (rover).
2State Space Representation (SSR): models to calculate expected code/carrier at any location. More precisely, clock, orbit, bias, ionospheric and tropospheric errors are calculated by a network of monitoring stations, a superset/enhancement of PPP.
Recent work on high accuracy GNSS positioning in 3GPP
Release 15
OSR (RTK method) and Phase 1 of SSR (PPP method) assistance data were specified in LPP based on RTCM standards.
Release 16
Phase 2 of SSR (PPP-RTK method) assistance was defined in LPP based on Compact SSR format.
Release 17
Integrity assistance data for SSR (PPP-RTK method) assistance was defined in LPP.

## Slide 4: Potential enhancements: GNSS assistance data via Sidelink / PC5 interface
In-Coverage scenario | Partial Coverage | Out-of-Coverage
RAT-dependent methods (Release 18 and beyond) |  | 
Proposed GNSS enhancements: Moving Base RTK via SLPP/PC5 (new type of GNSS assistance data required) Open point: UEs in coverage can obtain A-GNSS data on Uu interface via LPP  is there need to route LPP assistance data also via PC5? | Proposed GNSS enhancements: Moving Base RTK via SLPP/PC5 (new to 3GPP positioning protocols i.e., not yet supported in LPP) Extend support for A-GNSS assistance data from Uu / LPP / UE in coverage to PC5 / SLPP / UE outside of coverage | Proposed GNSS Enhancements: Moving Base RTK via SLPP/PC5 (new type of GNSS assistance data required)
Enables hybrid positioning based on RAT-dependent methods and GNSS | Enables hybrid positioning based on RAT-dependent methods and GNSS | Enables hybrid positioning based on RAT-dependent methods and GNSS

## Slide 5: Specification impact related to GNSS assistance data via Sidelink / PC5 interface
Already in 3GPP specs (TS 37.355)
RTK
PPP
PPP-RTK
New to 3GPP specs:
Moving Base RTK
*note, is a variant of classical RTK (already specified in LPP) with the only difference that the Reference Station (correction source) is moving as depicted below in the 2 vehicles platoon example.
Two type of GNSS assistance data is foreseen: already supported in 3GPP specs (i.e., LPP on Uu) and new
Specification impact expected to be minimum:
Moving Base RTK is a standard used by GNSS industry
All other GNSS methods (conventional A-GNSS – Rel.9; OSR, SSR – Rel15-Rel17) are already defined in LPP and can be translated to SLPP

## Slide 6: Conclusions & Proposals
3GPP to study GNSS assistance data for fused GNSS – NR Sidelink Positioning in Rel-19.
  GNSS positioning methods: RTK, Moving Base RTK, PPP, PPP-RTK
  Design SLPP procedures for distributed cooperative positioning based on GNSS assistance data independent of Uu to support partial coverage and out-of-coverage scenarios
  Signalling aspects in support of hybrid GNSS – NR Sidelink Positioning