## Slide 1
3GPP TSG RAN Rel-19 Workshop RWS-230438
Taipei, June 15 – 16, 2023
Considerations on NR SL Positioning
in Unlicensed Spectrum Agenda Item: 5

## Slide 2
Motivation
NR sidelink (SL) on unlicensed spectrum (SL-U) has been specified to support applications requiring high data rate, flexibility and low cost of deployment
NR SL positioning has been specified to support use cases such as V2X, public safety, commercial use-case, Industrial Internet of Things
The integration of NR SL positioning into the framework of NR SL on unlicensed spectrum will enhance NR SL to support the use cases:
  Autonomous driving:
    A huge amount of data exchanged between the vehicles to determine their positions
    No line-of-sight transmission between the UE and the gNB for the positioning information
  Gaming industry: high data rate to connect the devices and determine the positions of the devices in the interactive game

## Slide 3
Background
In Rel-18, NR SL on unlicensed spectrum has been specified
  Channel access mechanism for SL control (PSCCH), data (PSSCH), feedback (PSFCH), synchronization signal block (SSB) transmissions
  Physical channel design: number of starting positions of PSCCH in a slot, number of PSFCH occasions associated to a PSSCH transmission, number of S-SSB occasions in a period, interlace configuration of PSCCH, PSSCH, PSFCH, S-SSB
In Rel-18, NR SL positioning has been specified
  Dedicated and shared resource pool for SL positioning reference signal (SL-PRS)
  Resource allocation for SL-PRS
  Time and frequency domain patterns of SL-PRS
Observations
  NR SL positioning on unlicensed spectrum should be specified to enhance NR SL-U by providing the techniques to the devices in SL communication to determine their absolute or relative positions

## Slide 4
Proposals
Study channel access mechanism for SL-PRS transmission
  Channel occupancy time (COT) sharing between the UEs for SL-PRS transmissions in the dedicated and shared resource pools
  Cyclic prefix extension for SL-PRS to fill the gap between the transmissions to avoid the additional listen-before-talk (LBT)
Study slot structure in the dedicated and shared resource pools for SL-PRS
  To time-multiplex SL-PRSs of multiple UEs in a slot and guarantee the SL-PRS transmissions of these UEs without additional LBT
  The position of PSCCH associated to SL-PRS in a slot to guarantee the continuity of the PSCCH and SL-PRS transmissions