## Slide 1: WF on PSS/SSS Details
Intel, CATT, HTC, MediaTek, Hitachi, CATR, CMCC, New Postcom, Pantech
3GPP TSG RAN WG1 Meeting #71
New Orleans, USA, November 12th – 16th, 2012
R1-125350
Agenda: 6.3.1.1
Document for: Decision

## Slide 2: Backgrounds
Agreements on PSS/SSS in RAN1#69
  Alt 1: Avoid collisions between PSS/SSS and DM-RS by moving the PSS/SSS
    1a: keeping Rel-8 relative locations of PSS/SSS:
    1b: change relative locations of PSS/SSS
  Alt 2: Change the DM-RS pattern on NCT (i.e. in all subframes) to give better performance for PDSCH demodulation in the absence of a legacy control region (and thereby also avoiding collisions with PSS/SSS)
  Alt 3: Do nothing about PSS/SSS DM-RS collisions in Rel-11
    3a: Puncture DM-RS
    3b: Forbid PDSCH transmissions in PRBs with PSS/SSS
  The existing DM-RS patterns will be used on the NCT (subject to possibly being with puncturing as per Alt 3a). Study until RAN1#70 alternatives 1 and 3. Keep in mind the question of whether it is worth changing the PSS/SSS locations for NCT in Rel-11 given the considerations raised on DM-RS patterns.

## Slide 3: Proposals
Alt 3a is agreed for PSS/SSS collision handling with DM RS.
  Do nothing about PSS/SSS DM-RS collisions
    Puncture DM-RS for the REs colliding PSS/SSS